## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 - 30 August, 2019
Huawei, HiSilicon
Way forward on URLLC test methodology
R4-1910044

## Slide 2: Evaluation of the feasibility for test reliability of 99.999%
Take the following factors into account to evaluate the feasibility of test 99.999% reliability
  The goal of the evaluation should be to provide estimates of test time(s) and confidence level(s) for the methods in slide 3 (or other methods if identified) so that a conclusion on test feasibility, confidence level, reasonable test time and test methodology can be reached.
  Key factors impacting evaluation
    Target reliability level: 99.999%
    Possible confidence level (CL): {95%, 98%, 99%, 99.5%}
    Number of errors
  Other factors to describe
    The following factors may be relevant to the evaluation and assumptions used should be described when presenting results:
      Propagation condition (e.g., static, fading)
      Antenna configuration
      Number of retransmission
      Duplexing mode and TDD configuration
      Slot based transmission or non-slot based transmission
      MCS
      Rank
      PDSCH mapping type
      DMRS configuration
      CBW/SCS

## Slide 3: Test methodology for test reliability of 99.999%
Test methodology:
  Option 1: Run one long test to reach reliability of 99.999%
  Option 2: Run multiple small duration tests with different channel seeds and combine the results later
  Option 3: Leave to RAN5 to define (for UE only)
  Option 3a: Use RAN5 method for BS if applicable
  Option 4: Extrapolation to low BLER for some test cases
  Option 5: UTRA BLER test methodology from TS 25.141/34.121-1 as a starting point
  Other options are not precluded

## Slide 4: Test methodology for low latency
Test metric of delay is not feasible for low latency test in RAN4
Low latency related features are feasible to be tested under the test metrics other than delay, such as throughput and/or BLER.

## Slide 5: Reliability and Low latency
No combined performance requirements will be defined by meeting both reliability of 99.999% and low latency requirements