## Slide 1
3GPP TSG-RAN WG4 Meeting #92 R4-1910050
Ljubljana, SI, 26th– 30th August, 2019
Agenda Item: 9.16.2
WF on UE demodulation for NR HST
CMCC

## Slide 2: Agreements
SCS and channel bandwidth
  FDD: 10 MHz, SCS 15 kHz
  TDD: 40 MHz, SCS 30 kHz
  FFS for FDD 30KHz

## Slide 3: Agreements
Maximum Doppler
  For TDD 30KHz
    For HST single tap, maximum Doppler 1667Hz is feasible.
    For HST-SFN, further study the maximum Doppler frequency:
      Target speed of 500km/h
        Option 1: 1667Hz
        Option 2: 1500Hz
      Target speed of 350km/h
        1167Hz
  For FDD 15KHz
    Single tap HST
      Option 1: 1000Hz
      Option 2: 1250Hz
    HST-SFN
      Target speed of 500km/h
        Option 1: 1667Hz
        Option 2: 1250Hz
        Option 3: 875Hz
        Option 4: 972Hz
        Option 5: 780Hz
      Target speed of 350km/h
        Option 1: 875Hz
        Option 2: 780Hz
Note: for HST-SFN, other options are not precluded

## Slide 4: Agreements
Deployment scenario
  HST-SFN with bidirectional coverage
  HST single tap
  FFS for multi-path fading channel
  Applicability rule will be discussed

## Slide 5: Agreements
Channel model
  For HST single tap
    Option 1: Ds=300m, Dmin=2m
    Option 2: Ds=700m, Dmin=150m
  For HST-SFN, reuse LTE HST-SFN bi-directional channel model, and number of taps can be further discussed.
    Option 1: Ds=1000m, Dmin=50m
    Option 2: Ds=700m, Dmin=150m
    Option 3: Ds= 300m, Dmin=2m
    RRM impact needs to be considered
  For simulation alignment purpose
    HST-SFN: use 4-tap as baseline
    Option 1 Ds=300m, Dmin=2m for HST single tap
    Option 1 Ds=1000m, Dmin=50m for HST-SFN

## Slide 6: Agreements
Transmission scheme
  HST-SFN with joint transmission.
    Same transmission scheme as LTE HST-SFN
  Interested companies are encouraged to study the feasibility and performance benefits for HST-SFN with DPS transmission
  Focus on Rel-15 RAN1 physical layer design in this WI first. FFS for Rel-16 RAN1 physical layer design.

## Slide 7: Simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2x2; 2x4, | 
Precoding scheme | Random precoding based on type1 single panel codebook, bundle size 2 | 
Front loaded DMRS symbol | L0=2 | 
DMRS type | type 1 | 
Number of DMRS symbols | Option 1: DMRS 1+1+1 Option 2: DMRS 1+1+1+1 | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | HST-SFN | 
TDD pattern | DDDDDDDSUU ,S(6D:4G:4U) | 
TRS periodicity | 10ms, 2 slot TRS | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=1000m, Dmin=50m | 
Rank | Option 1: Rank = 1 Option 2: Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | For 500km/h Option 1: 1667Hz Option 2: 1250Hz Option 3: 875Hz Option 4: 972Hz Option 5: 780Hz For 350km/h Option 1: 875Hz Option 2: 780Hz | For 500km/h Option 1: 1667Hz Option 2: 1500Hz For 350km/h Option 1: 1167Hz
Testing metric | SNR @70% of maximum throughput | 
Note :
Interested companies are encouraged to provide simulation results of FDD 30kHz based on assumptions for FDD 15kHz.
  Other DM-RS configuration can be studied, e.g, 1+1.
Other common parameters are the same Rel-15 NR UE demodulation

## Slide 8: Simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 1x2, 1x4 (rank 1); 2x2; 2x4 (rank 2) | 
DMRS type | type 1 | 
Number of DMRS symbols | Option 1: DMRS 1+1+1 Option 2: DMRS 1+1+1+1 | 
Precoding scheme | Random precoding based on type1 single panel codebook, bundle size 2 | 
TDD pattern: | DDDDDDDSUU ,S(6D:4G:4U) | 
Front loaded DMRS symbol | L0=2 | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2 slot | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Option 1: Rank = 1 Option 2: Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 1000Hz Option 2: 1250Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note :
Interested companies are encouraged to provide simulation results of FDD 30kHz based on assumptions for FDD 15kHz.
  Other DM-RS configuration can be studied, e.g, 1+1.
Other common parameters are the same as Rel-15 NR UE demodulation

## Slide 9: Way forward
Network assisted signaling can be studied in future meetings for demodulation.