## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 – 30 August, 2019
Ericsson, Qualcomm Incorporated, Huawei, HiSilicon
Way forward on Rel-16 MTC RRM enhancement
R4-1910107

## Slide 2: Wake-up signal
Release 15 WUS framework is used to evaluate the release 16 WUS performance.
  Companies are expected to analyse the WUS detection performance of each WUS sequence assuming UE monitors two sequences based on Rel-15 WUS framework in R4-1816334.
  The simulation assumptions will be updated if necessary.

## Slide 3: MPDCCH performance improvement for RLM
RAN4 shall wait for further RAN1 progress and based on that agree on the simulation assumptions at next meeting.

## Slide 4: Preconfigured UL resource
Both in serving cell relaxed monitoring mode and in serving cell non-relaxed monitoring mode, if UE is configured with RSRP change for TA validation, the first and the second measurements used for validating the TA shall satisfy the following conditions
    The first measurement (RSRP1) shall be performed within following time range: T1 – N ≤ T1’ ≤ T1 + N;
    The second measurement (RSRP2) shall be performed within following time range: T2 – M ≤ T2’<T2;
    Where T1’ is the time when RSRP1 becomes available, T1 is the time when TA is obtained, N is TBD, T2’ is the time when RSRP2 becomes available, T2 is the time when TA is validated, M TBD.
Relaxation on serving cell monitoring is allowed regardless of TA validation mechanism.

## Slide 5: Preconfigured UL resource
eNB can configure the UE with any of K=1 and K=2, i.e. one or two thresholds for validating the TA when configured with serving cell measurement change attribute.

## Slide 6: DL quality reporting
The evaluation period at least includes T2.
The definition of measurement accuracy of DL quality report in MSG3 can be reused from MSG3 based DL quality report for NB-IoT.