## Slide 1: Analysis assumption for NR CA_n78-n79
Mediatek, Skyworks, Qorvo, [Qualcomm]
­­­3GPP TSG-RAN WG4 Meeting #92 R4-1910269
Ljubljana, Slovenia, 20th to 26th Aug. 2019

## Slide 2: Analysis assumption
Agreement 1:
Parameter | Value | Unit
Antenna isolation | 10 | dB
Diplexer out of band isolation | 15 | dB
n79 filter rejection on n78 | 25 | dB
n78 filter rejection on n79 | 25 | dB
n78/n79 front-end loss | 4 | dB
SNR requirement for QPSK | -1 | dB
Agreement 2: ΔTIB,c as below, ΔRIB,c is not required to be changed
Inter-band DC Configuration | E-UTRA and NR Band | ΔTIB,c [dB]
CA_n78-n79 | n78 | 0.56
 |  | [0.8]1,5
 |  | [1.5]2,5
 | n79 | 0.56
 |  | [1.5]3,5
 |  | [0.8]4,5
Note 1: 3300M to 3700M Note 2: 3700M to 3800M Note 3: 4400M to 4500M Note 4: 4500M to 5000M Note 5: These requirements apply for UE supports simultaneous RX/TX for CA_n78-n79 while NR band n78 not sharing path with band 77 in current release. Note 6: The requirements apply for UE not support simultaneous RX/TX for CA_n78-n79 Note 7: The CA_n78-n79 does not support mandatory simultaneous RX/TX in current release |  | 

## Slide 3
Agreement 3: For UE supporting band n77 and n79, CA_n77-n79 can also support CA_n78-n79 without mandatory simultaneous RX/TX in current release
Interested companies are encouraged to provide analysis

## Slide 4: Reference
R4-1909058 MSD on asyncronous operation for n78-n79
R4-1909946 B42_n79 for UE supporting NR bands n78 and n79 only
R4-1908061 Feasibility of asynchronous operation of CA_n78-n79 MSD due to cross band isolation