## Slide 1
3GPP TSG-RAN WG4 Meeting #92Bis R4-1910933
Chongqing, China, 14th – 18th Oct, 2019
Agenda Item: 8.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Agreements
Scenario
    for LTE PCell of EN-DC, the RRM enhanced requirements specified in Rel-16 LTE HST WI can be reused
    it is proposed to consider intra-frequency measurement for high speed scenario in Rel-16 NR HST WI

## Slide 3: Agreements
Cell re-selection
    it is proposed to enhance the intra-frequency cell reselection requirements (Tdetect,NR_Intra, Tmeasure,NR_Intra and Tevaluate,NR_Intra) to support high speed of 500km/h
    the intra-frequency cell reselection requirements of NR high speed scenario are proposed to be as following:
 | SMTC periodicity > 20ms |  |  | SMTC periodicity <= 20ms |  | 
DRX cycle length [s] | Tdetect,NR_Intra [s] | Tmeasure,NR_Intra [s] | Tevaluate,NR_Intra [s] | Tdetect,NR_Intra [s] | Tmeasure,NR_Intra [s] | Tevaluate,NR_Intra [s]
0.32 | 2.56*1.5 (8*1.5) | 0.32*1.5 (1*1.5) | 0.96*1.5 (3*1.5) | 2.56 (8) | 0.32(1) | 0.96(3)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3) | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3) | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3) | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 4: Agreements
Cell identification delay in connected state
    for intra-frequency measurement, it is proposed to only consider the case of without measurement gap in Rel-16 NR HST WI
    for no DRX case, the current PSS/SSS detection delay requirements, measurement delay requirements and SSB index acquiring delay requirements are applicable to the high speed scenario
    for the case of DRX cycle is configured, the current PSS/SSS detection delay, measurement delay and SSB index acquiring delay requirements are not suitable for the high speed scenario, and enhancement is necessary

## Slide 5: Agreements
Inter-RAT measurement
    it is proposed to enhance the NR inter-RAT measurement requirements before EN-DC and the LTE inter-RAT measurement requirements for SA
    NR inter-RAT measurement requirements before EN-DC are proposed as following:
    for LTE inter-RAT measurement in SA scenario, it is proposed to enhance TIdentify,E-UTRAN for the case that no DRX is in use with Tinter1 of 30ms
    for LTE inter-RAT measurement in SA scenario, it is proposed to enhance TIdentify,E-UTRAN for the case that DRX is in use
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 (8 x 1.5) | 0.32(1 x 1.5) | 0.96(3 x 1.5)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 Note1 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 6: Agreements
signaling
    it is proposed to introduce network flag to indicate UE to apply the enhanced measurement requirements in NR high speed scenario
    it is proposed to introduce UE capability to indicate whether UE supports the enhanced measurement requirements for NR high speed scenario