## Slide 1: WF for 30MHz channel bandwidth in band n28
Agenda item: 9.21.1
Source: Huawei, HiSilicon, Skyworks Solutions Inc.
3GPP TSG-RAN WG4 #92bis R4-1912979
Chongqing, China, 14th – 18th Oct, 2019

## Slide 2: General MPR requirements
Agreement:
  RAN4 need to specify general MPR requirements for 30MHz in band n28, since the relative channel bandwidth is limited by 3% for FDD band based on current spec.

## Slide 3: AMPR requirements
Agreement:
  NS_17 and NS_18 aren’t applicable to China.
  It’s possible for n28 30MHz deployment in EU.
  NS-18 is FFS depending on 30MHz support in Europe.
  NS-17 is not needed for 30MHz.

## Slide 4: MPR/AMPR assumption
PA calibrated to deliver -30dBc ACLR for a fully allocated QPSK DFT-S-OFDM waveform at 1 dB MPR,
-28 dBc image and carrier rejection,
30 MHz channel bandwidth located at the lowermost channel (703~733) (Center frequency is 718 MHz.)
CIM3: 60 dBc

## Slide 5: REFSENS
Evaluate two cases in band n28 with same UL allocation (assumption: 25RB for 15KHz SCS, 10RB for 30KHz SCS).
  Case 1: asymmetric channel bandwidth (UL 20MHz/DL 30MHz)
  Case 2: symmetric 30 MHz channel bandwidth

## Slide 6: Chairman note
  => No objections on proposal 1 in R4-1912466. Detailed wording will be discussed further.

## Slide 7: Reference
R4-1910888 Work plan for adding wider channel bandwidth in NR band n28, CBN, Huawei, HiSilicon
R4-1911496 [n28BW] TP on BS RF requirements for adding wider channel bandwidth in band n28, Huawei, HiSilicon, CBN
R4-1911497 [n28BW] Discussion on UE RF REFSENS for adding wider channel bandwidth in band n28, Huawei, HiSilicon, CBN
R4-1911498 [n28BW] Discussion on UE RF spurious emission and MPR simulations assumption for adding wider channel bandwidth in band n28, Huawei, HiSilicon, CBN
R4-1911613 n28 supporting 30MHz, Shanghai Chen Si Electronics
R4-1912466 Views on n28 Bandwidth Extension to 30MHz, Skyworks Solutions Inc.
R4-1912466 30 MHz channel bandwidth in Band n28, Qualcomm Incorporated
R4-1912369 TP on BS RF requirements for adding channel bandwidth in band n28, CATT