## Slide 1: Way forward on activation delay extension due to multiple SCell activation
Apple, …
R4-1913501
3GPP TSG-RAN WG4 Meeting #93
Reno, US, 18th – 22nd November 2019

## Slide 2: Background
Followings were agreed in last RAN4 #92bis meeting
Principle to define the activation requirement for multiple Scells
  while activating an SCell, if any other SCell is activated or deactivated, UE is assumed to do activation on multiple SCells in parallel, provided that “the SSB SCS of SCell being activated on the same band is the same” or “the SSB SCS of SCell being activated on the same band is different and the combination of SCSs of data and SSB for all CCs in the same band is supported by UE.
    Except MAC-CE processing and search.
  While activating an unknown SCell, if any other unknown SCell is activated, the activation delay of the concerned SCell should further consider the number of parallel cell detection performed by UE on multiple SCCs.
    The number of searcher is assumed as 2 in RRM requirements.
Activation delay is expected to be increased if the interruption due to activating/deactivating on another cell causes the UE to miss receiving an SSB on cell currently being activated

## Slide 3: HARQ feedback priority
Agreement in RAN4 #93:
  The activation timeline of the concerned SCell is not impacted by the HARQ feedback of another SCell

## Slide 4: Delay extension due to MAC PDU processing
Agreements in RAN4 #93:
  For activation of multiple cells, where single MAC command is used, the value of THARQ remains the same as that for single cell.
  MAC PDU processing for activation of multiple cells with a single MAC command will be 3 ms
Open issues for RAN4 #94:
  Requirement scope of multiple SCell activation:
    Option 1:
      In EN-DC, NE-DC, NR SA, RAN4 to define requirements only for the case where a single MAC command is used to activate multiple SCells
      For NR-DC RAN4 to define requirements for the case where one MAC command per CG is used.

## Slide 5: Delay extension due to interruption
Agreements in RAN4 #93
  Interruption occurs on the SSB for AGC settling of the target to-be-activated SCell
    In intra-band case (target to-be-activated SCell and aggressor SCell are in the same band), when the interruption occurs on the SSB for AGC settling of the target to-be-activated SCell, the activation delay extension shall be the whole AGC settling time delay right after this interruption, and the whole AGC settling time delay means the total time period for a new AGC settling procedure with the new TSMTC_MAX.
    In inter-band case (target to-be-activated SCell and aggressor SCell are in different bands), when the interruption occurs on the SSB for AGC settling of the target to-be-activated SCell, the activation delay extension shall be 1 extra TSMTC_MAX.
  When the interruption occurs on the SSB for cell synchronization or T/F tracking of the target to-be-activated SCell, the activation delay extension shall be 1 extra TRS.
  When the interruption occurs on the L1-RSRP reporting resource of the target to-be-activated SCell, the activation delay extension shall be the extra time for next available L1-RSRP/CSI reporting resource.
  When the interruption occurs on the CQI measurement/reporting occasion of the target to-be-activated SCell, the activation delay extension shall be the extra time for next available CQI measurement/reporting resource.
Open issues for RAN4 #94
  FFS on the delay extension when Interruption occurs on the L1-RSRP reporting resource of the target to-be-activated SCell
    Option 1: 1 extra L1-RSRP RS periodicity
    Option 2: 1 extra TL1-RSRP_Measurement_Period_SSB or TL1-RSRP_Measurement_Period_CSI-RS (depends on which RS is used for the L1-RSRP measurement)
    Other options are not precluded

## Slide 6: Delay extension due to searcher limitation
Agreements in RAN4 #93
  For activating known cells, the UE should be able to run its loops in parallel. No scaling in terms of number of SSB/SMTC’s is needed.
  For unknown SCell case, when more than 1 unknown SCells are activated, the activation delay should be extended such that the cell detection time for each SCell is scaled by N.
    Sequential search is not needed if MRTD is no larger than 260ns.
    N is FFS

## Slide 7: Other delay extension
Agreements in RAN4 #93
  When activating multiple SCells, TCSI_Reporting will be same as that for single cell.
Open issues for RAN4 #94
  Interruption(s) on other serving cells when multiple SCells are being activated.

## Slide 8: Wayforward for RAN4 #94
Companies are encouraged to provide analysis on the open issues summarized in previous slides.
Companies are encouraged to provide CR on the multiple SCell activation requirement in RAN4 #94.