## Slide 1: WF on Rel-15 EN-DC power class
vivo
3GPP TSG-RAN WG4 Meeting #93 R4-1913553
Reno, USA, 18-22 Nov 2019
Agenda item: 7.5.4.1

## Slide 2: Background
Because current R15 signalling doesn’t distinguish NR power class (PC) between EN-DC and SA mode, one case was identified as causing the ambiguity
Problematic case: For SA/NSA dual mode UE which support 2Tx UL MIMO in SA with 23+23dBm PA configurations but only 1Tx NR in ENDC.
Identified problem: this UE may report NR=PC2 in “RAN2 NR PC capability signalling”, but can only support NR=PC3 in NSA mode if only 1Tx NR in EN-DC

## Slide 3: WF
RAN4 agrees that
  When UE supports Power Class 2 UL MIMO in NR standalone operation mode with 2 23dBm Pas, UE supports Power Class 3 for NR when configured for EN-DC unless UE declares support of 2-MIMO layers for uplink for EN-DC for NR band that is part of EN-DC configuration
    In above case, in Rel-15 the network would not know that the NR power class was limited to PC3 in EN-DC operation, so performance may be sub-optimal, but functionality is not broken
  no new signalling to be introduced in R15 for this case.
  RAN4 will study the necessity to introduce new power class capability signalling in R16
Inform RAN2 the above RAN4 agreement.

## Slide 4: This page is only for demonstration purpose, separated discussion is needed for approval. Draft LS on ENDC power class in R15
1. Overall Description:
RAN4 has discussed the clarification of ENDC power class in R15. For SA/NSA dual mode UE which support PC2 2Tx UL MIMO in SA but only 1Tx NR in ENDC, power class of NR in ENDC may be different from the power class of SA NR in capability signalling because of UE configurations e.g. UE PA configurations of 23+23dBm can support NR=PC2 in SA UL MIMO but may only support NR=PC3 in NSA mode if only 1Tx NR in EN-DC.
As the solution, RAN4 has agreed that when UE supports Power Class 2 UL MIMO in NR standalone operation mode with 2 23dBm Pas, UE supports Power Class 3 for NR when configured for EN-DC unless UE declares support of 2-MIMO layers for uplink for EN-DC for NR band that is part of EN-DC configuration.
2. Actions:
To RAN 2:
RAN4 kindly ask RAN2 to be informed about the above agreement in RAN4.

## Slide 5: This page is only for demonstration purpose, separated discussion is needed for approval Proposed CR to 3GPP TS 38.101-3 V15.7.0 (2019-09)
6 Transmitter characteristics
6.1 General
Unless otherwise stated the transmitter characteristics are specified at the antenna connector(s) of the UE for the bands operating on frequency range 1 and over the air of the UE for the bands operating on frequency range 2. The requirements for frequency range 1 and frequency range 2 can be verified separately. For the carrier in frequency range 1, requirements can be verified with NR FR2 link disabled. For the carrier in frequency range 2, requirements can be verified in OTA mode with E-UTRA connecting to the network by OTA without calibration.
Unless otherwise stated, requirements for NR transmitter written in TS 38.101-1 [2] and TS 38.101-2 [3] apply and are assumed anchor agnostic. Unless otherwise stated, if UE meets the maximum output power requirements of Power Class 2 in NR standalone operation mode only by the sum of the power at two UE antenna connectors e.g. 23dBm+23dBm, the said UE supports Power Class 3 NR in EN-DC if UE does not declare support of 2-layer for EN-DC on this NR band. Requirements are verified under conditions where anchor resources do not interfere NR operation.

## Slide 6: Reference
(1) R4-1910728 About EN-DC power class clarification OPPO
(2) R4-1910810 On clarification of ENDC power class in R15 vivo
(3) R4-1912509 On EN-DC power class Huawei, HiSilicon
[4] R4-1913067 Summary of Tx diversity and eMIMO full power transmission, Ericsson