## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, USA, November 18 -22, 2019
Ericsson
Way forward on Rel-16 MTC RRM enhancement
R4-1914729

## Slide 2: Wake-up signal
Based on the Rel-16 WUS contributions provided to RAN4#92bis meeting, following options are identified:
  Option 1: : Rel-15 WUS reception requirements apply for Rel-16 UE.
  Option 2: Required number of repetitions for WUS reception with 1 tx antenna when DRX cycle length is ≤ 1.28 s is increased from 32 to 64. Others can be kept unchanged.
It is agreed to use option 1 for release 16 WUS, i.e. release 15 reception requirements are reused.

## Slide 3: Preconfigured UL resource
When TA is obtained in RRC_IDLE mode, the values of M and N are derived using option 1. The values are defined as follows:
DRX cycle [2] | min (Tmeasure_intra_UE cat M1 in nonDRX, DRX_cycle length) | Value of M and N [ms]
0.32 | min(960, DRX cycle) | 320
0.64 | min(960, DRX cycle) | 960
1.28 | min(960, DRX cycle) | 960
2.56 | min(960, DRX cycle) | 960

## Slide 4: Mobility enhancement: RSS based RSRP measurement for BL UEs
Improved measurement accuracy requirements for RSRP based on RSS is defined based on L1 period of 320 ms.
RSS based RRM measurements are allowed in RRC_CONNECTED state if they can be performed without using measurement gaps.
Es/Iot [dB] | Nokia | Ericsson | Huawei | Intel
≥ -6 | TBD | +/- 4 dB | TBD | TBD
≥ -12 dB | TBD | +/- 5 dB | TBD | TBD
-15 <= Es/Iot <= -12 dB | TBD | +/- 6 dB | TBD | TBD

## Slide 5: Mobility enhancement: RSS based RSRP measurement for non-BL CE UE
Es/Iot [dB] | Nokia | Ericsson | Huawei | Intel
≥ -6 | TBD | +/- 4 dB | TBD | TBD
≥ -12 dB | TBD | +/- 4 dB | TBD | TBD
-15 <= Es/Iot <= -12 dB | TBD | +/- 5 dB | TBD | TBD
Improved measurement accuracy requirements for RSRP based on RSS is defined based on L1 period of 320 ms.

## Slide 6: MPDCCH performance improvement for RLM
RLM core requirements, i.e., TS36.133 7.19, can be applicable for UE category M1 configured with improved MPDCCH.
RAN4 discuss the SNR test points of RLM Qin/Qout with improved PDCCH in RRM performance part.

## Slide 7: DL quality reporting
RAN4 should set more accurate DL channel quality report requirements compared with Rel-14 NB-IoT DL channel quality accuracy requirements.
Proposed 2-bits reporting mapping table.
Reported level | Reported value | MPDCCH repetition level | MPDCCH aggregation level
0 | noMeasurement | No measurement reporting | No measurement reporting
1 | candidateRep-1 | max(1, Rmax/4) | 24
2 | candidateRep-2 | Rmax | 24
3 | candidateRep-3 | min(2×Rmax, 256) | 24