## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, US, 18 – 22 November 2019
Huawei, HiSilicon
WF on Rel-16 eMTC RRM
R4-1914975

## Slide 2: DL quality report
Same MPDCCH parameters are used for DL quality reporting in idle and connected mode.
When RL is reported, the accuracy requirements of NB-IoT are re-used for eMTC DL quality reporting in both idle and connected modes.
When AL is reported, the accuracy requirements for eMTC DL quality reporting in both idle and connected modes are given in Table 1.
PDCCH Repetition | Pm-Dsg (%) | Conditions |  |  |  | 
 |  | Ês/Iot | Io NOTE 1 range |  |  | 
 |  |  | E-UTRA operating band groups NOTE 2 | Minimum Io |  | Maximum Io
 |  | dB |  | dBm/15kHz | dBm/BWChannel | dBm/BWChannel
AL NOTE 1 | ≤1 |  -6 dB | FDD-M1_A, TDD-M1_A | -121 | N/A | -70
 |  |  | FDD-M1_B | -120.5 | N/A | -70
 |  |  | FDD-M1_D | -119.5 | N/A | -70
 |  |  | FDD-M1_E, TDD-M1_E | -119 | N/A | -70
 |  |  | FDD-M1_F | -118.5 | N/A | -70
 |  |  | FDD-M1_G | -118 | N/A | -70
 |  |  | FDD-M1_N | -114.5 | N/A | -70
AL/4 NOTE 1 | >1 |  -6 dB | Note 4 | Note 4 | Note 4 | Note 4
NOTE 1: AL is the reported MPDCCH aggregation level that UE has reported. NOTE 2: Io is assumed to have constant EPRE across the bandwidth. NOTE 3: E-UTRA operating band groups are as defined in Section 3.5. NOTE 4: The same bands and the same Io conditions for each band apply for this requirement. |  |  |  |  |  | 

## Slide 3: DL quality report
Define the 2-bit DL quality report mapping as Table 2.
Reported value | NPDCCH repetition level
candidateRep-1 | Rmax/8 (NOTE 1)
candidateRep-2 | Rmax/4 (NOTE 2)
candidateRep-3 | Rmax (NOTE 3)
candidateRep-4 | 4×Rmax (NOTE 4)
NOTE 1: When Rmax is less than 8, set candidateRep-1 to 1. NOTE 2: When Rmax is less than 4, set candidateRep-2 to 1. NOTE 3: When Rmax is 1, set candidateRep-3 to 2. NOTE 4: When Rmax is more than 64, set candidateRep-4 to 256. NOTE 5: MPDCCH Aggregation level is assumed as 24. | 

## Slide 4: PUR
The requirements for measurement for PUR TA validation is derived based on the need from UE mobility perspective.
The requirements for measurement for PUR TA validation is defined independent of requirements for other measurement.
The requirements for measurement for PUR TA validation defines the time period before PUR transmission within which UE should have a RSRP measurement that fulfils the accuracy requirements.
UE should have an RSRP measurement with the 320ms before the PUR transmission.

## Slide 5: Mobility enhancement
Re-use the current measurement period for CRS based measurement for RSS based measurement.
UE capable of RSS based measurement should fulfil the RSS based measurement requirements for the serving cell as long as RSS is transmitted in in the serving cell.
RAN4 should discuss whether RSS measurement requirements are applicable to neighbour cell or not.