## Slide 1: WF on inter-frequency without MG
CMCC
3GPP TSG-RAN WG4 Meeting #93 R4-1915853
Reno, USA, 18th – 22nd Nov, 2019
Agenda Item: 9.15.1.5

## Slide 2: Background
R4-1912739 WF on inter-frequency without MG was agreed in RAN4#92 bis meeting.

## Slide 3: Impact on the specs
Definition of inter-frequency measurement without MG
CSSF within gap and CSSF outside gap
The delay requirements for inter-frequency measurement without MG
Scheduling and measurement restriction
UE capability
Minimum requirements at transitions
Measurement Gap Sharing

## Slide 4: Definition
The UE can perform inter-frequency SSB based measurements without measurement gaps if
  the SSB is completely contained in the active BWP of the UE.

## Slide 5: CSSF factor (1)
The definitions of CSSF within gap and outside gap are not changed.
The number of searchers is up to 2 when discussing the requirement of CSSF outside gap.
For CSSF outside gap, the performance of PCC in NR SA should remain the same. Therefore, the inter frequency MO without gap shares the same searcher as all the other SCCs.
When configured MG is partially overlapped with interfrequency SMTC and interfrequency SSB is completely contained in the active BWP of the UE
  Option 1: Define requirements based on the assumption that UE perform measurement outside gaps (same as intra-frequency measurement without MG)
  Option 2: Define requirements based on the assumption that UE perform measurement within gaps
Notes: 1910819

## Slide 6: CSSF factor (2)
Scenario | CSSFoutside_gap,i for FR1 PSCC | CSSFoutside_gap,i for FR1 SCC | CSSFoutside_gap,i for FR2 PSCC | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is required Note 2 | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is not required | CSSFoutside_gap,i for inter-frequency MO without MG
EN-DC with FR1 only CA | 1 | Number of configured FR1 SCell(s) + Y | N/A | N/A | N/A | Number of configured FR1 SCell(s) + Y
EN-DC with FR2 only intra band CA | N/A | N/A | 1 | N/A | Number of configured FR2 SCells + Y | Number of configured FR2 SCells + Y
EN-DC with FR1 +FR2 CA (FR1 PSCell) Note 1 | 1 | 2×(Number of configured SCell(s) + Y -1) | N/A | 2 | 2×(Number of configured SCell(s) + Y -1) | 2×(Number of configured SCell(s) + Y -1)
EN-DC with FR1 +FR2 CA (FR2 PSCell) Note 1 | N/A | Number of configured SCell(s) + Y | 1 | N/A | Number of configured SCell(s) + Y | Number of configured SCell(s) + Y
Note 1: Only one NR FR1 operating band and one NR FR2 operating band are included for FR1+FR2 inter-band EN-DC. Note 2: Selection of FR2 SCC where neighbour cell measurement is required follows clause 9.2.3.2. Note3: Y is the number of configured inter-frequency MOs without MG that are being measured outside of MG |  |  |  |  |  | 
Example: Table 9.1.5.1.1-1: CSSFoutside_gap,i scaling factor for EN-DC mode

## Slide 7: The delay requirements (1)
DRX cycle | TPSS/SSS_sync_inter
No DRX | max( 600ms, ceil( 5 x Kp) x SMTC period )Note 1 x CSSFinter
DRX cycle≤ 320ms | max( 600ms, ceil(1.5x 5 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(5 x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table1: Time period for PSS/SSS detection, (Frequency range FR1)
DRX cycle | TPSS/SSS_sync_inter
No DRX | max(600ms, ceil(Mpss/sss_sync_inter x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(600ms, ceil(1.5 x Mpss/sss_sync_inter x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(Mpss/sss_sync_inter x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table2: Time period for PSS/SSS detection, (Frequency range FR2)
For delay requirements, the same sample number of intra-frequency measurement without MG should be adopted for inter-frequency measurement without MG.

## Slide 8: The delay requirements (2)
DRX cycle | TSSB_time_index_intra
No DRX | max(120ms, ceil( 3 x Kp ) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(120ms, ceil (1.5 x 3 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | Ceil(3 x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table3: Time period for time index detection (Frequency range FR1)
Condition NOTE1,2 | TSSB_time_index_inter
No DRX | max(200ms, MSSB_index_inter x max(MGRP, SMTC period)) x CSSFinter
DRX cycle ≤ 320ms | max(200ms, (1.5 x MSSB_index_inter) x max(MGRP, SMTC period, DRX cycle)) x CSSFinter
DRX cycle > 320ms | MSSB_index_inter x DRX cycle x CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. | 
Table4: Time period for time index detection (Frequency range FR2)

## Slide 9: The delay requirements (3)
DRX cycle | T SSB_measurement_period_intra
No DRX | max(200ms, ceil( 5 x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(200ms, ceil(1.5x 5 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil( 5 x Kp ) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table5: Measurement period for interfrequency measurements without gaps(Frequency FR1)
DRX cycle | T SSB_measurement_period_intra
No DRX | max(400ms, ceil(Mmeas_period_inter x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(400ms, ceil(1.5x Mmeas_period_inter x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(Mmeas_period_inter xKp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table6: Measurement period for interfrequency measurements without gaps(Frequency FR2)

## Slide 10: The delay requirements (4)
Mpss/sss_sync_inter: For a UE supporting FR2 power class 1, Mpss/sss_sync_inter = 40 samples. For a UE supporting FR2 power class 2, Mpss/sss_sync_inter = 24 samples. For a UE supporting FR2 power class 3, Mpss/sss_sync_inter = 24 samples. For a UE supporting FR2 power class 4, Mpss/sss_sync = 24 samples.
MSSB_index_inter: For a UE supporting power class 1, MSSB_index_inter = 40 samples. For a vehicle mounted UE supporting power class 2, Mpss/sss_sync_inter = 24 samples. For a UE supporting power class 3, MSSB_index_inter = 24 samples. For a UE supporting power class 4, Mmeas_period_inter = 24 samples.
Mmeas_period_inter: For a UE supporting FR2 power class 1, Mmeas_period_inter =40 samples. For a vehicle mounted UE supporting FR2 power class 2, Mpss/sss_sync_inter=24 samples. For a UE supporting FR2 power class 3, Mmeas_period_inter =24 samples. For a UE supporting FR2 power class 4, Mmeas_period_inter = 24 samples.
When interfrequency SMTC is fully non overlapping with measurement gaps or interfrequency SMTC is fully overlapping with MGs, Kp=1
When interfrequency SMTC is partially overlapping with measurement gaps, Kp = 1/(1- (SMTC period /MGRP)), where SMTC period < MGRP

## Slide 11: Scheduling and measurement restriction
Synchronization is always assumed for partial and fully overlapped TDD carriers that to be measured for inter-frequency measurement without MG. FFS on how UE can aware on the synchronization condition
  For TDD bands on FR1, UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols to be measured, and on 1 data symbol before each consecutive SSB symbols to be measured and 1 data symbol after each consecutive SSB symbols to be measured within SMTC window duration
  No need to consider second SMTC case for scheduling restriction requirements in inter-frequency measurement without MG for TDD bands on FR1.
  No need to consider second SMTC case for scheduling restriction requirements in inter-frequency measurement without MG in FR1 mixed numerology(UE is not capable to support mixed numerologies) and FR2 cases.
  FFS: In FR1 mixed numerology(UE is not capable to support mixed numerologies) and FR2 cases, UE is not expected to transmit PUCCH/PUSCH/SRS or receive PDCCH/PDSCH/TRS/CSI-RS for CQI on all symbols within SMTC window duration.

## Slide 12: UE capability
FFS on optionality of inter-frequency measurement without MG

## Slide 13: Minimum requirements at transitions
When the measurement on one intra-frequency measurement object or inter-frequency measurement object transitions from measurements performed outside gaps to measurements performed within gaps or vice versa during one measurement period, the cell identification and measurement period requirements with the longer delay apply.

## Slide 14: Measurement gap sharing
Measurement gap sharing shall be applies when UE requires measurement gaps to identify and measure cells on intra-frequency carriers or when SMTC configured for intra-frequency measurement are fully overlapping with per-UE measurement gaps, and when UE requires measurement gaps UE is configured to identify and measure cells on inter-frequency carriers, or when SMTC configured for inter-frequency measurement are fully overlapping with per-UE measurement gaps, E-UTRA gap-needed inter-frequency carriers and inter-RAT UTRAN carriers and/or inter-RAT GSM carriers.

## Slide 15: Way forward
Send LS to RAN1 and RAN2 to inform RAN4 agreements on inter-frequency measurement without MG in next meeting
Agree on the TS38.133 CR in next meeting