## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, Nevada, USA, 18 - 22 November, 2019
Huawei, HiSilicon, China Telecom, MediaTek
Way forward on LTE FDD intra-band contiguous CA performance with minimum channel spacing
R4-1915885

## Slide 2: Way forward
Define demodulation performance requirements for intra-band contiguous CA with minimum channel spacing for FDD with the following bandwidth combinations:
Further study if single carrier requirements can be reused
  If single carrier requirements can be reused then define requirements for the following bandwidth combinations
    5+10MHz,
    5+20MHz
    10+10MHz
    10+20MHz
    15+15MHz
    15+20MHz
    20+20MHz
  If single carrier requirements can not be reused then list of channel bandwidth combinations for requirements definition is FFS for down-selection.
  Legacy UE may fail initial acquisition due to minimum channel spacing.
Applicable scenario:
  Scenario #1: Inter-band CA with >3 CCs, where Band 1 is with 1 CC and normal spacing (PCell) and Band 2 is with 2 intra-band contiguous CCs and minimum channel spacing (SCell).
  Scenario #2: Band 1 is configured with 1CC and normal spacing, and UE accesses the CC on Band 1, and then handed over to Band 2 with 2 intra-band contiguous CCs and minimum channel spacing

## Slide 3: Way forward
Simulation
  The test configurations for test 15 in Table 8.2.1.1.1-2 can be used as simulation assumptions but with intra-band contiguous CA with minimum channel spacing for alignment