## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 R4-1915913 Reno, NV, USA, 18th – 22nd November, 2019
Huawei, HiSilicon
Way forward on NR URLLC demodulation and CSI requirements

## Slide 2: UE demodulation requirements for high reliability
Introduce PDSCH low BLER high confidence requirement demodulation performance requirements with slot aggregation
  If feasible, define [1] test case to verify 10^-5 BLER
    Target BLER: 10^-5
    Target test confidence level: 99.999%
    Propagation conditions: Static channel
    MCS: MCS5 from MCS Table 3 for PDSCH
    Duplex mode: Both TDD and FDD
      FFS TDD patterns
    SCS:
      TDD: 30KHz
      FDD: 15KHz
        FFS 30KHz
    Test method: refer to R4-1915866 (ad hoc minutes for NR URLLC test feasibility)
      Method 1: Consider aggregation 1 or 2, but no HARQ for non-boosted SNR
      Method 2: No aggregation or HARQ for boosted SNR.
      FFS whether to use method 1 or method 2 for testing (as described below). Adjustment of the baseline parameters for the long test after simulations is not precluded.
Other test cases will be defined with higher BLER and/or lower confidence level
  Other parameter combinations of HARQ, aggregation, channel etc. and further requirements will be considered.
  When further requirements are specified, it will be decided case by case whether to test them at 10^-5 BLER and CL 99.999% or other conditions
  These test cases will include PDSCH aggregation if that is not included in the low BLER/high reliability testing.
    FFS PDSCH aggregation level

## Slide 3: UE CQI reporting requirements for high reliability
Introduce CQI reporting requirements to verify the support of CQI Table 3
  Option 1: CQI test in AWGN
  Option 2: CQI test in fading channel
  FFS:
    Target BLER
    Test metrics

## Slide 4: UE demodulation requirements for low latency
Introduce PDSCH demodulation performance requirements to verify PDSCH processing capability 2
  UL-DL configuration
    FFS on TDD pattern
    FFS on which slots will be scheduled only scheduling PDSCH transmissions on S slot
Introduce performance requirements to verify PDSCH mapping Type B with non-slot configured with fewer symbols than Rel-15 demod
  Option 1: define the additional PDSCH demodulation performance requirements
  Option 2: no specific requirement and verify it in the other introduced performance requirements
Introduce PDSCH demodulation performance requirements for pre-emption
  Verify the performance of UE flushing the URLLC PDSCH REs which is scheduled by DCI transmitted after that URLLC PDSCH
  FFS whether to define the demodulation requirements to verify decoding performance of PDSCH transmitted ahead of corresponding DCI

## Slide 5: BS demodulation requirements for high reliability
Introduce PUSCH low BLER high confidence requirement low BLER, ´high reliability test demodulation performance requirements with slot aggregation
  If feasible, define [1] test case to verify 10^-5 BLER
    Target BLER: 10^-5
    Target test confidence level: 99.999%
    Propagation conditions: Static channel
    MCS: MCS5 from MCS Table 2 for PUSCH
    Duplex mode: Both TDD and FDD
      FFS TDD patterns
    SCS:
      TDD: 30KHz
        FFS 15kHz
      FDD: 15KHz
        FFS 30KHz
    Test method: refer to R4-1915866 (ad hoc minutes for NR URLLC test feasibility)
      Method 1: Consider aggregation 1 or 2, but no HARQ for non-boosted SNR
      Method 2: No aggregation or HARQ for boosted SNR.
      FFS whether to use method 1 or method 2 for testing (as described below). Adjustment of the baseline parameters for the long test after simulations is not precluded.
Other test cases will be defined with higher BLER and/or lower confidence level
  Other parameter combinations of HARQ, aggregation, channel etc. and further requirements will be considered.
  When further requirements are specified, it will be decided case by case whether to test them at 10^-5 BLER and CL 99.999% or other conditions
  Other test cases will include PUSCH aggregation if it is not included in the low BLER/high reliability test
    FFS PUSCH aggregation level

## Slide 6: BS demodulation requirements for high reliability
  FFS on introduction of PUCCH demodulation performance requirements
    FFS on Target BLERDTX->ACK, NACK->ACK, ACK->NACK target error rates

## Slide 7: BS demodulation requirements for low latency
  FFS on introduction of PUSCH demodulation performance requirements with non-slot transmission
  FFS on introduction of Introduce PUSCH demodulation requirements to verify the support of PUSCH mapping Type B with non-slot configured with fewer symbols than Rel-15
  No FFS requirements for UL transmission with grant free/UL configured grant