## Slide 1: WF on SIB reading for cell reselection and HO in NR-U
Intel, ….
R4-1915847
3GPP TSG-RAN WG4 Meeting #93 Reno, USA, 18th – 22nd Nov, 2019

## Slide 2: Background
Observation 1: While camping on an unlicensed carrier, if there is PCI collision with the neighbor cells, the current cell reselection and HO requirements for NR-U [R4-1910551] can not be fulfilled because of the additional time for SIB reading.

## Slide 3: NR-U cell reslection and HO reqruiements
Proposal 1: The below side condition shall be applied to clarify the requirements for cell reselection and HO if target cell is unknown in NR-U agreed in [R4-1910551]
- NO PCI collision for neighbor cells deployed in CCA carriers. Exact wording in specification is TBD.
Proposal 2: For Rel16 NR-U WI, RAN4 will not further discuss the case with PCI collision in carriers using CCA

## Slide 4: Backup(1)
Cell reselection requirements for NR-U agreed in [R4-1910551]
where Md, Mm, Me are the number of DMTC occasions not available at the UE during the corresponding time periods

## Slide 5: Backup(2)
HO requirements in NR-U agreed in [R4-1910551]
“The interruption time for NR FR1 – NR FR1 handover in NR-U:
Tinterrupt = Tsearch + TIU + [20] + ms
where
Tsearch is the time required to search the target cell when the target cell is not already known when the handover command is received by the UE. If the target cell is known, then Tsearch = 0 ms. If the target cell is an unknown intra-frequency cell and the target cell Es/Iot≥[-2] dB, then Tsearch = (1+ L1)* Trs + 2 ms. If the target cell is an unknown inter-frequency cell and the target cell Es/Iot≥[-2] dB, then Tsearch = [(3+ L1´)* Trs + 2] ms where L1 and L1´ is the number of DRS occasions missed due to DL LBT during the intra-frequency and inter-frequency detection period, respectively.
T∆ is the time for fine time tracking and acquiring full timing information of the target cell. T∆ = (1+ L2) * Trs ms where L2 is the number of DRS occasions missing at the UE due to DL LBT during the time tracking period.
TIU is the interruption uncertainty in acquiring the first available PRACH occasion in the new cell. TIU can be up to: (1 + L3) * TSSB,RO + 10 ms where TSSB,RO is the SSB to PRACH occasion association period [3] and L3 is the number of PRACH occasions that are unavailable for PRACH transmission due to LBT failure.
Trs is the DRS periodicity of the target NR cell, details are FFS.
L1≤ L1,max, L´1≤ L´1,max, L2≤ L2,max, L3≤ L3,max, and the maximum values Li,max are TBD.
FFS on UE behavior when L1 > L1,max, L´1 > L´1,max, L2> L2,max, or L3> L3,max.”