## Slide 1: WF on NR-U BS RF RX FRC
ZTE,
R4-1916162
3GPP TSG-RAN WG4 #93
Reno, USA, 18th Nov. - 22th Nov. 2019

## Slide 2: Background
  Some NR-U BS Rx requirements require new FRC(s) to be defined. FRC(s) parameters are critical to define Rx wanted signal and interfering signal configurations. NR BS Rx requirements are essential to finished Rel-16 NR-U WI.

## Slide 3: Simulation assumptions - DMRS
DMRS pattern type 1:
  1 symbol front loaded + 1 additional
  No FDM, no data in DMRS symbol and 3dB power boosting for DMRS

## Slide 4: Simulation assumptions
Receiver type: MMSE
No PT-RS for FR1

## Slide 5: REFSENS and ICS assumptions
Parameter | Value
Propagation | AWGN
Modulation | QPSK
Coding rate | 1/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Channel estimation | practical
Criteria | SNR at 95% throughput

## Slide 6: Dynamic Range assumptions
Parameter | Value
Propagation | AWGN
Modulation | 16QAM
Coding rate | 2/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Channel estimation | practical
Criteria | SNR at 95% throughput

## Slide 7: MCS index and target coding rate
  REFSENS and ICS:
    MCS index = 4
    Target coding rate = 308/1024
  Dynamic Range:
    MCS index = 16
    Target coding Rate = 658/1024

## Slide 8
  REFSENS and ICS FRC
 | G-FR1-A1-10 | G-FR1-A1-11 | G-FR1-A1-12 | G-FR1-A1-13 | G-FR1-A1-14 | G-FR1-A1-15 | G-FR1-A1-16 | G-FR1-A1-17 | G-FR1-A1-18
 | 10MHz | 10MHz | 10MHz | 20MHz | 20MHz | 20MHz | 40MHz | 40MHz | 40MHz
Subcarrier spacing (kHz) | 15 | 30 | 60 | 15 | 30 | 60 | 15 | 30 | 60
Allocated resource blocks | 10 | 10 | 11 | 10 | 10 | 10 | 20 | 10 | 10
CP-OFDM Symbols per slot (Note 1) | 12 | 12 | 12 | 12 | 12 | 2 | 12 | 12 | 12
Modulation | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK
Code rate (Note 2) | 1/3 | 1/3 | 1/3 | 1/3 | 1/3 | 1/3 | 1/3 | 1/3 | 1/3
Payload size (bits) | 888 | 888 | 984 | 888 | 888 | 888 | 1736 | 888 | 888
Transport block CRC (bits) | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
Code block CRC size (bits) | - | - | - | - | - | - | - | - | -
Number of code blocks - C | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Code block size including CRC (bits) (Note 3) | 904 | 904 | 1000 | 904 | 904 | 904 | 1752 | 904 | 904
Total number of bits per slot | 2880 | 2880 | 3168 | 2880 | 2880 | 2880 | 5760 | 2880 | 2880
Total symbols per slot | 1440 | 1440 | 1584 | 1440 | 1440 | 1440 | 2880 | 1440 | 1440
NOTE 1:UL-DMRS-config-type = 1 with UL-DMRS-max-len = 1, UL-DMRS-add-pos = 1 with = 2, = 11 as per table 6.4.1.1.3-3 of TS 38.211 [5]. NOTE 2:MCS index 4 and target coding rate = 308/1024 are adopted to calculate payload size for receiver sensitivity and in-channel selectivity NOTE 3:Code block size including CRC (bits) equals to in sub-clause 5.2.2 of TS 38.212 [15]. NOTE 4:For reference channel A1-10, N,N+5,N+10,..N+45 where N={0,1,2,3,4,5,6}. NOTE 5:For reference channel A1-11, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+2,..., N+18 where N={0,1,2,3,4,5}. NOTE 6:For reference channel A1-12, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N, N+1, N+2,...,N+10 where N={0} .NOTE 7:For reference channel A1-13, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,..N+90 where N={0,1,2,3,...,15}. NOTE 8:For reference channel A1-14, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+5,N+10,..,N+45 where N={0,1,2,3,4,5}. NOTE 9:For reference channel A1-15, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+2,..., N+18 where N={0,1,2,..,6}. NOTE 10:For reference channel A1-16, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,...,N+190 where N={0,1,2,3,4,...,25}. NOTE 11:For reference channel A1-17, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N, N+10, ...,N+90 where N={0,1,2,3,4,...,15}. NOTE 12:For reference channel A1-18, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+5,N+10,..N+45 where N={0,1,2,3,4,5} |  |  |  |  |  |  |  |  | 

## Slide 9
  REFSENS and ICS FRC
 | G-FR1-A1-19 | G-FR1-A1-20 | G-FR1-A1-21 | G-FR1-A1-22 | G-FR1-A1-23 |  |  |  | 
 | 60MHz | 60MHz | 80MHz | 80MHz | 10MHz |  |  |  | 
Subcarrier spacing (kHz) | 30 | 60 | 30 | 60 | 60 |  |  |  | 
Allocated resource blocks | 20 | 10 | 20 | 10 | 6 |  |  |  | 
CP-OFDM Symbols per slot (Note 1) | 12 | 12 | 12 | 12 | 12 |  |  |  | 
Modulation | QPSK | QPSK | QPSK | QPSK | QPSK |  |  |  | 
Code rate (Note 2) | 1/3 | 1/3 | 1/3 | 1/3 | 1/3 |  |  |  | 
Payload size (bits) | 1736 | 888 | 1736 | 888 | 528 |  |  |  | 
Transport block CRC (bits) | 16 | 16 | 16 | 16 | 16 |  |  |  | 
Code block CRC size (bits) | - | - | - | - | - |  |  |  | 
Number of code blocks - C | 1 | 1 | 1 | 1 | 1 |  |  |  | 
Code block size including CRC (bits) (Note 3) | 1752 | 904 | 1752 | 904 | 544 |  |  |  | 
Total number of bits per slot | 5760 | 2880 | 5760 | 2880 | 1728 |  |  |  | 
Total symbols per slot | 2880 | 1440 | 2880 | 1440 | 864 |  |  |  | 
NOTE 1:UL-DMRS-config-type = 1 with UL-DMRS-max-len = 1, UL-DMRS-add-pos = 1 with = 2, = 11 as per table 6.4.1.1.3-3 of TS 38.211 [5]. NOTE 2:MCS index 4 and target coding rate = 308/1024 are adopted to calculate payload size for receiver sensitivity and in-channel selectivity NOTE 3:Code block size including CRC (bits) equals to in sub-clause 5.2.2 of TS 38.212 [15]. NOTE 4:For reference channel A1-19, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index NOTE 5:For reference channel A1-20, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index and 0,8,16,24,32,39,48,56,64,72 for PRB 39 testing NOTE 6:For reference channel A1-21, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,...,N+190 where N={0,1,2,3,4,...,26}. NOTE 7:For reference channel A1-22, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,..N+90 where N={0,1,2,3,...,15}. NOTE 8: For reference channel A1-23, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+2,..N+10 where N={0} |  |  |  |  |  |  |  |  | 

## Slide 10
  Dynamic range FRC
Reference channel | G-FR1-A2-7 | G-FR1-A2-8 | G-FR1-A2-9 | G-FR1-A2-10 | G-FR1-A2-11 | G-FR1-A2-12 | G-FR1-A2-13 | G-FR1-A2-14 | G-FR1-A2-15
CBW | 10MHz | 10MHz | 10MHz | 20MHz | 20MHz | 20MHz | 40MHz | 40MHz | 40MHz
Subcarrier spacing (kHz) | 15 | 30 | 60 | 15 | 30 | 60 | 15 | 30 | 60
Allocated resource blocks | 10 | 10 | 11 | 10 | 10 | 10 | 20 | 10 | 10
CP-OFDM Symbols per slot (Note 1) | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12
Modulation |  | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM
Code rate (Note 2) | 2/3 | 2/3 | 2/3 | 2/3 | 2/3 | 2/3 | 2/3 | 2/3 | 2/3
Payload size (bits) | 3752 | 3752 | 4032 | 3752 | 3752 | 3752 | 7424 | 3752 | 3752
Transport block CRC (bits) | 16 | 16 | 24 | 16 | 16 | 16 | 24 | 16 | 16
Code block CRC size (bits) | - | - | - | - | - | - | - | - | -
Number of code blocks - C | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Code block size including CRC (bits) (Note 3) | 3768 | 3768 | 4056 | 3768 | 3768 | 3768 | 7448 | 3768 | 3768
Total number of bits per slot | 5760 | 5760 | 6336 | 5760 | 5760 | 5760 | 11520 | 5760 | 5760
Total symbols per slot | 1440 | 1440 | 1584 | 1440 | 1440 | 1440 | 2880 | 1440 | 1440
NOTE 1:UL-DMRS-config-type = 1 with UL-DMRS-max-len = 1, UL-DMRS-add-pos = 1 with = 2, = 11 as per table 6.4.1.1.3-3 of TS 38.211 [5]. NOTE 2:MCS index 16 and target coding rate = 658/1024 are adopted to calculate payload size for receiver sensitivity and in-channel selectivity NOTE 3:Code block size including CRC (bits) equals to in sub-clause 5.2.2 of TS 38.212 [15]. NOTE 4:For reference channel A2-7, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+5,N+10,..N+45 where N={0,1,2,3,4,5,6}. NOTE 5:For reference channel A2-8, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N,N+2,..., N+18 where N={0,1,2,3,4,5}. NOTE 6:For reference channel A2-9, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N, N+1, N+2,...,N+10 where N={0}. NOTE 7:For reference channel A2-10, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,..N+90 where N={0,1,2,3,...,15}. NOTE 8:For reference channel A2-11, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+5,N+10,..,N+45 where N={0,1,2,3,4,5}. NOTE 9:For reference channel A2-12, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+2,..., N+18 where N={0,1,2,..,6}. NOTE 10:For reference channel A2-13, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,...,N+190 where N={0,1,2,3,4,...,25}. NOTE 11:For reference channel A2-14, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N, N+10, ...,N+90 where N={0,1,2,3,4,...,15}. NOTE 12:For reference channel A2-15, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+5,N+10,..N+45 where N={0,1,2,3,4,5} |  |  |  |  |  |  |  |  | 

## Slide 11
  Dynamic range FRC
 | G-FR1-A2-16 | G-FR1-A2-17 | G-FR1-A2-18 | G-FR1-A2-19 |  |  |  |  | 
 | 60MHz | 60MHz | 80MHz | 80MHz |  |  |  |  | 
Subcarrier spacing (kHz) | 30 | 60 | 30 | 60 |  |  |  |  | 
Allocated resource blocks | 20 | 10 | 20 | 10 |  |  |  |  | 
CP-OFDM Symbols per slot (Note 1) | 12 | 12 | 12 | 12 |  |  |  |  | 
Modulation | 16QAM | 16QAM | 16QAM | 16QAM |  |  |  |  | 
Code rate (Note 2) | 2/3 | 2/3 | 2/3 | 2/3 |  |  |  |  | 
Payload size (bits) | 7424 | 3752 | 7424 | 3752 |  |  |  |  | 
Transport block CRC (bits) | 24 | 16 | 24 | 16 |  |  |  |  | 
Code block CRC size (bits) | - | - | - | - |  |  |  |  | 
Number of code blocks - C | 1 | 1 | 1 | 1 |  |  |  |  | 
Code block size including CRC (bits) (Note 3) | 7448 | 3768 | 7448 | 3768 |  |  |  |  | 
Total number of bits per slot | 11520 | 5760 | 11520 | 5760 |  |  |  |  | 
Total symbols per slot | 2880 | 1440 | 2880 | 1440 |  |  |  |  | 
NOTE 1:UL-DMRS-config-type = 1 with UL-DMRS-max-len = 1, UL-DMRS-add-pos = 1 with = 2, = 11 as per table 6.4.1.1.3-3 of TS 38.211 [5]. NOTE 2:MCS index 16 and target coding rate = 658/1024 are adopted to calculate payload size for receiver sensitivity and in-channel selectivity NOTE 3:Code block size including CRC (bits) equals to in sub-clause 5.2.2 of TS 38.212 [15]. NOTE 4:For reference channel A2-16, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+8,N+16,...,N+152 where N={0,1,2,...,9}. NOTE 5:For reference channel A2-17, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+8,N+16....,N+72 where N={0,1,2,...,6} and 0,8,16,24,32,39,48,56,64,72 for PRB 39 testing. NOTE 6:For reference channel A2-18, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,...,N+190 where N={0,1,2,3,4,...,26}. NOTE 7:For reference channel A2-19, the allocated RB’s are uniformly spaced over the channel bandwidth at RB index N,N+10,N+20,..N+90 where N={0,1,2,3,...,15}. |  |  |  |  |  |  |  |  | 

## Slide 12: Agreements
SNR values (practical channel estimation) shall be provided for next February RAN4#94 meeting.
No margin should be included.

## Slide 13: References:
  [1]R4-1914286,Draft CR to TS 38.104: Introduction of NR-U in core specification – Rx part, Nokia
  [2]R4-1914232,simulation results for NR-U BS RX FRC,ZTE Corporation
  [3] R4-1914233,NR-U BS REFSENS and dynamic range requirement, ZTE Corporation
  [4] R4-1914234, NR-U BS ICS requirement, ZTE corporation