## Slide 1: WF on MPR Assumptions for PI/2 DMRS Simulations for FR1 and FR2
Qualcomm
3GPP TSG-RAN WG4 NR #93
Reno, USA, 18th - 22th Nov 2019
R4-1916209

## Slide 2: Background
Rel-15:
  Pi/2 BPSK modulation for PUSCH was intended to enable a lower PAPR UL waveform relative to QPSK and QAM.
  The full benefit of BPSK could not be realized due to the DMRS of these waveforms being a higher PAPR Zadoff-Chu modulation.
WI [1] was initiated to investigate the use of different modulation schemes for DMRS to lower its PAPR to be closer to that of the PUSCH Pi/2 BPSK modulation.
  RAN1 has defined a new Pi/2 BPSK modulated DMRS[2,3,4,5] which has a lower PAPR compared to that of Zadoff-Chu DMRS
[6] has simulation results that show Pi/2 BPSK having better EVM and ACLR performance for both FR1 and FR2 compared to Zadoff-Chu
[9] proposes improved MPR for both FR1 and FR2 by using Pi/2 BPSK DMRS
RAN4 further investigation can help determine if a MPR benefit exists from using the Pi/2 BPSK DMRS over Zadoff-Chu DMRS

## Slide 3: WF for FR1 and FR2
Besides the simulation evaluation, RF architecture and possible baseband implementation related to Pi/2 BPSK shall also be considered for evaluation of whether MPR could be improved due to new DMRS design for Pi/2 BPSK.
Other filter shaping parameters for the evaluation are not precluded.
Measurement is also encouraged for the MPR evaluation.

## Slide 4: Way Forward (FR1)
Perform MPR simulations based on the following assumptions for PC3
Simulation assumptions for FR1
  Waveform : shaped DFT-s-OFDM Pi/2 BPSK PUSCH data with up to 4 symbols of Rel-16 shaped Pi/2 BPSK DMRS in a slot
  Waveform time domain shaping function = [0.3 1 0.3]. Any additional shaping filters are not precluded
  Full sweeping of all possible combinations of RB starting locations, RB lengths, SCS’s (15kHz, 30kHz, 60kHz) , BW’s (5MHz,10MHz,15MHz,20MHz,25MHz,30MHz,40MHz,50MHz,60MHz,80MHz,90MHz, 100MHz) to get MPR
  MPR is evaluated as per the RAN4 specs
  Reference waveform : Same as Rel-15 FR1 reference waveform details of which are given below
    unshaped DFT-S-OFDM QPSK PUSCH data
    SCS=15kHz
    No waveform shaping
    Reference waveform BW=20MHz
    Reference waveform RB details
      RB# =100RB

## Slide 5: Way Forward (FR1)
  Use table 1 to generate the appropriate DMRS data
    For waveform length ≤ 4RB use the appropriate CGS sequence in table1. For each set of CGS sequences use the one that gives the maximum PAPR
    For waveform length ≥ 30 RB use Gold code sequence with c_init given in table 1 and any other cell ID not precluded
  The use of a subset of theses DMRS sequence lengths is also not precluded.
Sequence Length | Generation
6 (1 PRB) | 8PSK CGS sequences with phases given by Table 1 of [7] followed by DFT.
12 (2 PRB) | Binary CGS sequence given by Table 1 of [8] followed by pi/2 BPSK modulation followed by DFT.
18 (3 PRB) | Binary CGS sequence given by Table 2 of [8] followed by pi/2 BPSK modulation followed by DFT.
24 (4 PRB) | Binary CGS sequence given by Table 3 of [8] followed by pi/2 BPSK modulation followed by DFT.
≥30 (≥ 5 PRB) | Gold-sequence followed by π/2 BPSK modulation followed by DFT. Use formula from Rel.15 CP-OFDM DMRS and reuse Rel-15 Gold sequence generator. Use c_init= [0 0 0 0 1 1 0 1 0 0 0 1 1 0 0 0 1 1 1 0 1 1 0 0 0 1 0 1 0 1 0]
Table 1 – DMRS data generation

## Slide 6: Way Forward (FR2)
Perform MPR simulations based on the following assumptions for PC3
Simulation assumptions for FR2
  Waveform : shaped DFT-s-OFDM Pi/2 BPSK PUSCH data with up to 4 symbols of Rel-16 shaped Pi/2 BPSK DMRS in a slot
  Waveform time domain shaping function = [0.3 1 0.3]. Any additional shaping filters are not precluded
  Shaped DFT-s-OFDM Pi/2 BPSK PUCSH data with 1 symbol of Rel-16 Pi/2 BPSK DMRS in a slot
  Full sweeping of all possible combinations of RB starting locations, RB lengths, SCS’s (60kHz, 120kHz), BW’s (50MHz, 100MHz, 200MHz, 400MHz) to get MPR
  MPR is evaluated as per the RAN4 specs
  Reference waveform : Same as Rel-15 FR2 reference waveform details of which are given below
    unshaped DFT-S-OFDM QPSK PUSCH data
    SCS=120kHz
    No waveform shaping
    Reference waveform BW=100MHz
    Reference waveform RB details
      RB #=20
      RB_start=23

## Slide 7: Way Forward (FR2)
  Use table 2 to generate the appropriate DMRS data
    For waveform length ≤ 4RB use the appropriate CGS sequence in table2. For each set of CGS sequences use the one that gives the maximum PAPR
    For waveform length ≥ 30 RB use Gold code sequence with c_init given in table 1 and any other cell ID not precluded
  The use of a subset of theses DMRS sequence lengths is also not precluded.
Sequence Length | Generation
6 (1 PRB) | 8PSK CGS sequences with phases given by Table 1 of [7] followed by DFT.
12 (2 PRB) | Binary CGS sequence given by Table 1 of [8] followed by pi/2 BPSK modulation followed by DFT.
18 (3 PRB) | Binary CGS sequence given by Table 2 of [8] followed by pi/2 BPSK modulation followed by DFT.
24 (4 PRB) | Binary CGS sequence given by Table 3 of [8] followed by pi/2 BPSK modulation followed by DFT.
≥30 (≥ 5 PRB) | Gold-sequence followed by π/2 BPSK modulation followed by DFT. Use formula from Rel.15 CP-OFDM DMRS and reuse Rel-15 Gold sequence generator. Use c_init= [0 0 0 0 1 1 0 1 0 0 0 1 1 0 0 0 1 1 1 0 1 1 0 0 0 1 0 1 0 1 0]
Table 2 – DMRS data generation

## Slide 8: References
RP-182863, “Revised WID: Enhancements on MIMO for NR”, RAN1#82, Sorrento, Italy, December 2018
RAN1 95 Chairman’s notes, Spokane, USA, November 2018
RAN1 1901 Ah meeting Chairman’s notes, Taipei, Taiwan, January 2019
RAN1 96 meeting Chairman’s notes, Athens, Greece, March 2019
RAN1 96b meeting Chairman’s notes, Xi’an, China, April 2019
R4-1912560, “PI/2 BPSK DMRS”, RAN4_#92bis, Chongqing, China, Oct 2019
R1-1905921, Final Report of 3GPP TSG RAN WG1 #96b,Section 7.2.8.5, RAN1#97, May 2019.
R1-1901362, Joint proposal on length-12, length-18, and length-24 CG sequences for pi/2 BPSK, RAN1#AH_1901
R4-1913466, MPR enhancement with Pi2 BPSK DMRS, Intel, RAN4#93