## Slide 1: WF on CSI-RS based L3 measurement capability and requirements
OPPO, [ … ]
3GPP TSG-RAN4 Meeting #94e
Electronic Meeting, Feb.24th – Mar.6th 2020
R4-2002258

## Slide 2: Proposal
RAN4 further discuss and conclude the remaining issues for measurement capability in next meeting
    Clarify the understanding of MO configuration, intra-frequency measurement definition and layer definition
    Whether to restrict MO configuration to specify requirements for the limited or selected scenarios
    Define requirements of measurement capability for CSI-RS L3 measurement

## Slide 3: Proposal
  RAN4 to discuss whether/how to define measurement requirements for Case 1 and Case 2 in next meeting.
    Case 1: if associatedSSB is not configured
    Case 2: if associatedSSB is configured for CSI-RS
  The following issues should be discussed in RAN4:
    CSSF
    Scaling factor for RX beam sweeping
    Scheduling restriction
    Restrict for CSI-RS resources outside of DRX/MG duration
    Note: Others are not precluded.

## Slide 4: Issue 1: Measurement capacity

## Slide 5: Background
  In RAN4 94 e-meeting, the following open issues were discussed.
  Applicability and assumption for CSI-RS based measurement capability
    Applicability for CSI-RS based measurement capability
    Measurement capabilities per MO or per layer
  Requirements for measurement capability
    Number of frequency layers to be monitored
    Number of cells to be monitored
    Number of CSI-RS resource/beams to be monitored
    UE capability to indicate maximum number of CSI-RS resources in a slot per MO
    UE buffering and processing capability

## Slide 6: Background
  According to RAN1’s reply LS，frequency layer for CSI-RS mobility resources is measurement object (MO)
  Measurement capability depends on at least
    MO configuration/restriction
    Intra-frequency and inter-frequency measurement definition
    Frequency layer definition
  Measurement capability includes at least
    Number of frequency layers to be monitored
    Number of cells to be monitored
    Number of CSI-RS resource/beams to be monitored

## Slide 7: Applicability for CSI-RS based measurement capability
FFS on whether to introduce restriction of MO configuration
FFS whether to specify requirements for the limited or selected scenarios if no restriction of MO configuration
Candidate options:
  Option 1(MediaTek, OPPO): Only define the requirements when the CSI-RS based measurement is configured with SSB based measurement within the same MO, and UE can perform CSI-RS and SSB measurement with overlapped bandwidth in the same time duration
  Option 2(Ericsson, CATT, CMCC, Huawei, DOCOMO, ZTE, Nokia): No restriction on MO configurations
  Option 3: Other possible restriction in order to specify requirements for the limited or selected scenarios.

## Slide 8: Measurement capabilities per MO or per layer
  Majority view in 1st round discussion is to define measurement capabilities per layer
A frequency layer for CSI-RS is
  Option 1: just the same center frequency of CSI-RS resource
  Option 2: the same center frequency and BW of CSI-RS resource
  Option 3: one MO, i.e. same center frequency, same SCS
  FFS how to align the understanding of MO and frequency layer in RAN4.
  Depend on the definition/restriction of intra-frequency and inter-frequency measurement
  For example:
    If there are both intra and inter frequency measurement in one MO, can we still define the UE capability requirement based on MO?
    In one MO, if there several bandwidths, do they belong to same layer or different layer?
    If the intra-frequency measurement is defined without fixing the center-frequency, there may be several MOs for intra-frequency. Whether to define the MO number for intra-frequency?

## Slide 9: Number of frequency layers to be monitored
Option 1 (MediaTek, OPPO, ZTE, Apple, Ericsson, DOCOMO):
  CSI-RS based L3 measurement does not add additional frequency layers and cells to be monitored on top of the number specified for SSB based measurement.
Option 2(Huawei):
  Assuming no restriction on MO configurations:
    UE shall be able to measure at least 3 CSI-RS frequency layers.
    UE shall be able to measure at least 8 NR frequency layers in total, including SSB frequency layers and CSI-RS frequency layers.
    UE shall be able to measure at least 14 carriers of all RATs in total.
Option 3(CATT):
  If CSI-RS is configured with associated SSB, the measurement capability can be considered the same as SSB based measurement capability.(as option 1)
  If CSI-RS is not configured with any associated SSB, UE is capable to perform CSI-RS based layers.(as option 2)
Not preclude other options.

## Slide 10: Number of cells to be monitored
Option 1 (MediaTek, OPPO, Apple, Ericsson): No need to introduce additional number of cells to be monitored per layer based on L3 CSI-RS on top of the requirements already specified for SSB.
Option 2 (ZTE): UE shall be capable of performing CSI-RS based measurements for at least [8] identified cells in FR1 for intra frequency measurement and at least [4] identified cells in FR1 for inter frequency measurement, at least [6] identified cells in FR2 for intra frequency measurement and at least [4] identified cells in FR2 for inter frequency measurement.
Option 3 (Huawei, CATT): RAN4 should discuss the total number of cells and CSI-RS resources UE should measure per MO.

## Slide 11: Number of CSI-RS resource/beams to be monitored
Option 1(CATT, Huawei, OPPO): UE shall monitor at least 32 CSI-RS resources per frequency layer
Option 2(ZTE, Ericsson, CATT): Number of CSI-RS resources shall be monitored by UE,
  [24] CSI-RS resources for intra frequency measurements in FR1,
  [48] CSI-RS resources for intra frequency measurements in FR2,
  [16] CSI-RS resources for inter frequency measurements in FR1,
  [24] CSI-RS resources for inter frequency measurements in FR2.
Option 3(MediaTek): Requirements defined the same requirements as those for SSB.
Option 4(Qualcomm): The total number of CSI resources that UE can monitor should come from the UE capability maxNumberCSI-RS-RRM-RS-SINR.
  FFS how to split up

## Slide 12: UE capability to indicate maximum CSI-RS resources in a slot per MO
RAN to further discuss whether and how to to indicate maximum CSI-RS resources in a slot per MO
RAN4 decide whether to send LS to ask for RAN1 and RAN2 in next meeting

## Slide 13: UE buffering and processing capability
FFS on UE buffering and processing capability
  Option 1: UE capability on UE buffering and processing time RAN1 defined for PRS is re-used for CSI-RS L3 measurement.
  Option 2: Define UE capability on the minimum separation between two slots with CSI-RS resources.

## Slide 14: Issue 2: Measurement requirements

## Slide 15: Case1: if associatedSSB is not configured
The synchronization level between serving and target cell needs to be clarified in RAN4.
  FFS whether to introduce requirements of synchronization level for intra-frequency and inter-frequency measurement
Measurement requirements :
  Option 1: No requirements specified for CSI-RS L3 measurement
  Option 2: CSI-RS identification time is the CSI-RS measurement periodicity
  Option 2a: If sufficient synchronization of severing cell and neighbor cell can be guaranteed, CSI-RS identification time is the CSI-RS measurement periodicity
  Option 2b: UE shall base the timing on its serving cell, and the requirement needs at least consider the CSI-RS measurement time.

## Slide 16: Case 2: if associatedSSB is configured for CSI-RS,
Measurement requirements ：
  CSI-RS based cell identification can consider:
    1) Cell search via SSB
    2) PBCH decoding
    3) CSI-RS measurement,
    AGC margin should be considered as well.
FFS the case if the MO includes the serving CSI-RS resource with associated SSB
FFS the case if the MO doesn’t include the serving CSI-RS resource and the CSI-RS resource associated SSB is configured

## Slide 17: Scaling factor for RX beam sweeping
Option 1：
  If CSI-RS is not QCL-ed to the associated SSB, UE needs to sweep the RX beam.
    FFS on the scaling factor N
  If the CSI-RS is QCL-ed to the associated SSB, no Rx sweeping is needed only after SSB has been detected.
    Note SSB detection would still need beam sweeping.
  FFS the case without associatedSSB configured.

## Slide 18: CSSF
Option 1：
  RAN4 to re-use the existing requirement of CSSF as much as possible, and the framework of CSSF can be shared by SSB and CSI-RS based L3 measurement.

## Slide 19: Scheduling restriction
The requirements for scheduling restriction are only defined for CSI-RS L3 measurement without gaps
Identify all possible factors which would cause scheduling restriction in next meeting:
  Collision with UL transmission and DL measurement on TDD carrier
  The need of Rx beam sweeping in FR2
  Mix-numerology between data/SSB of serving cell and CSI-RS of neighbour cell

## Slide 20: CSI-RS resources outside of DRX/MG duration
FFS on CSI-RS resources outside of DRX/MG duration
  Option 1(CATT): UE is allowed not to measure the CSI-RS resources that are not within DRX on-duration or measurement gap;
  Option 2 (OPPO, Qualcomm, CATT, Intel, MediaTeK, Huawei): No UE performance requirement is defined for the CSI-RS resources that are not within DRX on-duration or measurement gap;
  Option 3(CATT): the network needs to make sure the configured CSI-RS resources falls within the configured measurement gaps
  Other options are not precluded