## Slide 1: WF on MPR/A-MPR simulation assumptions for NR V2X PC2 UE
Agenda item: 8.4.4.1
Source: Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #94-e R4-2002791
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
In last RAN4 #93 meeting and e-mail discussion, we discussed the basic simulation assumption of the required MPR/AMPR levels for simultaneous PSFCH transmission and PSSCH/PSCCH transmission
In RAN4 #94e, companies provide the MPR simulation results about S-SSB.
In order to derive MPR/AMPR for NR V2X PC2 UE, simulation assumptions were proposed.

## Slide 3: Assumption and parameters for PC2
parameter | Assumption
Center frequency | 5.9GHz
Maximum output power for all kinds of channel | 26 dBm
PA calibrationfor all kinds of channel | PA calibrated to deliver -31dBc ACLR for a fully RB allocated 20MHz QPSK DFT-s-OFDM waveform at 1dB MPR
Modulation for PSSCH | QPSK\16QAM\[64QAM]
PSSCH/PSCCH transmission | For other assumption, the sub-clause 8.1.2 from TR 38.886 can be referred to.
Simultaneous PSFCH transmission for multiple users | For other assumption, the WF (R4-2002758) on MPRA-MPR simulation assumptions and parameters for simultaneous PSFCH transmission can be referred to.

## Slide 4: MPR/AMPR Assumption of S-SSB for NR V2X PC2 UE
parameter | Assumption
Bandwidth | 10/20/30/40MHz
numerology | 15 kHz/30kHz/60kHz
Modulation for PSBCH | QPSK
S-PSS | M-sequence
S-SSS | Golden-sequence
Waveform | CP-OFDM
Carrier leakage | 25dBc
IQ image | 25dBc
CIM3 | 45 or 60 dBc
RB allocation | RBstart: All the possible cases LCRB: 11 RB
S-SSB structure | 

## Slide 5: Reference
R4-2001085 [V2X] TP on S-SSB MPR requirements for NR V2X in band n47, Huawei, HiSilicon
R4-1910707 LS to RAN4 on NR V2X S-SSB design, RAN1, CATT
R4-2001081 [V2X] MPR simulation results for PC2 NR V2X in band n47, Huawei, HiSilicon
R4-2001084 [V2X] TP on RF requirements for PC2 NR V2X UE in band n47, Huawei, HiSilicon
R4-2002032 draftCR for TS 38.101-1 PC2 RF requirements NR V2X, Huawei, HiSilicon
R4-2001215 Summary on E-mail discussion for NR V2X, LG Electronics
R4-2001214 TR update TR38.886 v0.5.0, LG Electronics