## Slide 1: WF on MPR With PI/2 BPSK DMRS
Qualcomm
3GPP TSG-RAN WG4 NR #94-e
24th Feb - 6th Mar 2020
R4-2000470

## Slide 2: Timeline
Tuesday March 3, noon PST: Interested companies complete first round of comments by editing and uploading a modified copy of WF document
Tuesday March 3, 5pm PST: Updated WF document created and uploaded (if necessary)
Wed March 4, noon PST: Interested companies complete second round of comments on updated WF document
Wed March 4, 5pm PST: WF tdoc complete and uploaded to inbox. Per Chairman deadline.

## Slide 3: Open Issues
  Rel-15 FR1 requirement for Pi/2 BPSK
    Option 1: Rel-15 FR1 requirement for Pi/2 BPSK should be revisited firstly.
    Option 2: No revisit is needed.
  Rel-16 FR1 MPR improvement for Pi/2 BPSK DMRS
    Option 1: Qualcomm’s proposed MPR values.
    Option 2: Only consider MPR values if Rel-15 requirement is revisited.
  FR2 MPR values for Pi/2 BPSK w Pi/2 BPSK DMRS
    Option 1: Current FR2 MPR tables remain unchanged.
    Option 2: FFS, due to up to 1.5 dB more power achievable (however this is mostly due to relaxed specification not new DMRS).

## Slide 4: Background (1)
Rel-15:
  MPR values for Pi/2 BPSK waveforms having Zadoff-Chu (ZC) modulated DMRS was agreed for both FR1 and FR2 and placed in the 38.101 specification.
  The full benefit of BPSK could not be realized due to the DMRS of these waveforms being a higher PAPR ZC modulation.
A new Pi/2 BPSK DMRS was created for use with Pi/2 BPSK modulated data that has lower PAPR
In RAN4#93 a WF was agreed to by all interested companies for performing MPR studies on Pi/2 DMRS waveforms. The goal was to determine whether an MPR reduction is possible with Pi/2 BPSK DMRS compared to what is in the current specification for ZC DMRS. (R4-1916209)
R4-1916209 clearly specifies the simulation methodology and restricts the MPR analysis to Pi/2 BPSK DMRS waveforms with Pi/2 BPSK data.

## Slide 5: Background (2) - Positions of each company
Company |  |  | 
 | Issue 1: Rel-15 FR1 requirement for Pi/2 BPSK | Issue 2: Rel-16 FR1 MPR improvement for Pi/2 BPSK DMRS | Issue 3: FR2 MPR values for Pi/2 BPSK w Pi/2 BPSK DMRS
Qualcomm | No revisit required | - The MPR for edge, outer and inner RB allocations for FR1 PC3 can be reduced to zero -The MPR for edge, outer and inner RB allocations for for FR1 PC2 can be reduced to 1.0, 0 and 0 respectively | FFS
Intel | No revisit | Intel has provided MPR values in last meeting, R4-1913466 | Intel has provided MPR values in last meeting, R4-1913466
Huawei | Revisit the Rel-15 power boost requirement and it is worth noting that the DMRS in Rel-15 is ZC based sequence, which has larger PAPR compared to that defined in Rel-16. | MPR could be better than Rel-15 requirements, but the precondition is to revise Rel-15 MPR requirement based on ZC DMRS evaluation. | Only for FR1 in Rel-16
Apple | pi/2 BPSK DMRS is a Rel-16 eMIMO feature and shall not have an impact on Rel-15. | RAN4 should conduct a further study on FR1 MPR with pi/2 BPSK DMRS for the next meeting | RAN4 should conduct a further study on FR2 MPR with pi/2 BPSK DMRS for the next meeting

## Slide 6: WF on Pi/2 BPSK DMRS
The purpose of this work item agreed to in R4-1916209 was to study the MPR requirements for Pi/2 BPSK DMRS with Pi/2 BPSK data for Rel-16
MPR requirements for Zadoff-Chu DMRS with Pi/2 BPSK data can be re-examined as a separate work item under Rel-15 TEI
Intel MPR results for FR1 PC3 also shows 0dB MPR requirements for edge, inner and outer RB allocations which is in agreement with Qualcomm results
Proposal 1:
  Add a new row to the FR1 PC3 MPR spec as shown in table 1
  Put MPR=0 for edge, inner and outer RB allocations for PC3, FR1 with IE powerBoostPiBPSK=0
  Put MPR=TBD for edge, inner and outer RB allocations for PC3, FR1 with IE powerBoostPiBPSK=1
Proposal 2:
  Study MPR for Pi/2 BPSK DMRS with Pi/2 BPSK data for FR1 PC2 and FR2 and present results at next meeting
Modulation |  | MPR (dB) |  | 
 |  | Edge RB allocations | Outer RB allocations | Inner RB allocations
DFT-s-OFDM | Pi/2 BPSK | ≤ 3.51 | ≤ 1.21 | ≤ 0.21
 |  | ≤ 0.52 | ≤ 0.52 | 02
 | Pi/2 BPSK w Pi/2 BPSK DMRS | TBD1 | TBD1 | TBD1
 |  | ≤ 0.02 | ≤ 0.02 | 02
 | QPSK | ≤ 1 |  | 0
 | 16 QAM | ≤ 2 |  | ≤ 1
 | 64 QAM | ≤ 2.5 |  | 
 | 256 QAM | ≤ 4.5 |  | 
CP-OFDM | QPSK | ≤ 3 |  | ≤ 1.5
 | 16 QAM | ≤ 3 |  | ≤ 2
 | 64 QAM | ≤ 3.5 |  | 
 | 256 QAM | ≤ 6.5 |  | 
NOTE 1: Applicable for UE operating in TDD mode with Pi/2 BPSK modulation and UE indicates support for UE capability powerBoosting-pi2BPSK and if the IE powerBoostPi2BPSK is set to 1 and 40 % or less slots in radio frame are used for UL transmission for bands n40, n41, n77, n78 and n79. The reference power of 0 dB MPR is 26 dBm. NOTE 2: Applicable for UE operating in FDD mode, or in TDD mode in bands other than n40, n41, n77, n78 and n79 with Pi/2 BPSK modulation and if the IE powerBoostPi2BPSK is set to 0 and if more than 40 % of slots in radio frame are used for UL transmission for bands n40, n41, n77, n78 and n79. |  |  |  | 
Table 1 – Proposed MPR table for FR1 PC3