## Slide 1: WF on Uplink Full Power Transmission
vivo,
3GPP TSG-RAN WG4#94-e Meeting DRAFT_R4-2002801
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Way Forward (1)
Guidelines:
  All the agreements in this WF are for Rel-16 eMIMO WI and this scope may not be reiterated for detailed issues.
  The numbering scheme is in accordance with second round discussion in [1]

## Slide 3: Way Forward (2)
Sub-topic 2-1: General Scope and Assumption in Rel-16 eMIMO
  Issue 2-1-1: General Assumption for UE Supported Mode
    UE’s support of full power transmission feature’s mode shall follow RAN1 and RAN2 design;
    If UE claim its support of one a mode (from mode-1, mode-2 and the other mode), corresponding performance requirement shall be tested.
    Issue 2-1-2: Down-scoping by only considering up to UE supporting 2 TX ports
    RAN4 only specify MOP requirement for UE supporting up to 2TX ports.
    Issue 2-1-3: Down-scoping by only considering FR1
    At least define UE RF MOP requirement for FR1;
    FFS the necessity and how to define full power transmission feature for FR2.
    Issue 2-1-4: Down-scoping on possible physical implementation for Mode-0, 1, and 2
    FFS UE is not assumed to have 20dBm PA implementation on any single TX antenna connector.
    Mode-2 UE is assumed to have one full rated PA and one non-full rated PA.

## Slide 4: Way Forward (3)
Sub-topic 2-1: General Scope and Assumption in Rel-16 eMIMO (Continual)
  Issue 2-1-5: Clarification on appropriate chapter for full power transmission MOP tests (for FR1)
    Keep Section 6.2 in TS38.101-1 only for single connector/port.
    FFS UE fallback behaviour for single port transmission, and how to capture the requirement (if any) in the specification.
    MOP requirement for full power transmission with 2 TX ports configured for FR1 shall be captured
      Option-1: in Section 6.2D
      Option-2: in new section.
  Issue 2-1-6 UE behavior for fallback DCI (DCI_0_0)
    Option 1: MOP should be tested in which antenna virtualization shall be allowed
    Option 2: Antenna virtualization is not allowed for fallback DCI
    Option 3: UE behaviour for fallback DCI is not needed to be discussed.
    FFS single-port transmitter requirements apply in fallback (same for e.g. UL-MIMO)

## Slide 5: Way Forward (4)
Sub-topic 2-2: Test Configuration and Requirement Applicability for Full Power Transmission MOP Test
  Issue 2-2-1: For Mode 1 UE,
    Only DFT-s-OFDM waveform need to be verified if Rel-15 UL-MIMO rank2 is supported and verified.
  Issue 2-2-2: For Mode 2 UE with 2 ports configuration
    RAN4 core requirement is defined based on full power TPMI(s) UE support;
    It is up to RAN5 to select test configuration to perform test.
  Issue 2-2-3: For Mode 2 UE with 1 port configuration
    Option-1: no need to test
    Option-2: Full power transmission with 2 TX antenna connectors should be verified (sum over two antenna ports connectors), i.e., either UE with antenna virtualization transparent TxD (23+23dBm) or UE with full rated PA (26dBm) is allowed.
  Issue 2-2-4: For Mode 0 UE (“the other mode”) with 2 ports configuration
    Option-1: All supported full power TPMIs are tested
    Option-2: Select only one of full power TPMI(s) for test
    Option-3: RAN4 core requirement is defined based on all supported full power TPMIs, and it is up to RAN5 to select test configuration to perform test.

## Slide 6: Way Forward (5)
Sub-topic 2-3: Unwanted Emissions for Full Power Transmission for FR1
  Issue 2-3-1: Whether unwanted emissions requirement are defined for full power transmission for FR1
    Unwanted emissions mustshould to be verified for all the configuration(s)s of full power transmission, in which MOP requirement is defined and tested.
  Issue 2-3-2: How unwanted emissions requirement are tested for full power transmission for FR1
    The individual outputs of all transmitting antennas shall be summed across frequency and compliance to the SEM specifications requirement should be verified.
    No impact on Rel-15 test for unwanted emission requirement. Regulatory guidance for unwanted emissions measurements should be followed (regardless of release)

## Slide 7: Way Forward (6)
Sub-topic 2-4: UE Power Class Capability
  Issue 2-4-1: New power class capability
    FFS new power class capability for full power transmission,
      Option-1: adding a new power-class capability for two-layer transmissions per NR band (Rel-16)
      Option-2: New power class capability can be defined for a UE transmitting over multiple antennae per NR band. The new power class will be determined as the sum of power on all antennae.
      Option-3: add new power class but how to add depends on the outcome of “EN-DC power class and UL MIMO clarifications” topic in agenda 6.5.4.1
      Option-4: No need to introduce new power class

## Slide 8: Reference
[1] R4-2002885, Email discussion summary for RAN4#94e_#16_NR_eMIMO_UE_RF, Samsung, RAN4#94-e