## Slide 1: WF on MPR requirement for intra-band contiguous UL CA
Huawei, HiSilicon, [Nokia]…
R4-20XXXX
3GPP TSG-RAN WG4 #94e
Feb 24th – Mar 06th, 2020
Electric meeting

## Slide 2: Inner and outer RB allocation
Contiguous RB allocations:
For aggregated channel bandwidth≤100MHz, Inner RB allocation is defined with the equation:
For RBStart,Low = max(1, floor(NRB_alloc /2)), where NRB_alloc=LCRB1*2^µ1+LCRB2*2^µ2
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤ceil[(1/2NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB1*2^µ2
For the case with only RBs configured in CC2, RBStart,Low and RBStart shall accounts for NRB1 in CC1:
RBStart = RBStart1 ∙ 2^m1, if LCRB1 > 0
RBStart = NRB1 ∙ 2^m1 + RBStart2∙2^m2, if LCRB1 = 0
For aggregated channel bandwidth>100MHz
  Option 1:
  For RBStart,Low = max(1, floor(NRB_alloc)), where NRB_alloc=LCRB1*2^µ1+LCRB2*2^µ2
  Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤Floor[(1/3NRB,agg) ]
  RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB1*2^µ2
For the case with only RBs configured in CC2, RBStart,Low and RBStart shall accounts for NRB1 in CC1
  Option 2: Same inner/outer allocation definition with bullet 2, but with a relaxed MPR.

## Slide 3
Inner and outer RB allocation
Non-Contiguous RB allocations:
Inner allocation: IMD3 falls within aggregated channel bandwidth, the equation can be as below:
For RBStart,Low = max(1, floor(NRB_alloc)),
where NRB_alloc = LCRB2 ∙ 2^µ2, if LCRB1=0
NRB_alloc = LCRB1 ∙ 2^µ1, if LCRB2=0
NRB_alloc = (NRB1- RBStart1) ∙ 2^µ1 + (RBStart1+ LCRB2) ∙ 2^µ2, otherwise
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤Floor[(1/3NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB2*2^µ2
Outer allocation:
  Option 1: further group into outer 1 and outer 2, where outer 2 means IM5 falls outside of the -13dBm/MHz SEM mask or in the -25dbm/MHz and -30dBm/MHz spurious region.
  Option 2: all allocations except inner allocation in bullet 1 is an outer allocation, take the worst MPR when defining MPR for outer allocation
  Option 3: all allocations except inner allocation in bullet 1 is an outer allocation, allow MPR to be reduced by the allocation ratio as was done for LTE CA.
  Option 4: further group into outer 1 and outer 2, allow MPR to be reduced by the allocation ratio as was done for LTE CA for outer 2 allocation

## Slide 4: MPR value: contiguous allocation
Modulation |  | MPR for bandwidth class B |  | MPR for bandwidth class C | 
 |  | inner | outer | inner | outer
DFT-s-OFDM | Pi/2 BPSK | TBD | TBD | TBD | TBD
 | QPSK | [1.5]dB | [6]dB | [3]dB | [8]dB
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
CP-OFDM | QPSK | [3.5]dB | [6]dB | [5]dB | [8]dB
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
For contiguous inner allocation, it is encouraged to further evaluate and provide simulation/measurement result on following RB allocation:
  20M+20M(15kHz+15kHz): large allocation , i.e. 53RB53+53RB0
  50M+50M(15kHz+15kHz): large allocation , i.e. 135RB135+135RB0
  100M+60M(30kHz+30kHz): large allocation , i.e. 54RB108+162RB0
  100M+100M(30kHz+30kHz): large allocation , i.e. 136RB137+136RB0
For contiguous Outer allocation, it is encouraged to further evaluate and provide simulation/measurement result on full RB allocations for ≤100MHz and >100MHz.

## Slide 5
MPR value: non-contiguous allocation
Modulation |  | MPR for bandwidth class B |  | MPR for bandwidth class C | 
 |  | inner | outer | inner | outer
DFT-s-OFDM | Pi/2 BPSK | TBD | TBD | TBD | TBD
 | QPSK | [3]dB | [13]dB | [5]dB | [14]dB
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
CP-OFDM | QPSK | [3]dB | [13]dB | [5]dB | [14]dB
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
For non-contiguous inner allocation, it is encouraged to further evaluate and provide simulation/measurement result on RB allocation with IMD5/7 falls into the SEM -13dBm/MHz
  20M+20M: i.e.1RB72+1RB31
  50M+50M: i.e. 1RB198+1RB94
  100M+60M: i.e. 1RB161+1RB132
  100M+100M : i.e. 1RB183+1RB87
For non-contiguous outer allocation, it is encouraged to further evaluate and provide simulation/measurement result on worst RB allocation case: 1RB+1RB for outer2 allocation
  20M+20M: i.e.1RB0+1RB105
  50M+50M: i.e.1RB0+1RB269
  100M+60M: i.e. 1RB0+1RB272
  100M+100M:i.e. 1RB0+1RB272
* Whether Outer allocation need to be further grouped into 2 type depends on the conclusion in slide 3

## Slide 6
AMPR on NS04 and NS27
Currently de-prioritize the NS04 and NS27 in Rel-16 before MPR requirement is completed