## Slide 1: WF on emission requirement for intra-band contiguous UL CA
Huawei, HiSilicon,[ ]…
R4-20XXXX
3GPP TSG-RAN WG4 #94e
Feb 24th – Mar 06th, 2020
emeeting

## Slide 2: Background
In R4-1910273, we used to have agreement on SEM requirement for intra-band contiguous CA which takes the approach as for intra-band EN-DC:
ΔfOOB (MHz) | Spectrum emission limit(dBm) | MBW
± 0 - 1 | Max(Round(10*log(0.15/BWchannel_CA)),-24) | 30kHz
± 1 - 5 | -10 | 1MHz
± 5 – BWchannel_CA | -13 | 1MHz
±BWchannel_CA- BWchannel_CA+5 | -25 | 1MHz
Note 1: BWchannel_CA=nominal channel spacing+Foffset,high + Foffset,low, where the nominal channel spacing, Foffset,high and Foffset,low refers to subclause 5.4A.1 and subclause 5.3A.3. |  | 
In RAN4 #94e meeting, the problem that IMD3 falls into offset 0-1MHz makes large MPR was raised, the summary can be summarized as below:
Since nominal channel space for CA are specified relative large and fixed with numerology which ensures there is a channel space entry less than or equal to the nominal channel space for any CC configurations, with the assumption on ACLR MBW=BWChannel_CA – 2*max(GB(low),GB(high)) and BWChannel_CA= nominal channel space+ Foffset,high + Foffset,low, the different solution on SCS adoption for each CC may lead to:
  BWChannel_CA > CBW1+CBW2 if adopts the SCS defined in 5.3A.1 of TS 38.101
  The wanted signal may not be captured within the MBW if adopts the SCS defined in 5.4A.1 of TS 38.101
WF | type | CC1 | CC2 | Limit1 | BO1 | Limit2 | BO2
CP-OFDM | NC | 1RB105 | 1RB51 | SEM -13dBm/1% BWchannel_CA | 2.3 | SEM -24dBm/30kHz | 6.3
 |  | 1RB70 | 1RB35 |  | 5.9 | SEM -24dBm/30kHz | 6.9
 |  | 1RB85 | 1RB63 |  | 6.4 | SEM -24dBm/30kHz | 12.3

## Slide 3: ACLR MBW
  Option 1[1st round comment]:
    Offset for ACLR: ±BWchannel_CA
    MBW= BWchannel_CA -2*max(BWGB1, BWGB2). SCS adoption of each CC is defined as current 5.3A.3 of 38.101
    Channel space can be less or equal to nominal channel space to ensure BWchannel_CA not exceed CBW1+CBW2:
    *For simulation and measurement assumption, nominal channel space is used since no risk on BWChannel_CA > CBW1+CBW2 for 20M+20M, 50M+50M, 100M+60M and 100M+100M
  Option 2[1st round comment]:
    ACLR MBW=BWchannel_CA-2max(BWGB1, BWGB2), where BWchannel_CA= nominal channel space+ Foffset,high + Foffset,low. Do not use largest common µ for Foffset,high and Foffset,low. Largest common µ is only used for nominal channel spacing.
    Offset for ACLR: ± BWchannel_CA
    Note that BWCA for different numerology can exceed CBW1+CBW2.
  Option 3A[2]:
    ), use the largest common µ which is defined in 5.4A.1 of TS 38.101
    ACLR MBW=BWchannel_CA-2max(BWGB1, BWGB2), where BWchannel_CA= nominal channel space+ Foffset,high + Foffset,low. use largest common µ for Foffset,high and Foffset,low.

## Slide 4: SEM offset and measurement bandwidth
1. The MBW for ∆fOOB 0-1MHz
use 1% BWchannel_CA until 40MHz aggregated channel bandwidth, 400kHz thereafter, the equation is as below:
  -13 dBm/Min(0.01*BWchannel_CA, 0.4) [MHz]
2. The starting frequency point for OOB domain:
Option 1: ± BWchannel_CA/2 with the condition that BWchannel_CA less than or equal to CBW1+CBW2

## Slide 5: Foffset,high and Foffset,low
Align the Foffset,high and Foffset,low specified in TS 38.101 and TS 38.104
  In TS 38.104:
    Foffset,low = (NRB,low*12 + 1)*SCSlow/2 + BWGB (MHz)
    Foffset,high = (NRB,high*12 - 1)*SCShigh/2 + BWGB (MHz)
    BWGB, low and BWGB, high are the minimum guard band defined in subclause 5.3.3for lowest and highest assigned component carrier, while NRB,low and NRB,high are the transmission bandwidth configurations according to Table 5.3.2-1 or Table 5.3.2-2 for the lowest and highest assigned component carrier, SCSlow and SCShigh are the sub-carrier spacing for the lowest and highest assigned component carrier respectively.
  In TS 38.101:
    Foffset,low = (NRB,low*12 + 1)*SCSlow/2 + BWGB (MHz)
    Foffset,high = (NRB,high*12 - 1)*SCShigh/2 + BWGB (MHz)
    BWGB = max(BWGB,Channel(k))
How to align?
  Decide in the next RAN4 meeting

## Slide 6: Reference
[1] R4-1910273,”RF requirement of intra-band UL CA”, RAN4 #92, Huawei, HiSilicon
[2] R4-1912422 ,”RF requirement of intra-band contiguous UL CA”, RAN4 #92bis, Huawei, HiSilicon
[3] R4-2000712, “[NRULCA] Definition of Intra-band Contiguous UL CA Bandwidths”, RAN #94e, Skyworks
[4] R4-2001385, “Problems with CA channel arrangement”, RAN4 #94e, Nokia
[5] R4-2002691, “email discussion_#18_NR_RF_FR1_Part_1”, RAN4 #94e, Huawei, HiSilicon