## Slide 1: WF on MPE solutions
OPPO, [xxx]
3GPP TSG-RAN WG4 Meeting #94-e Draft R4-2002819
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: PMPR reporting: values
Five options have been provided in this meeting and merged into two options in RAN4#94e. Further down selection is needed between following two options and focus on the PMPR values that is needed to solve RLF issue.
  Option A: Range from 1dB to [20, 31]dB, with 5 bits (up to 32 values), 1dB step;
  Option B: Range from 1dB to [>10]dB, with 2 bits (4 values) like {1~3, 4~6, 7~9, >=10} or {1~5, 6~8, 9~11, >=12};
  Or Compromise between Option A and B e.g. as shown in the table:
1 | 1 dB
2 | 2 dB
3 | 3 dB
4 | 4 dB
5 | 5 dB
6 | 6 dB
7 | 7 dB
8 | 8 dB
9 | 9 dB
10 | 10 dB
11 | 11-13 dB
12 | 14-16 dB
13 | 17-20 dB
14 | 21-24 dB
15 | 25 - 29 dB
16 | 30 dB and above

## Slide 3: PMPR reporting: report before or after it is applied
No conclusions has been reached regarding PMPR shall be reported before or after it is applied. More clarification on following two questions are needed.
  If PMPR is reported before it is applied by UE, how to predict the PMPR value in future?
  If PMPR is reported after it is applied by UE, how to make sure NW can receive PMPR report if PMPR applied is large?
  If UE is allowed report PMPR before applying P-MPR but if needed for MPE compliance, UE can also apply P-MPR first and then send the report.
Next RAN4 meeting should decide these details as they are not needed for the RAN2 signaling and a LS is sent in this meeting to RAN2.

## Slide 4: PMPR reporting: Periodic or triggered report
Triggered reporting is agreed to be introduced.
  A prohibit timer configured by NW to trigger the PMPR reporting will be introduced.
  PMPR reporting threshold is a NW configurable value.
  Further down selection of PMPR reporting trigger condition between following two options is needed from solving RLF perspective
    Option A: P-MPR is higher than a configurable threshold
    Option B: P-MPR changes comparing to last report is higher than a configurable threshold
No conclusions has been reached on introducing periodic reporting. More clarifications about the additional benefits is needed.
  If periodic reporting is agreed to be introduced, then PHR reporting period can be reused, i.e. {sf10, sf20, sf50, sf100, sf200, sf500, sf1000, and infinity}.
  Further discussion on the proposal to include P-MPR reporting in the same MAC-CE as PHR and reuse/share same trigger conditions of PHR which are currently defined in TS 38.321 section 5.4.6 and include both Periodic and triggered report reporting.

## Slide 5: PMPR reporting: “fast emergency signal”
it is agreed that “fast emergency signal” is not needed
No conclusion has been reached during RAN4#94e meeting, and approximately 4 certain companies support a fast emergency signal needs to be sent before PMPR reporting, while 10 other companies think only PMPR reported is enough and does not support “fast emergency signal”.
Further clarification is needed on the necessity of introducing “fast emergency signal” in addition to PMPR reporting, and also the relation between them or if fast P-MPR based event-triggered reporting can act as fast emergency signaling.
  If PMPR is reported before it is applied by UE, it is agreed that “fast emergency signal” is not needed
  If PMPR is reported after it is applied by UE, further discussion is needed
  Can fast P-MPR based event-triggered reporting work as fast emergency signaling?

## Slide 6: Dynamic duty cycle
No conclusion has been reached in RAN4#94e meeting. The benefit of dynamic duty cycle from improving UE performance and helping gNB scheduling perspective needs to be further discussed.
  If dynamic duty cycle is agreed to be introduced, the dynamic duty cycle calculation reference power is 0 dB PHR.
  If dynamic duty cycle triggered report is agreed to be introduced, the trigger condition shall be x% change in dynamic duty cycle capability, where x% is FFS.
  If dynamic duty cycle periodic report is agreed to be introduced, applicability period is the periodicity of the report.

## Slide 7: P bit in single entry PHR
Inform RAN2 about the misalignment in P-bit between single entry PHR and multi-entry PHR, and it depends on RAN2 to discuss how to cope with it.

## Slide 8: Energy Headroom Report (EHR)
Energy Headroom Report (EHR) will not be introduced

## Slide 9: Reference PCMAX
Different understanding on the definition of “reference PCMAX” is observed, no consensus has been reached. Alignment on the definition is needed. Then further discuss the necessity of introducing “reference PCMAX” UE capability.
  “Reference PCMAX” proposed in R4-2001781 does not mean real time actual PCMAX that UE used to calculate PHR, instead it means the PCMAX without considering any MPR, AMPR and PMPR which is a static value reported as UE capability in initial access.

## Slide 10: UE behavior after the network change (reduction) of the scheduled UL duty cycle
Make It is a common understanding that the P-MPR applied by UE is expected to be reduced when the UL duty cycle scheduled by NW is reduced and all other conditions are unchanged.
There is no consensus on whether UE shall reduce PMPR and whether the above common understanding is appropriate to be specified in the spec.