TSG-RAN Working Group 4 (Radio) #94-e	R4-2002821

Online, 24th February – 6th March 2020

Title:	[Draft] LS on MPE enhancements

Response to:

Release:	Rel-16

Work Item:	NR_RF_FR2_req_enh

Source:	Nokia, Nokia Shanghai Bell [to be RAN4]

To:	RAN2

Cc:

Contact Person:

Name: Petri Vasenkari

E-mail Address: petri.j.vasenkari@nokia.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

RAN4 has agreed further details on Rel-16 FR2 MPE enhancement solutions to mitigate RLF due to sudden and unpredictable large back off caused UE’s actions to ensure compliance with exposure regulation.

RAN4 would like to ask RAN2 to develop the following Rel-16 FR2 MPE signalling based on MAC-CE to ensure sufficiently short signalling delays:

- P-MPR reporting is assumed to be in the same MAC-CE as PHR.

- at least UE’s P-MPR based event-triggered reporting including also reporting of the actual P-MPR level that UE needs for FR2 MPE reasons.

- Network configurable P-MPR reporting threshold (e.g. P-MPR or changes of PMPR comparing to latest report is higher than a configurable P-MPR based threshold)

- A prohibit timer is enabled to be configured by network to trigger the P-MPR reporting

- P-MPR reporting ranges is still under discussion

2. Actions:

To RAN WG2 group.

ACTION: 	RAN4 asks RAN2 group to define Rel-16 MPE signalling based on the above-mentioned information.

3. Date of Next RAN4 Meetings:

3GPP RAN 4 RAN4#94-Bis	20th – 24th April 2020		e-meeting

3GPP RAN 4 RAN4#95		25th – 29thMay 2020		Athens, Greece