TSG-RAN Working Group 4 (Radio) #94-e	R4-20xxxxx

Online, 24th February – 6th March 2020

Title:	[Draft] LS on P bit in single entry PHR

Response to:

Release:	Rel-16

Work Item:	NR_RF_FR2_req_enh

Source:	RAN4

To:	RAN2

Cc:

Contact Person:

Name: Jinqiang Xing

E-mail Address: xingjinqiang@oppo.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

During the discussion of PMPR reporting in FR2 MPE enhancements, companies in RAN4 found there is inconsistency between single entry PHR MAC CE and multiple entry PHR MAC CE regarding “P bit” as can be seen in Figure 6.1.3.8-1 and Figure 6.1.3.9-1 below reproduced from TS38.321. The “P bit” exists in multiple entry PHR MAC CE, but in-exist in single entry PHR MAC CE.

RAN4 feels this might be an overlook in RAN2 specification and would like to inform RAN2 about this inconsistency. It is up to RAN2 to decide whether the introduction of “P bit” in single entry PHR MAC CE is necessary or not. No impact to RAN4 specification has been observed up to now.

- P: This field indicates whether the MAC entity applies power backoff due to power management (as allowed by P-MPRc as specified in TS 38.101-1 [14], TS 38.101-2 [15], and TS 38.101-3 [16]). The MAC entity shall set the P field to 1 if the corresponding PCMAX,f,c field would have had a different value if no power backoff due to power management had been applied;

Figure 6.1.3.8-1: Single Entry PHR MAC CE

Figure 6.1.3.9-1: Multiple Entry PHR MAC CE with the highest ServCellIndex of Serving Cell with configured uplink is less than 8

2. Actions:

To RAN WG2 group.

ACTION: 	RAN4 kindly ask RAN2 to take above information into consideration.

3. Date of Next RAN4 Meetings:

3GPP RAN 4 RAN4#94-Bis	20th – 24th April 2020		Canada

3GPP RAN 4 RAN4#95		25th – 29thMay 2020		Athens, Greece