## Slide 1: WF on remaining issues with Rel-16 beam correspondence
Apple Inc.
3GPP TSG-RAN WG4 Meeting #94-e R4-2002822 Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
The following contributions on the topic of beam correspondence in Rel-16 were discussed:
Ref | tdoc | source | title
[1] | R4-2000012 | Apple Inc. | Remaining issues with beam correspondence in Rel-16
[2] | R4-2000077 | Qualcomm Incorporated | FR2 Beam Correspondence using SSB only
[3] | R4-2000078 | Qualcomm Incorporated | Beam management CSI-RS design for BC requirement
[4] | R4-2000079 | Qualcomm Incorporated | Further enhancement of Beam Correspondence
[5] | R4-2000199 | Qualcomm Incorporated | On FR2 Initial access beam correspondence
[6] | R4-2000271 | Samsung | Discussion on beam correspondence in Rel-16
[7] | R4-2000394 | Intel Corporation | SSB based Beam Correspondence
[8] | R4-2000791 | Apple Inc. | On SSB based beam correspondence requirements
[9] | R4-2000858 | NTT DOCOMO, INC. | Views on beam correspondence enhancement based on SSB in Rel-16
[10] | R4-2001065 | Fraunhofer HHI | On the effect of beamforming with CA on beam correspondence
[11] | R4-2001199 | LG Electronics | Enhanced beam correspondence in rel-16 at FR2
[12] | R4-2001232 | OPPO | Environmental condition based beam correspondence enhancement
[13] | R4-2001325 | Ericsson, Sony | Test configuration and requirements for beam correspondence during initital access
[14] | R4-2001384 | Nokia, Nokia Shanghai Bell | FR2 Beam Correspondence enhancements
[15] | R4-2001490 | Sony, Ericsson | Views on SSB only and CSI-RS only beam correspondence
[16] | R4-2001493 | Sony | Enhanced reporting for beam correspondence in poor SNR condition
[17] | R4-2001761 | Huawei, HiSilicon | On beam correspondence requirement in Rel-16
[18] | R4-2001777 | Huawei, HiSilicon | TP for TR 38.831: beam correspondence based on CSI-RS only
[19] | R4-2002694 | Moderator | Email discussion summary for RAN4#94e_#21_NR_RF_FR2_req_enh_Part_2

## Slide 3: Topic 1: Beam correspondence based on SSB
Whether a BC based on SSB requirement is feasible
  Alt 1-1: Yes
  Alt 1-2: Yes, with the assumption that TRS can be configured and used for beam refinement
    See additional tracking CSI-RS configuration proposal in [7]
  Alt 1-3: Yes, with performance relaxation relative to the condition which assumes both SSB and CSI-RS are present
    Alt 1-3-1: 0 < ∆p ≤ 3 dB
    Alt 1-3-2: 3 < ∆p ≤ 5 dB
  Alt 1-4: Yes, with metric other than MOP
    Metric details are FFS
  Alt 1-5: No
    Not feasible to keep the existing performance and realistic UE operating scenarios
Side conditions
  SSB min SNR level = 6 dB
  P3 CSI-RS configuration is not used
  Tracking CSI-RS min SNR = 6 dB
Way forward: continue discussion of open issues until the next meeting

## Slide 4: Topic 2: Beam correspondence based on CSI-RS
Before agreeing to a “CSI-RS only” test (configuration), RAN4 should identify the deployment scenario that this test is going to verify.
“CSI-only” condition is necessary for RAN4 to specify requirements and test configuration for BC based on CSI-RS.
Based on the outcome of the discussion above, the method to achieve “CSI-RS only” condition:
  Alt 2-1: SSB and CSI-RS are present, but SSB’s PSD is backed-off by X dB from CSI-RS
  Alt 2-2: decrease SSB power until UE SSB based SS-SINR measurement reporting is within the threshold ≤ -3dB
  Alt 2-3: P1 CSI-RS is transmitted and the QCL relation is configured as ‘none’
  Alt 2-3: before agreeing a “CSI-RS only” test (configuration), RAN4 should identify the deployment scenario that this test is going to verify
Side conditions
  P1 CSI-RS is configured, the QCL (qcl-TypeD) relation is configured as ‘SSBnone’
    Periodicity is TBD msSlot80(120kHz)
  P2 CSI-RS is not configured
  P3 CSI-RS configuration
    maxNumberRxBeam in UE capability IE of MIMO-ParametersPerBand repetitions per resource set
    QCL Type C to SSB and Type D to SSBP1 CSI-RS
Way forward: continue discussion of open issues until the next meeting

## Slide 5: Topic 3: Initial access beam correspondence
Whether RAN4 shall introduce a requirement on initial access beam correspondence
  Alt 3-1: Yes
  Alt 3-2: No
  Alt 3-3: Verify a related “BC property”
Proposed solutions are FFS and pending agreement on the feasibility of the requirement
Way forward: continue discussion of open issues until the next meeting

## Slide 6: Topic 4: Additional beam correspondence enhancements
Feasibility of utilizing the existing UE measurement including RSRP and/or L1-SINR
  Alt 4-1-1: Proposed enhancement is feasible for Rel-16
  Alt 4-1-2: Proposed enhancement is not feasible for Rel-16
Feasibility of CA impact
  Study ‘beam squint’ impact, other factors of impact are precluded
  Alt 4-2-1: Proposed enhancement is feasible for Rel-16
  Alt 4-2-2: Relaxations can be rolled into existing requirements, such MPR/REFSENS in Rel-16
  Alt 4-2-3: Proposed enhancement is not feasible for Rel-16, and eBC shall not be specified for inter-band CA or intra-band NC CA
UL beam sweeping request indication
  Alt 4-3-1: Proposed enhancement is feasible for Rel-16
  Alt 4-3-2: Proposed enhancement is not feasible for Rel-16
Way forward: continue discussion of open issues until the next meeting

## Slide 7: Topic 5: Beam correspondence capability aspects
The following open issues are recommended for further discussion until the next meeting:
  Whether the Rel-15 UE bit0/bit1 BC capability is applicable to Rel-16 enhancements
  Whether a new capability for Rel-16 enhanced beam correspondence is needed
  Test applicability rule