## Slide 1: WF on multiband relaxation framework
SONY
3GPP TSG-RAN WG4 Meeting #94-Electronic Meeting,
Feb.24th – Mar.6th 2020
Draft R4-2002828

## Slide 2: Background
To resolve the issues of multiband requirement in FR2 which is raised from RAN5 (R5-199424), RAN4 has discussed the following issues during the email discussion of RAN4#94-e :
  If multiband requirement framework needs some enhancements how to do those
  If multiband requirement framework needs some enhancements

## Slide 3: Way forward
  RAN4 agrees to make modifications to multiband relaxation framework
  The modifications to multiband relaxation framework is valid from Rel-15.
  The modifications to multiband relaxation framework:
    Open issue 1: Whether to keep the current format of multiband requirement in TS38.101-2 (summation of total relaxation)
      Option 1: Keep the current format and introduce additional maximum cap to the per-band relaxation.
      Option 2: Replace multiband relaxation framework to per-band relaxation.
    Open issue 2: Rel-15 and Rel-16 adoption
      Option 1: Adopt option 1 for Rel-15, and adopt option 1 from Rel-16.
      Option 2: Adopt option 1 for Rel-15, and adopt option 2 from Rel-16.
      Option 3: Adopt option 2 for Rel-15, and adopt option 2 from Rel-16.
    Open issue 3: The values for the selected relaxation framework(s) in open issue 1 (, respectively)
      Option 1: Define the values as in R4-2000022: ∆MBP,n ≤ 0.75 dB and ∆MBS,n ≤ 0.75 dB.
      Option 2: Define the values as in R4-2000200 (table below). Relaxation is same no matter what band combinations UE supports, with the exceptions listed in notes.
      Option 3: Other values are not precluded.
  RAN4 continue discussion of open issues in the next meeting
Band | DMBP (dB) | DMBS (dB)
n257 | 0.73 | 0.73
n258 | 0.6 | 0.7
n260 | 0.51 | 0.41
n261 | 0.52,4 | 0.74
Note 1: n260 peak and spherical relaxations are 0 dB for UE that exclusively supports n261+n260 Note 2: n261 peak relaxation is 0 dB for UE that exclusively supports n261+n260 Note 3: n257 peak and spherical relaxations are 0 dB for UE that exclusively supports n261+n257 Note 4: n261 peak and spherical relaxations are 0 dB for UE that exclusively supports n261+n257 |  | 

## Slide 4: Reference
R4-2002695 Email discussion summary for RAN4#94e_#23_NR_RF_FR2_req_enh_Part_4, Nokia