## Slide 1: WF on multiband relaxation framework
SONY
3GPP TSG-RAN WG4 Meeting #94-Electronic Meeting,
Feb.24th – Mar.6th 2020
Draft R4-2002828

## Slide 2: Background
To resolve the issues of multiband requirement in FR2 which is raised from RAN5 (R5-199424), RAN4 has discussed the following issues during the email discussion of RAN4#94-e :
  If multiband requirement framework needs some enhancements how to do those
  If multiband requirement framework needs some enhancements

## Slide 3: Way forward
  RAN4 agrees to make modifications to multiband relaxation framework
  The modifications to multiband relaxation framework is valid from Rel-15.
  The modifications to multiband relaxation framework:
    Open issue 1: Whether to keep the current format of multiband requirement in TS38.101-2 (summation of total relaxation)
      Option 1: Keep the current format and introduce additional maximum cap to the per-band relaxation.
      Option 2: Replace multiband relaxation framework to per-band relaxation.
    Open issue 2: Rel-15 and Rel-16 adoption
      Option 1: Adopt option 1 for Rel-15, and adopt option 1 from Rel-16.
      Option 2: Adopt option 1 for Rel-15, and adopt option 2 from Rel-16.
      Option 3: Adopt option 2 for Rel-15, and adopt option 2 from Rel-16.
    Open issue 3: The values for the selected relaxation framework(s) in open issue 1 (, respectively)
      Option 1: Define the values as in R4-2000022: ∆MBP,n ≤ 0.75 dB and ∆MBS,n ≤ 0.75 dB.
      Option 2: Define the values as in R4-2000200 (table below). Relaxation is same no matter what band combinations UE supports, with the exceptions listed in notes.
      Option 3: Other values are not precluded.
  RAN4 continue discussion of open issues in the next meeting
  MBR values for band n259 will also be discussed and agreed in the next meeting.
Band | DMBP (dB) | DMBS (dB)
n257 | 0.73 | 0.73
n258 | 0.6 | 0.7
n260 | 0.51 | 0.41
n261 | 0.52,4 | 0.74
Note 1: n260 peak and spherical relaxations are 0 dB for UE that exclusively supports n261+n260 Note 2: n261 peak relaxation is 0 dB for UE that exclusively supports n261+n260 Note 3: n257 peak and spherical relaxations are 0 dB for UE that exclusively supports n261+n257 Note 4: n261 peak and spherical relaxations are 0 dB for UE that exclusively supports n261+n257 |  | 

## Slide 4: Reference
R4-2002695 Email discussion summary for RAN4#94e_#23_NR_RF_FR2_req_enh_Part_4, Nokia