## Slide 1: WF on radiative degradation mechanisms for larger frequency separation
Qualcomm, …
R4-2002826
3GPP TSG-RAN WG4 Meeting #94-e
Online Meeting, 24 Feb-6 Mar 2019
Agenda: 8.14.1.6
Email Thread: #23

## Slide 2: Background
Beam squint happens when DL BM reference signals and UL/DL control and/or data channels of interest are not within the same CC, see figure on right
Beam squint causes a received signal to have a frequency selective characteristic
  It is a radiative-domain impairment
  It causes gain droop, like impairment caused by active circuitry in the conducted domain
Factors that can cause beam squint to become significant (see R4-2002147):
  Practical FR2 devices that may use analog beam forming
  Signal has wide fractional BW (for example: = aggregated channel BW/ center frequency)
  High–directivity beams (higher directivity beams may suffer more degradation)
  Practical implementation constraints
Difference in antenna gain, ‘x’ dB
gNB
UE
Conducted power in transmitted CCs
Ref signal for BM
Blue CC squints away from target direction due to separation in frequency from reference signal
Power received OTA
‘x’ dB

## Slide 3: WF on Beam Squint Analysis
For any FR2 UE power class of interest, companies are encouraged to:
  Share estimated impact to RF performance. Some examples:
    CA EIRP
    CA Refsens
    Impact of closed loop power control on MPR
  Identify how to capture in standard
    Preserve backward compatibility with Rel-15
    Identify sub-sections that may be affected
    Identify parameters or methods to quantify effect, including dependencies.
      For example of dependency, in intra-band CA case: frequency separation
    Side conditions, like location of beam-management reference signals in relation to CA configuration