3GPP TSG-RAN WG4 #94-e	R4-2002603

Online, 24th February – 6th March 2020

Source:	Huawei, HiSilicon

Title:	TP for TR 37.716-11-11 DC_20A_n41A

Agenda item:			9.3.2

Document for:	Approval

# 1. Introduction

In this contribution, we propose a text proposal for TR 37.716-11-11 to finish DC_20A_n41A.

# 2. Text Proposal

----- Unchanged sections omitted -----

### 6.1.21	DC_20_n41

#### 6.1.21.1	Operating bands for DC

Table 6.1.21.1-1: DC band combination of 1 LTE band + 1 NR band

| EN-DC band | E-UTRA Band | NR Band | Single UL allowed |
| --- | --- | --- | --- |
| DC_20_n41 | 20 | n41 | DC_20A_n41A |

#### 6.1.21.2	Configuration for DC

Table 6.1.21.2-1:  Inter-band EN-DC configurations of 1 LTE band + 1 NR band

| EN-DC configuration | Uplink EN-DC configuration (NOTE 1) | E-UTRA configuration | NR configuration |
| --- | --- | --- | --- |
| DC_20A_n41A | DC_20A_n41A | 20A | n41A |

#### 6.1.21.3	Maximum output power for DC

Table 6.1.21.3-1: Maximum output power for inter-band EN-DC of 1 LTE band + 1 NR band

| DC configuration | Power class 3 (dBm) | Tolerance (dB) |
| --- | --- | --- |
| DC_20A_n41A | 23 | +2/-3 |

#### 6.1.21.4	Spurious emission band UE co-existence for DC

Table 6.1.21.4-1: Spurious emissions for inter-band EN-DC of 1 LTE band + 1 NR band

| E-UTRA and NR DC Configuration | Spurious emission |
| --- | --- |
|  | Protected band | Frequency range (MHz) | Maximum Level (dBm) | MBW (MHz) | NOTE |
| DC_20A_n41A | E-UTRA Band 1, 2, 4, 10, 24, 25, 30, 31, 32, 33, 34, 39, 40, 43, 48, 50, 51, 65, 66, 70, 72, 73, 74, 75, 76 | FDL_low | - | FDL_high | -50 | 1 |  |
|  | E-UTRA Band 3, 8, 12, 13, 14, 17, 38, 42, 44, 45, 52, 67, 68, 69, 71, 85 NR Band n77, n78, n79 | FDL_low | - | FDL_high | -50 | 1 | 2 |
|  | Frequency range | 758 | - | 788 | -50 | 1 |  |
|  | E-UTRA Band 9, 11, 21 | FDL_low | - | FDL_high | -50 | 1 | 30 |
|  | Frequency range | 1884.5 | - | 1915.7 | -41 | 0.3 | 8, 30 |
| NOTE 2: As exceptions, measurements with a level up to the applicable requirements defined in Table 6.6.3.1-2 are permitted for each assigned carrier used in the measurement due to 2nd, 3rd, 4th or 5th harmonic spurious emissions. Due to spreading of the harmonic emission the exception is also allowed for the first 1 MHz frequency range immediately outside the harmonic emission on both sides of the harmonic emission. This results in an overall exception interval centred at the harmonic emission of (2MHz + N x LCRB x 180kHz), where N is 2, 3, 4, 5 for the 2nd, 3rd, 4th or 5th harmonic respectively. The exception is allowed if the measurement bandwidth (MBW) totally or partially overlaps the overall exception interval. NOTE 8: Applicable when co-existence with PHS system operating in 1884.5 -1915.7MHz. NOTE 15: These requirements also apply for the frequency ranges that are less than FOOB (MHz) in Table 6.6.3.1-1 and Table 6.6A.3.1-1 from the edge of the channel bandwidth. NOTE 30: This requirement applies when the carrier is confined within 2545-2575MHz or 2595-2645MHz and the channel bandwidth is 10 or 20 MHz |

#### 6.1.21.5	MSD analysis for DC

For 2UL/2DL UE coexistence study 2nd, 3rd, 4th and 5th order harmonics and 2nd, 3rd, 4th and 5th order intermodulation products were calculated and presented in Table 6.1.21.5-1

Table 6.1.21.5-1: Harmonic and IMD analysis

| UE UL carriers | fx_low | fx_high | fy_low | fy_high |
| --- | --- | --- | --- | --- |
| UL frequency (MHz) | 832 | 862 | 2496 | 2690 |
| 2nd harmonics frequency limits | 2*fx_low | 2*fx_high | 2* fy_low | 2* fy_high |
| 2nd harmonics frequency limits (MHz) | 1664 | 1724 | 4992 | 5380 |
| 3rd harmonics frequency limits | 3*fx_low | 3*fx_high | 3* fy_low | 3* fy_high |
| 3rd harmonics frequency limits (MHz) | 2496 | 2586 | 7488 | 8070 |
| UL | f1_low | f1_high | f2_low | f2_high |
|  | 832 | 862 | 2496 | 2690 |
| DL | f1_low | f1_high | f2_low | f2_high |
|  | 791 | 821 | 2496 | 2690 |
| Two tone 2nd order IMD products | (fx_low – fy_high) | (fx_high – fy_low) | (fx_low + fy_low) | (fx_high + fy_high) |
| IMD frequency limits (MHz) | 1634 | 1858 | 3328 | 3552 |
| Two-tone 3rd order IMD products | ¦2*fx_low – fy_high¦ | ¦2*fx_high – fy_low¦ | (2*fx_low – fy_high) | (2*fx_high – fy_low) |
| IMD frequency limits (MHz) | 772 | 1026 | 4130 | 4548 |
| Two-tone 3rd order IMD products | (2*fx_low + fy_low) | (2*fx_high + fy_high) | (2*fx_low + fy_low) | (2*fx_high + fy_high) |
| IMD frequency limits (MHz) | 4160 | 4414 | 5824 | 6242 |
| 3rd order IMD products | (fx_low – fy_high + fy_low) | (fx_high + fy_high – fy_low) | (fy_low – fx_high + fx_low) | (fy_high + fx_high – fx_low) |
|  | 638 | 1056 | 2466 | 2720 |
| Two-tone 3rd order IMD products | (fx_low – max BW fy) | (fx_high + max BW fy) | (fy_low – max BW fx) | (fy_high + max BW fx) |
| IMD frequency limits (MHz) | 752 | 942 | 2476 | 2710 |
| Two-tone 4th order IMD products | ¦3*fx_low – fy_high¦ | ¦3*fx_high – fy_low¦ | (3*fy_low – fx_high) | (3*fy_high – fx_low) |
| IMD frequency limits (MHz) | 194 | 90 | 6626 | 7238 |
| Two-tone 4th order IMD products | (2*fy_low – 2*fx_high) | (2*fy_high – 2*fx_low) |  |  |
| IMD frequency limits (MHz) | 3268 | 3716 |  |  |
| Two-tone 4th order IMD products | (3*fx_low + fy_low) | (3*fx_high + fy_high) | (3*fy_low + fx_low ) | (3*fy_high +fx_high) |
| IMD frequency limits (MHz) | 4992 | 5276 | 8320 | 8932 |
| Two-tone 4th order IMD products | (2*fx_low + 2*fy_low) | (2*fx_high + 2*fy_high) |  |  |
| IMD frequency limits (MHz) | 6656 | 7104 |  |  |
| Two-tone 5th order IMD products | (4*fy_low – fx_high) | (4*fy_high – fx_low) | ¦4*fx_low – fy_high¦ | ¦4*fx_high – fy_low¦ |
| IMD frequency limits (MHz) | 9122 | 9928 | 638 | 952 |
| Two-tone 5th order IMD products | (3* fy_low-2*fx_high ) | (3*fy_high-2*fx_low) | ¦2*fy_low –3* fx_high¦ | ¦2*fy_high – 3*fx_low¦ |
| IMD frequency limits (MHz) | 5764 | 6406 | 2406 | 2884 |
| Two-tone 5th order IMD products | (4*fy_low + fx_low ) | (4*fy_high +fx_high) | (4*fx_low + fy_low) | (4*fx_high + fy_high) |
| IMD frequency limits (MHz) | 10816 | 11622 | 5824 | 6138 |
| Two-tone 5th order IMD products | (3*fy_low + 2*fx_low ) | (3*fy_high +2*fx_high) | (3*fx_low +2* fy_low) | (3*fx_high + 2*fy_high) |
| IMD frequency limits (MHz) | 9152 | 9794 | 7488 | 7966 |

Based on the table 6.1.21.5-1:

- 2nd order harmonic products may also fall into Rx frequencies of bands 46, n79

- 3nd order harmonic products may also fall into Rx frequencies of bands 38/n38, 41/n41, 69

- 2nd IMD products may also fall into Rx frequencies of bands 3/n3, 9, 22, 35, 42, n77, n78

- 3rd IMD products may also fall into Rx frequencies of bands 5/n5, 6, 7/n7, 8/n8, 12/n12, 13, 14, 17, 18, 19, 20/n20, 22, 26, 27, 28/n28, 29, 38/n38, 41/n41, 44, 45, 67, 68, 69, 71/n71, n77, n79, 85

- 4th IMD products may also fall into Rx frequencies of bands 42, 43, 45, n77, n78, n79

- 5th IMD products may also fall into Rx frequencies of bands 5/n5, 6, 7/n7, 8/n8, 12/n12, 13, 14, 17, 18, 19, 20/n20, 26, 27, 28/n28, 29, 38/n38, 41/n41, 44, 45, 67, 68, 69, 71/n71, 85

The 3nd order harmonic products may make interference in a part of the band n41 (2496-2586MHz). But, in a lot of cases there will be not interference because the 2nd order harmonic products can be outside the carrier (including guard bands) used in band n41. In very specific cases and if the 3nd order harmonic products by the carrier in band 20 is in the carrier in band n41, the single UL (SUO) in band n41 could be used to resolve this interference, and/or, two Tx antennas. Thus, future studies are needed.

Tables below list the MSD required for the dual connectivity configuration due to IMD 3 and 5.

Table 6.1.21.5-2: Reference sensitivity exceptions due to dual uplink operation for EN-DC in NR FR1 (two bands)

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA or NR band | UL Fc (MHz) | UL/DL BW (MHz) | UL LCRB | DL Fc (MHz) | MSD (dB) | Duplex mode | IMD order | Single UL allowed |
| DC_20_n41 | 20 | 851 | 5 | 25 | 810 | 12.1dB | FDD | IMD 3 | Yes |
|  | n41 | 2512 | 10 | 50 | 2512 | N/A | TDD | N/A |  |
| DC_20_n41 | 20 | 841 | 5 | 25 | 800 | 8.1dB | FDD | IMD 5 | Yes |
|  | n41 | 2564 | 10 | 50 | 2564 | N/A | TDD | N/A |  |

#### 6.1.21.6	∆TIB and ∆RIB values

For DC_20_n41, the (TIB,c and (RIB,c values are given in the tables below.

Table 6.1.21.6-1: ΔTIB,c

| Inter-band DC Configuration | E-UTRA and NR Band | ΔTIB,c [dB] |
| --- | --- | --- |
| DC_20_n41 | 20 | 0.3 |
|  | n41 | 0.3 |

Table 6.1.21.6-2: ΔRIB,c

| Inter-band DC Configuration | E-UTRA and NR Band | ΔRIB [dB] |
| --- | --- | --- |
| DC_20_n41 | 20 | 0 |
|  | n41 | 0 |

#### 6.1.21.7		Self-interference analysis

This section provides the formulation to determine whether the DL carriers would be impacted by UL harmonics, 2UL inter-modulation products (IMD), or DL harmonic mixing with UL interferer based on UL and DL channel combinations. The potential self-interference mechanism has been identified in section 6.1.21.5 except for harmonic mixing and UL harmonic order higher than 5 which are used to generate an interference mixing coefficient table for this DC combination, as shown in Table 6.1.21.7-1.

Table 6.1.21.7-1: Band 20 and Band n41 interference mixing coefficients

| EUTRA-NR DC Configuration | EUTRA/NR Band | UL Coefficient | DL Coefficient | Harmonic/IMD Order | Victim Band | Interference Type |
| --- | --- | --- | --- | --- | --- | --- |
| DC_20A_n41A | 20 | a | 3 | b | 0 | 3 | n41 | Harmonic |
|  | n41 | c | 0 | d | -1 |  |  |  |
| DC_20A_n41A | 20 | a | -2 | b | -1 | 3 | 20 | IMD |
|  | n41 | c | 1 | d | 0 |  |  |  |
| DC_20A_n41A | 20 | a | 4 | b | -1 | 5 | 20 | IMD |
|  | n41 | c | -1 | d | 0 |  |  |  |

Equations (1) and (2) below are used to calculate the interference center frequency (fINT) and its effective bandwidth (BWINT) where coefficients a, b, c, and d are defined in Table 6.1.21.7-1 and CBW stands for channel bandwidth.

(1)

(2)

Formula (3-1) and (3-2) below are then used to indicate when the interference is overlapping with RX1 and RX2, respectively.

(3-1)

(3-2)

----- Unchanged sections omitted -----

# Reference