3GPP TSG-RAN WG4 Meeting #94-e	R4-200

Online, 24 Feb. – 6 Mar., 2020

Source: 	Huawei, HiSilicon

Title: 	TP for TR 37.716-21-21:DC_2A_n7A-n78A

Agenda Item:	9.7.2

Document for:	Approval

# Introduction

The WID for NR DC was updated in RAN #86 meeting. This contribution provides a TP for TR 37.716-21-21 to finish the UE RF requirements for the band combination.

# Discussion

Based on co-existence study, own Rx impact of the 3rd band is shown as the followings.

-	5th order IMD of DC_2A_n7 UL will fall into Rx of bands n78

We use the Diplexer-quadplexer based RF front-end architecture to analyze the amount of IMD using the following component linearity assumptions:

Table 2-3 General linearity parameters

| Component | IP5 (dBm) |
| --- | --- |
| Antenna switch | 53 |
| Diplexer | 53 |
| Quadplexer | 53 |
| PA forward mixing | 28 |
| PA reverse mixing | 30 |
| LNA | -10 |

Table 2-4 Attenuation and isolation

| Parameters | Values (dB) |
| --- | --- |
| Antenna isolation | 10 |
| PCB isolation PA-PA | 60 |
| Diplexer isolation | 15 |
| Tx duplexer rejection at Rx Band | 50 |

Based on these parameters we get the following MSD.

| DC bands | UL DC | IMD | UL Fc (MHz) | UL BW (MHz) | UL RB # | DL Fc (MHz) | MSD (dB) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DC_2A_n7A-n78A | 2 | IMD5 | ¦2*fB2 -3*fn7¦ | 1900 | 5 | 25 | 1980 | N/A |
|  | n7 |  |  | 2525 | 5 | 25 | 2645 | N/A |
|  | n78 |  |  | 3775 | 10 | 50 | 3775 | 4.5 |

In R4-2001130 it is proposed 3.9 dB MSD for the combination. The average value 4.2 dB is adopted in the TP.

# References

[1]	RP-191744, “Revised WID on EN-DC of x bands (x=1,2,3,4) LTE  and NR 2 bands”, LG Electronics

# Text Proposal

<TP for TR 37.716-21-21>

## 6.x	DC_2_n7-n78

### 6.x.1	Operating bands for DC

Table 6.x.1-1: DC band combination of one LTE band + NR 2DL/1UL

| E-UTRA and NR DC Band | E-UTRA and NR Band | Uplink (UL) band | Downlink (DL) band | Duplex mode |
| --- | --- | --- | --- | --- |
|  |  | BS receive / UE transmit | BS transmit / UE receive |  |
|  |  | FUL_low – FUL_high | FDL_low – FDL_high |  |
| DC_2_n7-n78 | 2 | 1850 MHz | – | 1910 MHz | 1930 MHz | – | 1990 MHz | FDD |
|  | n7 | 2500 MHz | – | 2570 MHz | 2620 MHz | – | 2690 MHz | FDD |
|  | n78 | 3300 MHz | – | 3800 MHz | 3300 MHz | – | 3800 MHz | TDD |

### 6.x.2	Channel bandwidths per operating band for DC

Table 6.x.2-1: Supported bandwidths per DC band combination of one LTE band + NR 2DL/1UL

| E-UTRA and NR DC Configuration | UL Configuration | NR Band | SCS [kHz] | 5 | 10 | 15 | 20 | 40 | 50 | 60 | 80 | 90 | 100 | Max BW [MHz] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DC_2A_n7A-n78A | DC_2A_n7A DC_2A_n78A | 2 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  | 160 |
|  |  | n7 | 15 | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  |  |
|  |  |  | 30 |  | Yes | Yes | Yes | Yes |  |  |  |  |  |  |
|  |  |  | 60 |  | Yes | Yes | Yes | Yes |  |  |  |  |  |  |
|  |  | n78 | 30 |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  |
|  |  |  | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |
|  |  |  | 120 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |

### 6.x.3	Co-existence studies

Based on Table 5.3-1 in TR 37.716-21-21 [2], there is a MSD issue for the following cases.

-	5th order IMD of DC_2A_n7 UL will fall into Rx of bands n78

### 6.x.4	∆TIB and ∆RIB values

For DC_2_n7-n78, the (TIB,c and (RIB values are given in the tables below.

Table 6.x.4-1: ΔTIB,c

| Inter-band DC Configuration | E-UTRA and NR Band | ΔTIB,c [dB] |
| --- | --- | --- |
| DC_2_n7-n78 | 2 | 0.6 |
|  | n7 | 0.5 |
|  | n78 | 0.8 |

Table 6.x.4-2: ΔRIB

| Inter-band DC Configuration | E-UTRA and NR Band | ΔRIB [dB] |
| --- | --- | --- |
| DC_2_n7-n78 | 2 | 0.2 |
|  | n7 | 0.5 |
|  | n78 | 0.5 |

### 6.x.5	MSD

Based on Table 5.3-1 in TR 37.716-21-21 [2], there is IMD5 products produced by Band 2 and n7 that impact the reference sensitivity of NR band n78.

The required MSD levels from interested companies are provided in Table 6.x.5-1. Based on the MSD levels, RAN4 will specify the MSD exception requirements as shown in the following Table 6.x.5-2.

Table 6.x.5-1: Proposed MSD levels from interested companies for EN-DC_2A_n7A-n78A

| DC bands | UL DC | IMD | HW (R4-200846) | LG (R4-2001130) | MSD (dB) |
| --- | --- | --- | --- | --- | --- |
| DC_2A_n7A-n78A | 2 | IMD5 | ¦2*fB2 -3*fn7¦ | 4.5 | 3.9 | 4.2 |
|  | n7 |  |  |  |  |  |
|  | n78 |  |  |  |  |  |

Table 6.x.5-2: MSD exception for Scell due to dual uplink operation for EN-DC_2A_n7A-n78A

| DC bands | UL DC | IMD | UL Fc (MHz) | UL BW (MHz) | UL RB # | DL Fc (MHz) | MSD (dB) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DC_2A_n7A-n78A | 2 | IMD5 | ¦2*fB2 -3*fn7¦ | 1900 | 5 | 25 | 1980 | N/A |
|  | n7 |  |  | 2525 | 5 | 25 | 2645 | N/A |
|  | n78 |  |  | 3775 | 10 | 50 | 3775 | 4.2 |

## <End of TP >