## Slide 1: Way Forward on PC 1.5 behavior when P-Max is not present
KDDI, [Sprint, CMCC, Softbank, Huawei, Intel, OPPO, …]
3GPP TSG-RAN WG4 Meeting #94-e R4-2002833
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
Default power class issue when P-Max is not present for 29dBm UE
  Regulation aspect [1]: if a UE can transmit using 29dBm when P-Max is not present in regions that do no allow 29dBm UE (e.g. Japan), it will violate local regulation.
    Note: Since 26dBm UE is allowed in Japan, there will be no regulation issue that UEs transmit using 26dBm when P-Max is not present.
  UE coverage aspect [2]: UE coverage may be shrinked caused by current cell selection mechanism when UE cannot transmit using the maximum output power if P-Max is not present.

## Slide 3: Discussion in RAN4#94-e
The following 3 options are proposed and most related companies support “Option 3” during 1st round discussion [3]
  Option 1: Add a new SIB parameter to allow 29 dBm operation in LTE as proposed in R4-2000424.
  Option 2: Allow 29 dBm operation when P-Max is not present as proposed in R4-2000905.
  Option 3: Only allow 29 dBm operation in NR and EN-DC for now, and not in LTE so that the Work Item can be completed. If an arrangement can be found in the future, then PC 1.5 may be enabled for LTE at that time.
    P-Max need to be broadcast by NR and EN-DC networks to avoid regulation issue in regions that do now allow 29dBm UE.
    Mandatory broadcasting P-Max by LTE networks is very costly since it requires new feature or configuration on already deployed base stations.

## Slide 4: Way forward
Only allow 29dBm in NR and EN-DC for current WI. The solution of 29dBm LTE will be postponed until we find an acceptable way for LTE 29dBm case.
  Requirements for 29dBm NR and EN-DC should apply If P-Max is not present.

## Slide 5: Reference
[1] R4-1915204, “29 dBm HPUE regulatory aspects”, Sprint
[2] R4-1806899, “Discussion on p-MAX for 5G NR Cell selection issue”, CMCC
[3] R4-2002700 “Email discussion summary for RAN4#94e_#27_LTE_NR_B41_Bn41_PC29dBm”, Sprint