## Slide 1: Way Forward on reuse of PC2 Cell Group A-MPR for PC1.5 EN-DC
Sprint, [Skyworks], [Qorvo], [Intel], [Qualcomm], [Apple]
3GPP TSG-RAN WG4 Meeting #94-e R4-20xxxxx
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
Questions have been raised about whether or not PC2 A-MPR can be re-used for PC1.5 intra-band EN-DC
While most companies agree that PC2 A-MPR can be re-used for PC1.5, at least one company believes that completely new A-MPR is required to be defined for PC1.5
Also, during the discussions questions were raised about if the cell group A-MPR is applied relative to the Cell group power class power, or relative to the EN-DC power class power minus 3 dB.

## Slide 3: Discussion in RAN4#94-e
There was a contribution explaining why PC2 A-MPR could be re-used for PC 1.5 in R4-2000425 [1]
The Round 1 discussions on this topic were captured as sub-issue 1-1 in R4-2002700 [2]

## Slide 4: Way forward
Using the baseline architecture of 26dBm + 26dBm = PC2 for PC2 intra-band EN-DC and 26dBm + 26dBm = PC1.5 for PC1.5 for intra-band EN-DC,
1) Companies that believe that for intra-band EN-DC the per CG NS_04 A-MPR is applied per CG relative to the CG power class are encouraged to explain how that aligns with the text in 38.101-3. Also, companies encouraged to explain why PC2 CG A-MPR can be applied to PC1.5 intra-band EN-DC.
2) Companies that believe that for intra-band EN-DC the per CG NS_04 A-MPR is applied per CG relative to Ppowerclass_en-dc – 3dB are encouraged to explain how that aligns with the text in 38.101-3. Also, companies encouraged to explain why PC2 CG A-MPR cannot be applied to PC1.5 intra-band EN-DC.

## Slide 5: Reference
[1] R4-2000425, “Applying the PC2 A-MPR requirements to PC1.5”, Sprint
[2] R4-2002700, “Email discussion summary for RAN4#94e_#27_LTE_NR_B41_Bn41_PC29dBm,” Moderator (Sprint)