## Slide 1: WF on EN-DC FDD+TDD HPUE China Unicom, CHTTL, vivo, Xiaomi
3GPP TSG-RAN WG4 Meeting #94-e R4-2002835
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Backgrounds
The scope of the WI is as following
The objective of this WI is to specify the standard needed for Power Class 2 (PC2) high power UE for EN-DC for 1 LTE FDD band and 1 NR TDD band (23dBm LTE + 23dBm NR and 23dBmLTE + 26dBm NR). The scope of this WI is the example band combination DC_3A_n78n. Specifically, it includes the following aspects:
Design the UE capability report signalling and facilitate SAR compliance based on the outcomes of the studies in TR 37.815
Standardize RF requirements
Evaluate any additional impact to the requirements due to the high power on UL.
Note: RAN4 needs to discuss whether existing RAN2 signalling can be reused to solve the issues in this WI. If there is RAN2 signalling impact then RAN4 will send LS to RAN2 to inform the solution. No RAN2 TUs are requested for this WI.

## Slide 3: Agreements
Two fixed LTE reference configurations of the PC2 FDD-TDD EN-DC, DutyLTE1=70% , DutyLTE2=40% were agreed
Average of two proposed options i.e. IMD2: 31.9 dB ; IMD4: 18.5dB for DC_3A_n78 combination were agreed
The following capability set was agreed, corresponding to DutyLTE1 and DutyLTE2.
  maxNRDuty1 ∈ {30%, 40%, 50%, 60%, 70%, 80%, 90%, 100% , Full_duty_supported}
  maxNRDuty2 ∈ {30%, 40%, 50%, 60%, 70%, 80%, 90%, 100% }
  Full_duty_supported: no restriction on uplink scheduling for both LTE and NR bands for applicability of PC2 inter-band EN-DC (FDD+TDD) requirements, i.e. SAR compliance will be fulfilled by UE based mechanisms e.g. P-MPR etc. if UE indicate maxNRDuty1= Full_duty_supported, maxNRDuty2 signaling will be overridden i.e. UE will follow Full_duty_supported capability.

## Slide 4: Way Forward
Following issues shall be further discussed in the next meeting:
  Choosing “default value” or “blind scheme” when capability parameters are absent
    Option1: Using default value of maxNRDuty for two cases of LTE and NR power combination
    Option2: Following blind scheme by reduced power (PLTE) and use of the common UL-DL patterns on the TDD CG
  Choosing “PC fallback” or “blind scheme” when the UL EN-DC scheduling exceeds the UE capability
    Option1: UE should fallback to PC3
    Option2: Blind scheme should be followed
Target on finishing this WI is in RAN#88.

## Slide 5: Reference
R4-2000316 Discussion on power class 2 UE for EN-DC FDD-TDD Samsung
R4-2000878 Discussion on configurations for FDD-TDD EN-DC High Power UE CHTTL,
R4-2001037 Consideration on SAR compliance schemes for PC2 FDD+TDD HPUE China Unicom
R4-2000447 MSD analysis on high power UE for DC_3-n78 Xiaomi
R4-2001188 MSD test results for Power Class 2 UE for EN-DC (1 LTE FDD band +1 NR TDD band) LG Electronics
R4-2001326 Specification of EN-DC Power Class 2 for FDD-TDD band combinations Ericsson
R4-2002097 Power class and configured power for PC2 FDD-TDD EN-DC Qualcomm
R4-2000121 on UE capability reporting for EN-DC (FDD+TDD) HPUE vivo
R4-2000968 Discussion on HPUE for TDD+FDD ZTE