3GPP TSG-RAN WG4 Meeting #94-e	R4-2002852

# Online, 24 Feb. – 6 Mar., 2020

Title:	LS to RAN2 on introduction of channel bandwidth combination set to asymmetric channel bandwidths

Response to:

Release:	Release 16

Work Item:	NR_n66_BW

Source:	RAN4

To:	RAN2

Cc:

Contact Person:

#### Name:	Liehai Liu

#### E-mail Address:	liuliehai@huawei.com

Attachments:

1. Overall Description:

During RAN4#94-e meeting, RAN4 agreed to introduce channel bandwidth combination set to asymmetric channel bandwidths defined in clause 5.3.6, in TS 38.101-1 [1], with following agreements:

- UE shall support asymmetric channel bandwidth combination set 0 which was defined in Rel-15 by default.

- For n66,  support of asymmetric channel bandwidth combination set 1 is optional in Rel16.

2. Actions:

To RAN4:

RAN4 respectfully asks RAN2 to consider the UE capability signalling for asymmetric channel bandwidth combination set.

3. Date of Next RAN4 Meeting:

TSG-RAN4 Meeting #94-Bis		20 - 24 Apr 2020                    Canada, CA

TSG-RAN4 Meeting #95		 25 - 29 May 2020                   Athens, GR

4. Reference

R4-2002851, CR for TS 38.101: adding wider channel bandwidths for n66, Huawei, HiSilicon