## Slide 1: WF on NR-U RRM Requirements (Part 1) (all agreements in RAN4#94-e in email thread #46)
Ericsson
3GPP TSG-RAN WG4 Meeting #94-e R4-2002283
Electronic Meeting, February 24-March 06, 2020
Agenda Items: 8.1.4, 8.1.4.1-8.1.4.6, 8.1.4.14

## Slide 2
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Specification Structure
Do not add “a” in section numbers in 36.133 for NR-U sections. Follow the section naming outline earlier agreed in R4-1914628 (RAN4#93)
“container” CR in R4-2000039
  R4-1914628 (agreed in RAN4#93) is enough and CR R4-2000039 with just NR-U section titles is unnecessary
  The CR in R4-2000039 shall not be pursued in future meetings

## Slide 4: General Applicability Rules
TBA

## Slide 5: SIB Reading in Cell Reselection and Handover Requirements
Discuss WF in R4-2002281 (WF on SIB reading in cell reselection and HO requirements for NR-U, Intel)
  If no agreement in RAN4#94-e, the topic shall not be pursued in the future meetings

## Slide 6: SI Reading in RRC Release with Redirection, RRC Re-establishment, and Paging Interruption Requirements
RAN4 to further discuss the maximum SI acquisition time in paging interruption, RRC re-direction and RRC re-establishment in NR-U

## Slide 7: Cell Reselection (Excluding SI Reading and Paging)
Mm,max for other DRX cycles (0.64 sec and 1.28 sec):
  Mm,max = [8] for DRX cycle = 0.64 seconds
  Mm,max = [4] for DRX cycle = 1.28 seconds
X dB offset condition for the at least one cell to be checked by the UE:
  Do not specify the X dB offset condition for the at least one cell to be checked by the UE

## Slide 8: Handover Requirements (Excluding SIB Reading)
Wait for RAN2 response LS on UL LBT failure detection/recovery for the target cell

## Slide 9: RRC Release with Redirection
TBA

## Slide 10: RRC Re-Establishment
Do not specify K3,max
Do not specify K1,max and K2,i,max
Do not specify KSI,max

## Slide 11: SCell Activation
Time period in the known cell condition for SCell activation:
  do not extend the time period in the known SCell condition
Does the interruption window length at SCell activation depend on DL LBT failures?
  Conclusion: postpone discussion till R15 get agreed

## Slide 12: SCell Activation Delay
X=5 ms, Y=5 ms, Z=5 ms
THARQ (in ms) is the timing between DL data transmission and acknowledgement as specified in TS 38.213. In the event of UE not being able to transmit the acknowledgment due to UL CCA failures: THARQ is extended to also include the time to all next HARQ feedback retransmission opportunities, until the time of its successful transmission, as specified in TS 38.213; no extension of THARQ due to UL LBT failures is allowed for channel access category 1
  The term “channel access category 1” needs to be aligned with RAN1 terminology (e.g., in TS 37.213)
TCSI_reporting = TCSI_reporting,ref +L4*TCSI-RS +CSI, where
  TCSI_reporting,ref is CSI reporting delay as specified in section 8.3.2,
  UE behavior upon exceeding L4,max (L4,max=TBD) is to abandon the SCell activation procedure,
  CSI is the total additional delay in CSI reporting due to UL LBT failures, according to TS 38.213
FFS: UE behavior and the SCell activation delay extension due to any LBT failures when sCellDeactivationTimer is not configured

## Slide 13: PSCell Addition
Time period in the known cell condition for PSCell addition:
  do not extend the time in the known cell condition in PSCell addition delay requirement
In the event of UE not being able to transmit PRACH due to UL CCA failures on this carrier: PRACH is the total time extended to also include the time to all next PRACH retransmission opportunities, until the time of its successful transmission, as specified in TS 38.213; PRACH=0 for channel access category 1
  The term “channel access category 1” needs to be aligned with RAN1 terminology (e.g., in TS 37.213)

## Slide 14: Active TCI State Switching
Time period in the known state condition for active TCI state switching:
  do not extend the time in the known cell condition in active TCI switching delay requirement
RRC-based: upon exceeding LRRC,known,max, UE shall stop the active TCI state switching procedure and declare beam failure; upon exceeding L1RRC,unknown,max or L2RRC,unknown,max the UE shall abandon the active TCI state switching procedure and declare beam failure
MAC-CE based: upon exceeding LMAC,known,max, the UE shall stop the active TCI state switching procedure and stay in the old state; upon exceeding L1MAC,unknown,max or L2MAC,unknown,max the UE shall abandon the active TCI state switching procedure and stay in the old state
  NOTE: The above agreement on MAC-CE based switching can be revisited if/when the change in Rel-15 specification is agreed
THARQ (in ms) is the timing between DL data transmission and acknowledgement as specified in TS 38.213. In the event of UE not being able to transmit the acknowledgment due to UL CCA failures: THARQ is extended to also include the time to all next HARQ feedback retransmission opportunities, until the time of its successful transmission, as specified in TS 38.213; no extension of THARQ due to UL LBT failures is allowed for channel access category 1
  The term “channel access category 1” needs to be aligned with RAN1 terminology (e.g., in TS 37.213)