## Slide 1: WF on NR-U RRM Requirements (Part 2) (all agreements in RAN4#94-e in email thread #47)
MediaTek inc
3GPP TSG-RAN WG4 Meeting #94-e R4-2002284
Electronic Meeting, February 24-March 06, 2020
Agenda Items: 8.1.4

## Slide 2
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Active BWP switching
Introduce UL BWP switch requirements (delay and interruption) triggered by consistent UL LBT failures
UL BWP switch requirements triggered by consistent UL LBT failures
  Option 1: Follow DCI and timer-based BWP switch
  Option 2: FFS

## Slide 4: SSB based RLM
For SSB-based RLM in-sync
  Lin,max = 7 for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
  Lin,max = 5 for 40<Max(TDRX,TSSB)≤320
  Lin,max = 3 for TDRX>320
No additional requirements for due to consecutively missing SSBs due to for SSB-based RLM INS
The set of SSB that UE is required to monitor
  Option 1: UE is required to monitor at least one SSB from the set of SSBs that are QCLed with each other
  Option 2: UE is required to monitor SSBs from the set of SSBs that are QCLed with each other within the set of configured RLM-RS resources, until it detects an SSB during this SMTC during RLM or link recovery procedures
  Option 3: UE shall monitor all SSBs configured for RLM, regardless of QCL information

## Slide 5: SSB based RLM
The RLM requirements shall not relay on COT information availability
  FFS whether the decision is applicable to both FBE and LBE or only one of them
FFS whether UE can expect gNB to transmit RLM-RS with same transmit power across different occasions
Whether to extend the OOS evaluation period based on the number of unavailable SSB
  Option 1: No. Out-of-sync evaluation period is extend by a fixed number of samples
  Option 2: Yes. OOS evaluation is based on Lout, where Lout ≤Lout,max is the number of SSBs not available at the UE during TEvaluate_out_SSB
  Option 3: Select option 2 in FBE networks and option 1 in LBE networks

## Slide 6: CSI-RS based RLM
How to handle CSI-RS based RLM
  Option 2: Adapt the same approach for the extension of the INS and OOS evaluation periods for CSI-RS based RLM as in SSB based RLM
  Option 3: RAN4 deprioritizes defining requirements for CSI-RS based RLM in Rel-16 NR-U networks.

## Slide 7: BFD and CBD
How to handle BFD
  Option 1: Adapt the same approach for RLM OOS
  Other options are not precluded
How to handle CBD
  Option 1: Adapt the same approach for RLM
  Other options are not precluded

## Slide 8: Timing
One shot timing adjustment is not allowed when UE changes its DL timing reference cell to any activated SCell if SpCell is unavailable to UE for a certain number of DL SSB detection attempts.
deriveSSB-IndexFromCell is optional on unlicensed band