## Slide 1: WF on CLI RRM Performance Requirements
3GPP TSG-RAN WG4 Meeting #94-e Electronic Meeting, Feb.24th – March 6th 2020
Agenda Item: 8.2.3
R4-2002222
LG Electronics

## Slide 2: Measurement accuracy for CLI
Define measurement accuracy for SRS-RSRP
  For 120kHz in FR2
    Option1: use average value among companies’ results (9dB)
    Option2: keep FFS, and discuss it in the next meeting
  Companies are encouraged to provide simulation results for SRS-RSRP, then final accuracy values will be derived based on provided simulation results in the next meeting
Define measurement accuracy for CLI-RSSI
  Re-use LAA RSSI accuracy requirements for CLI-RSSI for FR1, and allow 1.5dB relaxation for CLI-RSSI for FR2
FR | SCS | Accuracy Requirement ( ±[ ]dB)
FR1 | 15kHz | [3]
 | 30kHz | [4]
 | 60kHz | [5.5]
FR2 | 60kHz | [6.5]
 | 120kHz | FFSTBD

## Slide 3: Measurement accuracy for CLI
Measurement accuracy for extreme condition and high Io
  Extreme condition with Io=-70dBm/BW is derived by adding 4.5/3dB for FR1/FR2 to the absolute L1-RSRP accuracy in normal condition.
  Normal condition with Io=-50dBm/BW is derived by adding 3.5/3dB for FR1/FR2to the absolute L1-RSRP accuracy in normal condition with Io=-70dBm/BW.
  Extreme condition with Io=-50dBm/BW is derived by adding 2/2dB for FR1/FR2 to the absolute L1-RSRP accuracy in extreme condition with Io=-70dBm/BW.
    Extreme condition with Io=-50dBm/BW
      Option 1: x = 2
      Option 2: x = 3

## Slide 4: Test case list for CLI performance
Following test cases are defined
  Companies are encourage to investigate whether timing shift for constant offset compensation brings interruption to E-UTRAN for EN-DC case.
Sub-test for SRS-RSRP and CLI-RSSI (as starting point)
  SRS-RSRP for FR1: 3 sub-tests with different SRS-RSRP and Io levels (similar to SS-RSRP)
  SRS-RSRP for FR2: 2 sub-tests with different SRS-RSRP and Io levels (similar to SS-RSRP)
  CLI-RSSI : 1 sub-test (similar to LAA RSSI)
# | Test cases for SRS-RSRP
1 | [SRS-RSRP measurement delay with non-DRX FR1 EN-DC]
2 | [SRS-RSRP measurement delay with DRX FR2 EN-DC]
3 | SRS-RSRP measurement delay with DRX FR1 SA
4 | SRS-RSRP measurement delay with non-DRX FR2 SA
5 | [SRS-RSRP measurement accuracy FR1 EN-DC]
6 | [SRS-RSRP measurement accuracy FR2 EN-DC]
7 | SRS-RSRP measurement accuracy FR1 SA
8 | SRS-RSRP measurement accuracy FR2 SA
# | Test cases for CLI-RSSI
1 | [CLI-RSSI measurement delay with non-DRX FR1 EN-DC]
2 | [CLI-RSSI measurement delay with DRX FR2 EN-DC]
3 | CLI-RSSI measurement delay with DRX FR1 SA
4 | CLI-RSSI measurement delay with non-DRX FR2 SA
5 | [CLI-RSSI measurement accuracy FR1 EN-DC]
6 | [CLI-RSSI measurement accuracy FR2 EN-DC]
7 | CLI-RSSI measurement accuracy FR1 SA
8 | CLI-RSSI measurement accuracy FR2 SA

## Slide 5: Test configuration for CLI performance
BW and SCS
  15kHz+10MHz, 30kHz+40MHz, 120k+100MHz
Timing difference between DL and CLI measurement resource
  TC × NTA_offset + 4.67us for FR1 and TC × NTA_offset + 3.67us for FR2
AoA setup for FR2
  Option 1: single AoA (Setup#1)
  Option 2: 2 AoA

## Slide 6: Test configuration for CLI performance
SRS configuration for SRS-RSRP measurement accuracy test
 | Field | SRSConf.x
SRS-ResourceSet | srs-ResourceSetId | 0
 | srs-ResourceIdList | 0
 | resourceType | Periodic
 | Usage | Codebook
SRS-Resource | SRS-ResourceId | 0
 | nrofSRS-Ports | Port1
 | transmissionComb | n2
 | combOffset-n2 | 0
 | cyclicShift-n2 | 0
 | resourceMapping startPosition | 0
 | resourceMapping nrofSymbols | n1
 | resourceMapping repetitionFactor | n1
 | freqDomainPosition | 0
 | freqDomainShift | 0
 | freqHopping c-SRS | 12
 | freqHopping b-SRS | 0
 | freqHopping b-hop | 0
 | groupOrSequenceHopping | Neither
 | resourceType | Periodic
 | periodicityAndOffset-p | sl1
 | sequenceId | 0