## Slide 1: WF on Power class fallback enhancement
NTT DOCOMO, INC., …
TSG RAN WG4 meeting: 94-e Electronic Meeting R4-200xxxx
Feb.24th – Mar.6th 2020

## Slide 2: Background
[1] received several comments as summarized below.
#1
  Network needs to distinguish from UEs with this enhanced feature from UEs without this feature. Thus, capability signaling is required.
#2
  In the proposed equation, the division by maxUplinkDutyCycle (in logarithm) can be seen but it seems impossible since it is condition that "UE capability of maxUplinkDutyCycle is absent".
#3
  ΔPpowerclass parameter should not be used for the purpose of "graceful" fallback to PC3; the intent of this parameter is to compensate for differences between the indicated power class and the applicable power-class requirement (should only be difference between power class values if any). Use another (new) notion instead
#4
  In the condition that 10log(% UL symbols / maxULDutyCycle) < 3dB, then UE should apply requirements of supported power class. Does this mean that if uplink symbols exceeds max UL Duty Cycle, the PC2 should still apply?

## Slide 3: WF
At least the followings are needed to introduce this feature.
  #1: dedicated capability signaling is requred.
  #2:
    In the equation of 10Log(the percentage of uplink symbols transmitted/ maxUplinkDutyCycle), in case the field of UE capability maxUplinkDutyCycle is absent, it should be clarified that the division is 50%.
  #3: A new parameter is introduced to return the log equation.
  #4: UE Power Class is PC2 when the new parameter is being valid.

## Slide 4: Reference
[1] R4-2002158: CR for power class fallback enhancement, Huawei, Hisilicon