## Slide 1: WF on UL MIMO PC2
Huawei, HiSilicon, vivo, OPPO
R4-2002738
3GPP TSG-RAN WG4 #94-e
Feb 24th – Mar 06th, 2020
Electronic meeting

## Slide 2: Remaining issues for UL MIMO PC2
Power class ambiguity needs change or not
Spec language: “UE supporting UL MIMO” or “UE configured for UL MIMO”
Emission requirement correction for UL MIMO
Power class signalling for Rel-16
Need for new MPR requirements

## Slide 3: Power class ambiguity
Option 1: Power class baseline is UL MIMO, and exception is allowed for UE configured to single antenna port. Either PC2 or PC3 MOP requirements could apply for a PC2 UE supporting UL MIMO.
Option 2: Power class baseline is single antenna port mode, and exception is allowed for UE configured to UL MIMO. Either PC2 or PC3 UL MIMO MOP requirements could apply for a PC3 UE.
Option 3: Power class should be the same for both UL MIMO or single antenna port mode.
Option 4: No clarification is needed to current spec
Options 5: Power class is the same for both UL MIMO or single antenna port mode. Exception is allowed for some UE implementation and RAN5 test cases may consider this kind of exception
Conclusion: No conclusion yetFurther discussion based on these options
Option 2.
The Rel-15 UE advertises its minimum power capability for all transmissions and the PHR is adjusted by a UL-MIMO PC2 configured with two-port configuration (PHR correct and reflects PC2 capability for this case). The ambiguity is removed (save a possible additional power-class indication for two-layer transmission)
UEs capable of transparent TxD according to Rel-16 FP (UE indicating the modes supported)
Option1.
UE fulfil UL MIMO PC2 requirements shall indicate PC2 capability

## Slide 4: “UE supporting UL MIMO” or “UE configured for UL MIMO”
Generally, “UE configured for UL MIMO” is agreeable. But the changes should be checked case by case.
Conclusion:
CR R4-2001316 or R4-2000354 could be used as baseline to check where to make changes for “UE supporting UL MIMO” instead of “UE configured for UL MIMO”.
Requirments for single antenna port mode with different implementation should also be checked for applying the changes
  fallback behaviour specified with power capability according to indicated power class (ue-PowerClass)

## Slide 5: Emission requirement correction for UL MIMO
Emission requirements in Rel-15 are not aligned with the regulatory requirements
MPR requirements in Rel-15 are defined based on the SE/SEM requirements applied at each antenna connectors for UL MIMO
If the unwanted emissions requirements for UL MIMO should be changed, no consensus on which release to capture the changes
Conclusion:
In principle, tThe emission requirements should be changed for Rel-15 to align with the regulatory requirements: the sum of the power from all connectors
Allow measurements per antenna connector if these are compared to a 3 dB tighter emission limit (additionalalternative measurement configuration)
MPR requirements should be revisited for UL-MIMO PC2 (Rel-15) in conjunction with the changed emission requirements with solid justifications
FFS on which release to reflect the changes of emission requirements

## Slide 6: Power class signalling for Rel-16
It was agreed in previous RAN4 meetings that no new signalling is introduced for Rel-15 (SA) and some clarifications are captured in TS 38.101-3 for NSA scenario
Rel-16 spec does not include the clarification as that in Rel-15 spec and ambiguity still exists
In principle, iIntroduction of new power class for MR-DC is agreeable discussed
Conclusion:
Introduce new power class for NR band in MR-DC in Rel-16 No need to change the MR-DC power-class indication for the NR band since Option 2 is chosen
FFS whether the signaling similar to E-UTRA in MR-DC could be defined for NR Consider additional power-capability indication for UL-MIMO PC2 in the context of the FP eMIMO Rel-16 WI (e.g. indication for FP that also works for UL-MIMO PC2 Rel-15). Discussed after the agreement is reached in “power class ambiguity ” page.
Send RAN4 agreement of new signaling for Rel-16 to RAN2No LS to RAN2 before RAN4 has concluded on signaling for FP (eMIMO Rel-16 WI)
Further discuss the introduction of new power class for MR-DC

## Slide 7: Need for new MPR requirements
MPR requirements is related to the applied SE/SEM requirements
Initial proposed change is for PC2 UE at edge RB allocation
Conclusion:
The MPR issue is considered together with the emission issue
MPR for UL-MIMO PC2 HPUE should to be consideredspecified e.g. along the lines of the initial proposal
If needed, new MPR for UE supporting UL MIMO PC2 should be defined in Rel-15 and which release should be introduced will be considered together with change of emission requirements
MPR for UL MIMO is revisited for Rel-15. Specific values and which clause for the requirement are FFS.

## Slide 8
Reference
[1] R4-2000063, Clarification of Power Class related features, NTT DOCOMO, INC.
[2] R4-2001229, Further on UL MIMO PC2 fallback, OPPO
[3] R4-2002037, On UL MIMO requirements, Huawei, HiSilicon
[4] R4-2002038, On EN-DC power class, Huawei, HiSilicon
[5] R4-2000356, Correction on UL MIMO Emission requirements and alignment with RAN1 terminology, Qualcomm Incorporated
[6] R4-2000795, On the condition of antenna configuration for UL-MIMO in FR1, SoftBank Corp.
[7] R4-2000117, CR to 38.101-1 clarification of MIMO power class in R15, vivo
[8] R4-2001316, Correction of transmitter characteristics for UL-MIMO: power class 2 and fallback, Ericsson
[9] R4-2000354, Correction on UL MIMO Emission requirements and alignment with RAN1 terminology, Qualcomm Incorporated
[10] R4-2000118, draft LS on clarification of EN-DC power class in R15, vivo
[11] R4-2002141, Draft LS on EN-DC power class, Huawei, HiSilicon