## Slide 1: WF on NR V2X RRM requirements
LG Electronics, MediaTek
3GPP TSG-RAN WG4 #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
R4-2002230

## Slide 2
NR V2X RRM part 1

## Slide 3
Rx drop rate for selection/reselection of NR V2X synchronization reference source
  X=2slots, Y=0.3%, Tdetect,SyncRef UE_V2X = [8]sec for FR1 all SCS
  If technical issue is found, it needs to be revised.
Ping-Pong effect when gNB is timing reference source
  Not define related RRM requirement
Side condition of S-RSRP measurement for initiation/cease SLSS transmissions
  - 6dB
Terminology ‘S-RSRP’ vs ‘PSBCH-RSRP’
  Postpone discussion till RAN4 #94bis
Terminology ‘V2X’ vs ‘SideLink’ in Rel-16 RAN4’s all requirements
  Postpone discussion till RAN4 #94bis
Synchronization requirements

## Slide 4
Distance-based HARQ feedback option 1
  Postpone discussion to the WI Performance part
Sidelink RLM requirement
  Postpone discussion till RAN4 94bis
  Conclusion: Do not to define sidelink RLM requirement in R16 if sidelink RLM procedure is not finalized before RAN4 94bis
Annex.B.4 for NR V2X RRM side conditions
  Specify Annex B.4 for NR V2X RRM side conditions. Exact values are FFS and further discuss after RF REFSENS is decided
Unicast, groupcast related & AnnexB.4

## Slide 5
NR V2X RRM part 2

## Slide 6
RAN4 RRM define the requirement for gNB or eNB using as synchronization source
Regarding SL+Uu band combination, that is, in case that V2X UE can schedule data on both Uu and SL,
  Option 1 : Not to define RRM requirement due to time limit
  Option 2 : Define related RRM requirement
  Option 3 : Further study
Any requirement related to gNB/eNB

## Slide 7
Whether to define dedicated requirement for pre-emption behavior(CR R4-2002228)
  Capture the pre-emption requirement as part of resource (re-)selection requirement as following sentence
    [When the pre-emption mechanism is enabled for the resource pool that UE is monitoring and selecting resource from,] after UE selects from the resource not excluded based on L1 SL-RSRP measurement procedure, the UE shall be capable of triggering reselection of already signalled resource(s) as a resource reservation when the conditions specified in [1] are satisfied.
      [1] (corresponding RAN2 spec)
Measurement requirements(1)

## Slide 8
Do not define dedicated requirement for re-evaluation behaviour.
RAN4 to evaluate both of PSSCH DMRS and PSCCH DMRS measurement accuracy based on the simulation. Whether to define both of them or only the worst case can be decided after the evaluation.
  The simulation assumption is captured in R4-2002232.
Consider only 1 shot when defining the accuracy requirement for L1 SL-RSRP.
Define PSCCH measurement requirement based on 10 PRBs and 2 symbols.
Define PSSCH measurement requirement
  Postpone the discussion till RAN4 #94bis
Collision between PSSCH-DMRS and PSCCH
  Postpone the discussion till RAN4 #94bis
Do not define S-RSSI in autonomous resource reselection.
Measurement requirements(2)

## Slide 9
Companies are encouraged to submit the L1 SL-RSRP measurement simulation results in next RAN4 meeting.
SINR side condition for L1 SL-RSRP
  Option 1: Follow LTE side condition for L1 SL-RSRP measurements
  Option 2: The side condition for L1 SL-RSRP measurements shall be larger than the side condition for 1st stage SCI
Discuss whether the definition on PSSCH RSRP in multiple antennas configuration impact RAN4 spec.
  Option 1: Send the LS to RAN1 for further clarification
  Option 2: Add an editor note, “If RAN1 agrees to an RSRP measurement procedure for multiple Tx port that RAN4’s accuracy requirement defined based on single Tx port may not apply, companies can re-discussion on RSRP accuracy requirement based on the RAN1’s agreement”.
  Option 3: Multiple Tx antenna configuration doesn’t impact the RSRP calculation in RAN4.
Measurement requirements(3)

## Slide 10
S-RSSI measurement accuracy in congestion control
  Reuse S-RSSI measurement accuracy in LTE-V2X
Measurement requirements(4)

## Slide 11
Interruption for switching between LTE SL and NR SL
  RAN4 RRM will discuss whether and how to define the interruption requirement for switching between LTE SL and NR SL.
Interruption for Sync. source change
  For the scenario that SL UE is changing its sync source from GNSS to a syncRef UE that is synchronized to GNSS directly or in-directly
    Option 1 : interruption is not needed to be specified
    Option 2 : interruption is needed to be specified
    Option 3 : need further discussion
  For the scenario that SL UE is changing its sync source from gNB to eNB or eNB to gNB
    Option 1 : interruption is not needed to be specified
    Option 2 : interruption is needed to be specified
Interruption requirements