# 3GPP RAN WG4 Meeting #94-e                                                                          R4-2002232

# Online, 24th February – 6th March 2020

Source:	LG Electronics

Title:	Simulation assumption of PSSCH-RSRP and PSCCH-RSRP measurement

Agenda item:	8.4.5.3

Document for:	Approval

# Introduction

In this contribution, we propose simulation assumptions of PSSCH-RSRP measurement and PSCCH-RSRP measurement based on the new RS structure for measurement related to requirement of autonomous resource selection/reselection measurements.

# Discussion

## PSSCH-RSRP and PSCCH-RSRP measurement accuracy

- Simulation assumption

Table 2.1-1 shows simulation assumptions for PSSCH-RSRP measurement and PSCCH-RSRP measurement.

Table 2.1-1: Simulation assumptions for PSSCH-RSRP measurement and PSCCH-RSRP measurement accuracy

| Parameters | Value | Comments |
| --- | --- | --- |
| Duplex mode | TDD |  |
| Measurement bandwidth for PSSCH-RSRP | 10 resource blocks | Minimum {10, 15, 20, 25, 50, 75, 100} PRBs (possible sub-channel size) |
| Measurement bandwidth for PSCCH-RSRP | 10 resource blocks | Minimum {10, 12, 15, 20, 25} PRBs (candidate numbers of PRBs) |
| Duration of the scheduled resources for transmission of PSSCH (ld) | 9 symbols | TS38.211 Table 8.4.1.2.2-1 |
| Number of PSCCH symbol in a slot(l = PSCCH symbol position) | 2 symbols(l={1,2}) | TS38.211 Table 8.4.1.2.2-1 |
| Number of PSSCH DMRS symbol in a slot(l = PSSCH DMRS position) | 2 symbols (l={3,8}) | TS38.211 Table 8.4.1.2.2-1 |
| Sub Carrier Spacing | 15kHz, 30kHz, 60 kHz |  |
| L1 measurement | 1 shot measurement |  |
| L3 filtering | Disabled |  |
| Transmit antenna | 1 |  |
| Receive antennas | 2 | Note that the measured value shall not be lower than the corresponding value of any of the individual diversity branches. |
| Number of DMRS CDM group(s) without data | 1 |  |
| DMRS port(s) | 0 |  |
| Ratio of PSSCH EPRE to DM-RS EPRE (dB) | 0 |  |
| Propagation conditions | AWGN, TDL- C with 30ns, 1400Hz, TDL- C with 100ns, 300Hz TDL- C with 10ns, 1400Hz, TDL- C with 100ns, 150Hz |  |
| CP length | Normal |  |
| Carrier frequency | 5.9GHz |  |
| Frequency Offset relative to UE frequency reference | 0Hz |  |
| PSSCH_Ec/Iot | {-6, -3, 0, 3} dB | AWGN noise , The minimum SNR point is selected based on PSCCH performance (companies are encouraged to provide results on SA BLER vs SNR) |
| PSCCH_Ec/Iot | {-6, -3, 0, 3} dB | AWGN noise , The minimum SNR point is selected based on PSCCH performance (companies are encouraged to provide results on SA BLER vs SNR) |
| Note 1: AWGN is a mandatory propagation conditions. The company is also encouraged to submit the simulation with other propagation condition. |

- Performance metrics for PSSCH-RSRP

The following performance metrics can be considered

- The CDF curves (including the 95% and 5% CDF points) for delta PSSCH-RSRP.

Delta PSSCH-RSRP is defined as follows:

Delta PSSCH-RSRP = Measured PSSCH-RSRP – Ideal PSSCH-RSRP.

Ideal PSSCH-RSRP is defined as the true value assuming perfect channel estimation using the same sampling rate and sampling occasions as used in the measured PSSCH-RSRP evaluation.

- Performance metrics for PSCCH-RSRP

The following performance metrics can be considered

- The CDF curves (including the 95% and 5% CDF points) for delta PSCCH-RSRP.

Delta PSCCH-RSRP is defined as follows:

Delta PSCCH-RSRP = Measured PSCCH-RSRP – Ideal PSCCH-RSRP.

Ideal PSCCH-RSRP is defined as the true value assuming perfect channel estimation using the same sampling rate and sampling occasions as used in the measured PSCCH-RSRP evaluation.

# Conclusion

In this paper, we provided simulation assumptions for evaluating PSSCH-RSRP measurement accuracy and PSCCH-RSRP measurement accuracy. Based on the simulation assumption, we encourage companies to provide simulation results in RAN4#94bis.

# Reference

[1] R4-1915783, “WF on NR V2X RRM requirement”, LG Electronics