## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #94-e Meeting
Electronic Meeting, 24 Feb. – 6 Mar., 2020
R4-2002245

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | FFS
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | FFS
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | FFS
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | FFS
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | FFS
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | FFS
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | FFS

## Slide 3: Agreement
Define MAC CE based spatial relation info switching delay for PUCCH
Define RRC based spatial relation info switching delay for P-SRS
Define DCI based spatial relation info switching delay for A-SRS
  When spatial relation info associated with DL-RS
    For unknown TCI state, there is no requirement
    For known TCI state, refer to RAN1 spec.
No requirements are defined for spatial relation info switching delay for PUSCH
No requirements are defined for spatial relation info switching for PUCCH when PUCCH-SpatialRelationInfo is not configured

## Slide 4: Way Forward
Whether to define delay requirement for spatial relation info switching associated with UL SRS
Option 1: Yes
Option 2: No
# | Scenario | Whether to introduce requirement
2 | PUCCH-RRC-UL | FFS
4 | PUCCH-MAC-UL | FFS
7 | pSRS-RRC-UL | FFS
9 | spSRS-MAC-UL | FFS
11 | aSRS-DCI-UL | FFS

## Slide 5: Way Forward
Whether to define delay requirement for RRC based spatial relation info switching for PUCCH?
Option 1: Yes
Option 2: No
# | Scenario | Whether to introduce requirement
1 | PUCCH-RRC-DL | FFS

## Slide 6: Way Forward
Delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH
For known TCI state
  Option 1: THARQ +3ms
  Option 2: THARQ +3ms, if the fine timing of the downlink RS is acquired. Otherwise, no requirement
  Option 3: THARQ +3ms + time for time tracking if applicable
  Option 4: UE to switch beams at THARQ + 3ms (RAN1 specification). Performance guaranteed (in terms of timing etc) after reception 1 SSB(similar to TCI state switching)
For unknown TCI state
  Option 1: THARQ + 3ms + TL1-RSRP
  Option 2: THARQ + 3ms + TL1-RSRP + time for time tracking if applicable
  Option 3: No requirement
# | Scenario | Whether to introduce requirement
3 | PUCCH-MAC-DL | Yes

## Slide 7: Way Forward
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
For known TCI state
  Option 1: Define delay based on RRC based TCI state switching requirements
  Option 2a: TRRCprocessing (timing is acquired)
  Option 2b: TRRCprocessing (timing is not required)
  Option 3: No requirements
For unknown TCI state
  Option 1: Define delay based on RRC based TCI state switching requirements
  Option 1a: TRRCprocessing + TL1-RSRP
  Option 2: No requirements
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes

## Slide 8: Way Forward
Delay requirement for RRC based spatial relation info switching associated with SRS for P-SRS
  Option 1: TRRCprocessing
  Option 2: No requirements
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes

## Slide 9: Way Forward
Whether to define delay requirement for MAC CE based spatial relation info switching for SP-SRS?
Option 1: Yes
Option 2: No
# | Scenario | Whether to introduce requirement
8 | spSRS-MAC-DL | FFS

## Slide 10: Way Forward
Delay requirement for MAC CE based spatial relation info switching associated with SRS for PUCCH
Option 1: THARQ +3ms
Option 2: Deprioritize
Option 3: Refer to RAN1 requirement
Note the conclusion in Page 4 will have impact to this page
# | Scenario | Whether to introduce requirement
4 | PUCCH-MAC-UL | FFS

## Slide 11: Way Forward
When the UL signal has spatial relation to an unknown TCI-state,
  Option 1: UE transmits with previous TX beam/ arbitrary beam
  Option 1a: UE transmits using previous TX beam
  Option 2: Up to UE implementation
  Option 3: UE behaviour shall not be specified for the period until TCI state becomes known.