## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e R4-2002244
Electronic Meeting, 24 Feb. – 6 Mar., 2020

## Slide 2: Background
In RAN4#93 WF on BWP switching on multiple CCs was approved - R4-1915933

## Slide 3: Simultaneous BWP switching on multiple CCs (1)
Issue 1-1-1: RRC based simultaneous triggering for NR-DC operation
Agreement: RRC based simultaneous triggering for BWP switch on multiple CCs for NR-DC operation is not considered
Issue 1-1-2: Delay requirements for DCI/timer based BWP switch
Agreement: ; N: Number of CCs with simultaneous BWP switch; K is number of CCs that can be processed simultaneously; D is incremental delay for BWP switch processing on additional CCs
Options for D
  D=100us for Type 1; 200 us for Type 2 (Huawei, MediaTek)
  D = 450us for Type 1; 1.5ms for Type 2 (Qualcomm, Apple)
Options for K
  K=1 (Huawei, Apple, Intel, QC)
  K=2 (MediaTek)
  K=4 (NEC)

## Slide 4: Simultaneous BWP switching on multiple CCs (2)
Issue 1-1-3: Delay requirements for RRC based BWP switch
Option 1a ( Intel, Vivo, Apple, Qualcomm): ; N: Number of CCs with simultaneous BWP switch; K: Number of CCs that can be processed simultaneously
  Options 1a-1
    K=1 (Intel, Apple, Vivo, Qualcomm)
Option 1b (NEC, Nokia?) : ; D= BWP switching delay without processing delay of RRC
  Options 1b-1
    K=Based on UE capability discussion (NEC)
    K=1 (QC)
Option 2 (Huawei, MTK): on each individual CC

## Slide 5: Simultaneous BWP switching on multiple CCs (2)
Issue 1-1-4: Interruption requirements for simultaneous BWP switch
Agreement: Consider interruption on each CC separately
For interruption length:
Option 1(Huawei, Nokia): Use same interruption requirements as single CC case on each CC
Option 2 (Vivo, Ericsson): Extend interruption compared to single CC case; Extension depends on number of CCs undergoing simultaneous BWP switch
Option 3a (Vivo): Interruption length is determined by smallest SCS among all CCs before and after BWP switch
Option 3b (Intel):
  Option 3b-1
    K=1 (Apple, Intel)

## Slide 6: Partial Overlap BWP switching on multiple CCs (1)
Issue 1-2-1: DCI based partial overlap BWP switch for NR-DC
Option 1 (NEC, QC, Vivo): Not considered
Option 2 (Huawei, Ericsson, Intel, Nokia, MTK): Considered
Option 2a (Qualcomm): Considered when defined only for cases when UE supports per FR gap
Issue 1-2-2: Conditions when requirements for partial overlap BWP switch are defined
Option 1 (Vivo, Intel, Apple, MTK, Qualcomm): When UE is capable of per FR gap and BWP switch is on different FR/When BWP switch on one CC doesn’t cause interruption on other CCs (with partial overlap BWP switch)
Option 2 (Ericsson, NEC): No restriction

## Slide 7: Partial Overlap BWP switching on multiple CCs (2)
Issue 1-2-3: Delay requirements for DCI/Timer/RRC based BWP switch
DCI Based: Depends on outcome of Issue 1-2-1, 1-2-2
RRC Based: Depends on outcome of Issue 1-2-2
Timer Based: Depends on outcome of Issue 1-2-2
Issue 1-2-4: Interruption requirements for partial overlap BWP switch
Agreement: Same as single CC, considered on each CC separately