## Slide 1: Way forward on multiple SCell activation and UE-specific CBW switching
Apple, …
R4-20xxxxx
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
Agenda item: 8.15
Document for: Approval

## Slide 2: Part 1: Way forward on multiple SCell activation

## Slide 3: Requirement scope of multiple SCell activation (sub-topic 1-1 in R4-2002187)
Agreement in RAN4 #94e:
  In EN-DC, NE-DC, NR SA, RAN4 will define requirements only for the case where a single MAC command is used to activate multiple SCells; while in NR-DC RAN4 will define requirements for the case where one MAC command per CG is used.
    In one single CG, there are no other NR SCell activations going on when the activation/deactivation command is received or sCellDeactivationTimer turns to be expired.
    In one single CG, there are no other NR SCell activation, deactivation, addition or release before activation is completed for all the SCells activated by the single MAC CE

## Slide 4: MAC PDU and MAC CE processing delay (sub-topic 1-2 & 1-3 in R4-2002187)
Agreement in RAN4 #94e:
  MAC CE processing time:
    For NR-CA, EN-DC, NE-DC, and NR-DC with non-simultaneous MAC commands, the MAC processing and application time shall be 3ms.
    FFS: In NR-DC scenario, for simultaneously received MAC commands on dual NR CGs, the MAC processing and application time shall be
      Option 1: 3ms;
      Option 2: 6ms.
    (will be deleted later) moderator question: can we agree on option 1, since in NR-DC case UE may receive different types MAC CEs simultaneously (e.g. SCell activation and TCI change) as well but the MAC CE decoding/application time is not changed in spec?
  MAC PDU processing time:
    If the single MAC PDU contains MAC commands for SCell activation (multiple cells), TCI state activation for PDCCH (for SCell group), TCI state activation for PDSCH (for SCell group) and SP CSI-RS activation (for SCell group) then the MAC processing and application time should be 3ms.

## Slide 5: Delay extension due to interruption on L1-RSRP measurement resource(sub-topic 1-4 in R4-2002187)
Agreements in RAN4 #94e:
  FFS on the necessity of the delay extension due to interruption on L1-RSRP measurement resource
    Option 1: In NR CA, there is no additional interruption on the L1-RSRP reporting resource of the target to-be-activated SCell and no additional delay extension is needed. In NR DC, EN-DC, NE-DC, only 1 extra L1-RSRP RS periodicity is needed when interruption occurs on the L1-RSRP reporting resource of the target to-be-activated SCell.
    Option 2: no need to consider whether delay extension is needed or not when a SSB that would have been used for L1-RSRP measurement is interrupted. The interruptions relating to other SCells have already occurred when the UE starts the L1-RSRP measurement.
    Option 3 (new added):
      For per-FR MG capable UE, there is no additional interruption on the L1-RSRP reporting resource of the target to-be-activated SCell and no additional delay extension is needed.
      For per-UE MG capable UE in NR CA, FFS.
      For per-UE MG capable UE in NR DC, FFS.
      For per-UE MG capable UE in EN-DC and NE-DC, FFS.
    (will be deleted later) Moderator question/comment: in new added option 3:
      regarding NR CA and NR DC (with sync MAC CE) case, “FFS” means we need to figure out if RF tuning for FR1 SCell activation can happen at different time from RF tuning for FR2 SCell.
      regarding NR DC (with async MAC CE) case, “FFS” means we need to figure out if we need to consider this NR-DC case without per-FG MG capability in our requirement design scope (we can discuss this in the slide of requirement simplification)
      regarding EN-DC, NE-DC case, “FFS” means we need to figure out if we need to consider the interruption from LTE Scell activation, on top of the question in NR CA
  If delay extension due to interruption on L1-RSRP measurement resource is needed, FFS on following options:
    Option 1: if interruption occurs on L1-RSRP resource for measurement, then total delay should be extended by X extra L1-RSRP RS periodicity. X is number of L1-RSRP resource for measurement being interrupted
    Option 2: In NR CA, there is no additional interruption on the L1-RSRP reporting resource of the target to-be-activated SCell and no additional delay extension is needed. In NR DC, EN-DC, NE-DC, only 1 extra L1-RSRP RS periodicity is needed when interruption occurs on the L1-RSRP reporting resource of the target to-be-activated SCell.

## Slide 6: scaling factor for cell detection time of target being-activated SCell(sub-topic 1-5 in R4-2002187)
Agreements in RAN4 #94e:
  When more than 1 unknown SCells are activated, the cell detection time for each SCell is scaled by N. N shall be the sum of the number of all unknown FR1 SCells being activated and the number of FR2 bands with unknown SCells being activated.
    the cell identification and RRM measurement requirements for other SCCs is not assumed do not apply during the longest cell detection time among unknown SCells being activated for target SCell activation in multiple SCell activation requirement design
    FFS: definition of “cell detection time”
      Option 1: means the time of cell synchronization and AGC settling for unknown case, i.e., “TFirstSSB_MAX + TSMTC_MAX+TRS” in FR1 unknown case, “24*Trs” in FR2 unknown case without existing active serving cell on same band
      (will be deleted later): Moderator comment: this new issued has been identified by Huawei. Since it’s difficult to tell the actual implementation timeline for AGC and cell sync, in the option 1 they are mixed together for scaling due to searcher limitation.

## Slide 7: Interruption(s) on other serving cells when multiple SCells are being activated(sub-topic 1-6 in R4-2002187)
Agreements in RAN4 #94e:
  FFS: if there is one single MAC CE for multiple SCell activation in each CG, is the interruption of RF tuning/retuning is aligned on time domain among multiple being-activated SCells within each CG?
    (will be deleted later) moderator question: E.g., can UE tune RF at different time points for different to-be-activated Scells due to different SSB periodicity or SMTC periodicity? If no, then the interruption due to RF tuning shall be aligned on time domain.
  FFS: Interruption(s) on other serving cells when multiple SCells are being activated
    Option1: In EN-DC, NE-DC, NR SA, the total interruption length of multiple SCell activations shall be same as the longest single interruption time among those SCell activations. In NR-DC, if two MAC CEs are used for multiple SCell activations in different CGs, it can be up to two individual interruptions during the activation delay, and each interruption length shall be same as the longest single interruption time among SCell activations in that CG.
    Option 2: In case of activation of multiple cells, there will be multiple interruptions to other active cells. A group of contiguous cells being activated will only cause one interruption on already active cells. Each non-contiguous cell being activated/deactivated can cause an independent interruption to already active cells. The length of interruptions should be the same as defined in Rel-15

## Slide 8: Interruption to AGC settling (sub-topic 1-7 in R4-2002187)
Agreements in RAN4 #94e:
  FFS: Interruption to AGC settling
    Option 1:
      For simultaneous activation (MAC CE on same time point),
        if the concerned SCell activation requires AGC, its activation delay is not extended;
        if the concerned SCell activation does not require AGC, its activation delay is extended by one SMTC period if AGC is required by any other SCell in the same band.
        (will be deleted later): moderator question: like on slides #6, does UE allow to perform RF tuning/retuning on different time points for different being-activated Scells after receive single MAC CE?
        (will be deleted later): moderator question: if single interruption due to RF tuning/retuning is assumed, the interruption due to AGC settling shall consider FR1 unknown (2 AGC occasions), FR1 known with >160ms sCellMeasCycle (1 AGC occasion), FR1 known with 160ms sCellMeasCycle (0 AGC occasion), does the Huawei proposal need to consider this kind of mixed case for AGC interruption?
      For non-simultaneous activation (MAC CE on different timing points for different CGs),
        if the concerned SCell activation requires AGC, its activation delay is extended by the whole AGC settling time;
        if the concerned SCell activation does not require AGC, its activation delay is extended by one or two SMTC periods.
    Other option is not precluded

## Slide 9: Activation requirement for mixed types of to-be-activated Scells (sub-topic 1-8 in R4-2002187)
Agreements in RAN4 #94e:
  FFS: mixed unknown and known to-be-activated Scells
    Option 1:
      If there is no active serving cell on the FR2 band and if the target SCells being activated are unknown to UE,
        Only one unknown SCell shall execute L1-RSRP measurement and reporting;
        Other unknown SCells shall hold on its activation procedure until their TCI states are configured;
        The TCI state configuration for these SCells shall be different;
        Only single interruption due to single RF switch on is considered.
      If there is no active serving cell on the FR2 band and if at least one of the target SCells being activated is known cell and at least one of the target SCells is unknown cell,
        All unknown SCell won’t need L1-RSRP measurement and reporting;
        All unknown SCells shall hold on its activation procedure until their TCI states are configured;
        The TCI state configuration for these SCells shall be different;
        Only single interruption due to single RF switch on is considered.
    Other option is not precluded

## Slide 10: Multiple SCell activation requirement for per-FR MG capable UE (sub-topic 1-9 in R4-2002187)
Agreements in RAN4 #94e:
  If UE has per-FR gap capability, the existing interruption applicability shall still apply, i.e., interruption from FR1 CC will not impact CCs in FR2 and vice versa, but this UE still needs to consider the time extension caused by other to-be-activated SCells in the same frequency range as the target SCell and the searcher limitation.

## Slide 11: Delay extension of multiple SCells activation for inter-band FR2 CA (sub-topic 1-10 in R4-2002187)
Agreements in RAN4 #94e:
  Postpone the discussion for multiple SCell activation in inter-band FR2 CA to next RAN4 meeting.

## Slide 12: Simplification on requirement scope of multiple SCell activation
Agreement in RAN4 #94e:
  Do not consider interruption of LTE SCell activation to NR SCell activation in EN-DC and NE-DC cases
  FFS: whether or not define requirement of multiple SCell activations in different CGs for UE without per-FR MG capability in NR-DC
    If requirement shall be defined for this case, FFS if the delay extension due to interruption could be decided by the largest time component in victim SCell activation
    (will be deleted later) Moderator comment: since MAC CEs can be async between CGs, then that means interruption from one CG can happen anytime to other CG activation, but the timeline of UE to activate a SCell is purely UE implementation, it’s very difficult to decide which part is interrupted by RF tuning from other CG Scell activation.
  FFS: whether or not to define requirement of multiple SCell activations of if to-be-activated SCells includes FR1 unknown and FR1 known SCells on the same band mixed unknown and known case in FR1
    (will be deleted later) Moderator comment: MTK showed some gain for mixed known and unknown case in FR2, and therefore here we only keep FR1 case for discussion. in FR1, unknown and known case has 3 different AGC settling time, the delay extension due to interruption of AGC settling would be complicated in FR1 intra-band, as shown in annex 1.
  FFS: whether or not to define requirement of multiple SCell activations of mixed SCell measurement cycles in FR1 intra-band if to-be-activated SCells includes FR1 known SCells with 160ms SCell measurement cycle(s) and >160ms SCell measurement cycle(s) on the same band
  FFS: new suggestion from moderator: FFS if delay requirement of multiple SCell activation shall be designed based on at most one interruption during the target SCell activation
    (will be deleted later) Moderator comment: 2 or 3 times of interruption on Scell activation (e.g. RF tuning interruption from other CG, AGC interruption from FR1 intra-band unknown SCell): do we need to avoid this case in requirement?

## Slide 13: Annex 1: analysis for interruption cases from other SCell activation/deactivation (for information)
To-be-activated target SCell (configured deactivated SCell) types | Possible Interruption source (Aggressor to-be-activated Scells)
Type 1: FR1 known SCell with meas_cyc=160ms | SCell in FR2 when NR-DC (per-UE MG capable) Type 2 SCell on same band Type 3 SCell on same band
Type 2: FR1 Known SCell with meas_cyc>160ms | SCell in FR2 when NR-DC (per-UE MG capable) Type 3 SCell on same band
Type 3: FR1 Unknown SCell | SCell in FR2 when NR-DC (per-UE MG capable)
Type 4: FR2 SCell with active serving cell(s) on same band and with configured SMTC | SCell in FR1 when NR-DC (per-UE MG capable)
Type 5: FR2 SCell with active serving cell(s) on same band but without configured SMTC | SCell in FR1 when NR-DC (per-UE MG capable)
Type 6: FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting, and UE receives the SCell activation command, semi-persistent CSI-RS activation command and TCI state activation command at the same time | SCell in FR1 when NR-DC (per-UE MG capable)
Type 7: FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting, and UE receives TCI state activation command after SCell activation command | SCell in FR1 when NR-DC (per-UE MG capable)
Type 8: FR2 known SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting | SCell in FR1 when NR-DC (per-UE MG capable)
Type 9: FR2 unknown SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting | SCell in FR1 when NR-DC (per-UE MG capable)
Type 10: FR2 unknown SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting | SCell in FR1 when NR-DC (per-UE MG capable)
Note: in the above table, the interruption from LTE SCell activation and interruption from RF tuning/retuning of SCell activation in the same CG are not considered. If those interruptions shall be considered from the discussion in the previous slides, this table will be revised.

## Slide 14: Part 2: Way forward on UE-specific CBW switching

## Slide 15: UE-specific CBW change (sub-topic 3-1 in R4-2002187)
Agreements in RAN4 #94e:
  Clarification on UE-specific CBW change
    the requirement of UE-specific CBW change applies for the reconfiguration of offsetToCarrier or carrierBandwidth to target UE.
  Delay requirement on UE-specific CBW change
    TChannelBWSwitch = TRRC Processing + TUE processing
      FFS on UE processing time for UE specific channel BW switch (TUE processing ).
      TRRC Processing is same as RRC processing time in RRC-based BWP switch requirement.
  FFS: Interruption requirement on UE-specific CBW change
    Option 1: same as interruption requirement for RRC-based BWP switch
    Other option is not precluded.