## Slide 1: Way forward on FR2 inter-band CA requirement
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #94e
Online, 24th February – 6th March, 2020
Agenda: 8.15.1.10
R4-2002251

## Slide 2: Agreements on cell detection/measurement requirement
There is no impact on idle/inactive mode requirement. Rel-15 Cell detection/measurement requirement shall be reused for FR2 inter-band CA.

## Slide 3: Agreements on the scaling factor CSSFoutside_gap
The scaling factor CSSFoutside_gap shall be defined for FR2 inter-band CA. The values of CSSFoutside_gap need to be defined for the following types of CCs :
  FR2 PSCC in EN-DC mode or FR2 PCC in SA/NE-DC mode
  FR2 SCC where neighbour cell measurement is required
  FR2 SCC where neighbour cell measurement is not required
Companies are encouraged to provide the analysis on the principles on how to define the values of CSSFoutside_gap and clarify the following aspects:
  Total searcher number
  Total band number in FR2
  How to share searcher among these carriers
  Two options are provided as starting point:
    Option 1:
    Option 2:
Scenario | CSSFoutside_gap,i for FR2 PCC (in SA or NE-DC mode) or PSCC (in EN-DC mode) | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is required | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is not required
FR2 inter-band CA | 1 | 2×(Number of configured FR2 band(s) - 1) | 2×(Number of configured SCell(s) – (Number of configured FR2 band(s) -1))
Scenario | CSSFoutside_gap,i for FR2 PCC (in SA or NE-DC mode) or PSCC (in EN-DC mode) | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is required | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is not required
FR2 inter-band CA | 1 | 2 | 2×(Number of configured SCell(s) - 1)

## Slide 4
The existing interruption requirements for CA can also be applied for FR2 inter-band CA scenario
Agreements on interruption requirements

## Slide 5: Agreement on beam management requirement
Beam management requirements for FR2 inter-band CA scenario:
    Option 1: Rel-15 beam management requirement for FR1+FR2 CA shall be reused for FR2 inter-band CA scenario as is.
    Option 2: UE should be configured with beam management resources on one cell in each band for which it is using independent beams. RAN4 to use SCell beam management requirements as being defined in eMIMO WID as baseline.

## Slide 6: Agreement on scheduling restriction requirement
Scheduling restriction requirement for UE supporting independent beam
    Whether there are scheduling restrictions on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band.
      Option 1: Yes
      Option 2: No
    Whether to introduce the scheduling restriction requirements for FR2 inter-band CA scenario
      Option 1: Yes, to clarify there is no scheduling restriction.
      Option 2: Yes, to clarify there is scheduling restriction among different FR2 bands.
      Option 3: No
Scheduling restriction requirement for UE supporting common beam
    Whether there are scheduling restrictions on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band.
      Option 1: Yes
      Option 2: No
    Whether to introduce the scheduling restriction requirements for FR2 inter-band CA scenario
      Option 1: Yes, to clarify there is no scheduling restriction.
      Option 2: Yes, to clarify there is scheduling restriction among different FR2 bands.
      Option 3: No

## Slide 7: Agreement on measurement restriction requirements
Measurement restriction requirement for UE supporting common beam
    Whether there are measurement restrictions for UE performing RLM/BFD/CBD/L1-RSRP measurements on different FR2 bands.
      Option 1: Yes
        The measurement restriction requirements due to RLM/BFD/CBD/L1-RSRP measurements being performed on different FR2 bands need to be introduced for FR2 inter-band CA
      Option 2: No

## Slide 8: Agreement on SCell activation delay requirements
SCell activation delay requirements in the following cases need to be clarified for FR2 inter-band CA
    Case 1: SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band
    Case 2: SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR2
For case 1, whether the existing SCell activation delay requirements in case of “SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band” can be reused for FR2 inter-band CA
    Option 1: Yes.
    Option 2: No.
For case 2, whether the existing SCell activation delay requirements in case of “SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1” can be reused for FR2 inter-band CA
    Option 1: Yes.
    Option 2: No.
      The timeline for L1-RSRP measurement on multiple bands needs FFS for multiple unknown cells.