## Slide 1
3GPP TSG-RAN WG4 Meeting #94-e R4-2002253
Electronic Meeting, Feb.24th – Mar.6th 2020
Agenda Item: 8.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1912781 WF on RRM for NR HST, RAN4#92BIS
  R4-1915887 WF on RRM for NR HST, RAN4#93

## Slide 3: Cell re-selection requirements
  Whether to keep M2, M3, M4 for cell re-selection with DRX cycle =0.32s:
    Option 1 (CATT, NOKIA,): remove M2, M3, M4 without restriction on SMTC period
    Option 2 (HW, MTK): keep M2, M3, M4
    Option 3 (QC, vivo, Samsung, Intel): When SMTC < 40, remove M2, M3, M4; when SMTC >= 40, M2 = 1.5, M3 = M4 = 2
    Option 4 (Ericsson, CMCC, Apple): When SMTC < =40, remove M2, M3, M4; when SMTC >40, M2 = 1.5, M3 = M4 = 2

## Slide 4: Cell identification delay requirements for non-DRX case
Rel-15 SSB index acquiring delay requirements for non-DRX case is reused for NR HST (tentative agreements in 1st round)

## Slide 5: Cell identification delay requirements for DRX case
Whether to keep the relaxation factor of 1.5 for DRX cycle <= 0.32s
  Option 1(MTK): keep the factor
  Option 2 (CATT, NOKIA, HW): remove the factor without restriction on SMTC period
  Option 3 (QC): the scaling factor can be removed if SMTC < [40] ms, otherwise keep the factor
  Option 4 (CMCC, DCM, Ericsson, Apple, Samsung, Intel): the scaling factor can be removed if SMTC <= [40] ms, otherwise keep the factor

## Slide 6: Cell identification delay requirements for DRX case
Measurement delay for DRX cycle <= 0.32s
  for measurement delay with DRX cycle < 320ms, 5 samples are used (tentative agreements in 1st round)
  for measurement delay with DRX cycle = 320ms, the number of samples is:
    Option 1: 3 samples
    Option 2: 4 samples
    Option 3: 5 samples

## Slide 7: Cell identification delay requirements for DRX case
Measurement delay for DRX cycle > 0.32s
  Option 1: 3 samples are used when SMTC <= 40ms, 5 samples are used when SMTC >40ms
  Option 2: 3 samples are used when SMTC < 40ms, 5 samples are used when SMTC >= 40ms
  Option 3: 5 samples
  Option 4: 3 samples applied for all the candidate SMTC
  Applied DRX cycle in cell identification requirements for HST
  For NR HST, enhanced requirements are considered for DRX cycle <= 1.28s, and no enhanced requirements are considered for DRX cycle = 2.48s (tentative agreements in 1st round)

## Slide 8: RLM
Q1: whether the outcome on the scaling factor for L3 measurement can be reused for RLM?
  Option 1: YES
  Option 2: NO
Q2: If the answer to Q1 is NO, whether 1.5x relaxation factor for RLM shall be kept?
  Option 1: keep the 1.5x scaling factor
  Option2: 1.5x relaxation factor is kept when TSSB >= TBD, 1.5x relaxation factor is removed when TSSB < TBD

## Slide 9: Beam management
CBD based on SSB/CSI-RS
  Rel-15 CBD requirements based on SSB/CSI-RS (including delay and accuracy) are reused for NR HST (tentative agreements in 1st round)
BFD based on SSB/CSI-RS
  Q1: whether the outcome on the scaling factor for L3 measurement can be reused for BFD?
    Option 1: YES
    Option 2: NO
  Q2: If the answer to Q1 is NO, whether 1.5x relaxation factor for BFD shall be kept?
    Option 1: keep the 1.5x scaling factor
    Option2: 1.5x relaxation factor is kept when TSSB >= TBD, 1.5x relaxation factor is removed when TSSB < TBD

## Slide 10: Beam management
L1-RSRP based on SSB/CSI-RS
  Reuse Rel-15 SSB/CSI-RS based L1-RSRP measurement requirements, including the measurement accuracy and measurement delay except the 1.5x scaling factor, for NR HST(tentative agreements in 1st round)
  Whether to remove the 1.5x scaling factor in the measurement delay requirements for L1-RSRP, the outcome of L3 measurement can be applied(tentative agreements in 1st round)

## Slide 11: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Enhance NR- EUTRA inter-RAT measurement requirements to support HST(tentative agreements in 1st round)
  Cell re-selection requirements on NR- EUTRA inter-RAT measurement in idle mode
    Option 1 (CMCC, HW, Ericsson, vivo, Nokia, Apple, MTK, Intel): The principle is that NR to EUTRA inter-RAT measurements follows the R16 EUTRA HST enhanced measurement requirements. And the details are shown in the following Table:
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 (8) | 0.32(1) | 0.96(3)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
    Option 2 (QC):
DRX cycle length [s] | TdetectEUTRA_FDD [s] (number of DRX cycles) | TmeasureEUTRA_FDD [s] (number of DRX cycles) | TevaluateEUTRA_FDD [s] (number of DRX cycles)
0.32 | 7.68 (24) | 1.28 (4) | 1.6(5)
0.64 | 12.8 (16) | 1.28 (2) | 1.92 (3)
1.28 | 12.8(10) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 12: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification without DRX in connected mode
    Reuse R15 inter-RAT measurement requirement with non-DRX case in TS 38.133 (including both Tinter1 = 60ms and Tinter1 = 30ms) for NR HST (tentative agreements in 1st round)

## Slide 13: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification with DRX in connected mode
    Option 1(CMCC, Ericsson)
    Option 2 (HW, QC)
DRX cycle length (s) | TIdentify, E-UTRAN (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.2.2 apply | Non-DRX requirements in clause 9.4.2.2 apply
0.16 < DRX-cycle<1.28 | Note1 (10) | Note1 (10)
1.28 | Note1 (8) | Note1 (8)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. |  | 
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.256 | 3.84* CSSFinterRAT (15*CSSFinterRAT) | 3.84*K (15*CSSFinterRAT)
0.32 | 4.8*K (15*CSSFinterRAT) | 4.8*K (15*CSSFinterRAT)
0.32< DRX-cycle ≤10.24 | Note1 (20*CSSFinterRAT) | Note1 (20*CSSFinterRAT)
NOTE 1: The time depends on the DRX cycle length. NOTE 2: CSSFinterRAT is as defined in clause 9.4.3.2. |  | 

## Slide 14: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification with DRX in connected mode
    Option 3 (Vivo)
    Option 4 (QC, Vivo)
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.16< DRX-cycle ≤0.32 | Note1 (15*CSSFinterRAT) | Note1 (15*CSSFinterRAT)
0.64 | 5.12*CSSFinterRAT (8*CSSFinterRAT) | 5.12*CSSFinterRAT (8*CSSFinterRAT)
1.28 | 8.96*CSSFinterRAT (7*CSSFinterRAT) | 8.96*CSSFinterRAT (7*CSSFinterRAT)
1.28< DRX-cycle ≤10.24 | Note1 (20*CSSFinterRAT) | Note1 (20*CSSFinterRAT)
NOTE 1: The time depends on the DRX cycle length. |  | 
QC compromised proposal for NR- EUTRA inter-RAT measurement in connected mode for DRX case |  | 
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.16<DRx cycle<=0.32 | Note1 (15) | Note1 (15)
0.32< DRx cycle <= 0.64 | Note1 (10) | Note1 (10)
0.64 < DRx cycle <= 1.28 | Note1 (8) | Note1 (8)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. NOTE 2: The requirement only applicable to CSSFinterRAT = 1 case |  | 

## Slide 15: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  Enhance EUTRA-NR inter-RAT measurement requirements to support NR HST (tentative agreements in 1st round)
  Cell re-selection requirements on EUTRA-NR inter-RAT in idle mode
    Option 1 (CMCC, Ericsson, Nokia, Apple, MTK): the cell re-selection requirements on EUTRA-NR inter-RAT measurement follow R16 HST NR cell re-selection requirements
    Option 2 (QC): discuss possible options between non-HST inter-RAT requirement and HST intra-frequency measurement requirement.

## Slide 16: Inter-RAT measurement
EUTRA - NR Inter-RAT measurement
  Cell identification without DRX in connected mode
    Option 1 (CMCC, Ericsson, Apple, MTK): cell identification requirements on EUTRA-NR inter-RAT measurement in connected mode for non-DRX case follow R16 HST NR requirements
    Option 2 (QC): discuss possible options between non-HST inter-RAT requirement and HST intra-frequency measurement requirement.
    Option 3 (Vivo): Since for non-HST the measurement period requirement of an inter-RAT NR carrier in LTE is same as that of inter-frequency requirement in NR, our proposal is to follow the same enhancement methodology, but the baseline should be inter-frequency requirement
    Option 4 (Nokia): RAN4 should consider the overall system delay and consider whether the existing requirements are sufficient or whether R16 HST NE measurement requirements would need to be applied.
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(200ms, Ceil(8  1.5)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 8  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. | 

## Slide 17: Inter-RAT measurement
EUTRA - NR Inter-RAT measurement
  Cell identification with DRX in connected mode
    Option 1 (CMCC, Ericsson, Apple, MTK): cell identification requirements on EUTRA-NR inter-RAT measurement in connected mode for non-DRX case follow R16 HST NR requirements
    Option 2 (QC): discuss possible options between non-HST inter-RAT requirement and HST intra-frequency measurement requirement.
    Option 3 (Vivo): Since for non-HST the measurement period requirement of an inter-RAT NR carrier in LTE is same as that of inter-frequency requirement in NR, our proposal is to follow the same enhancement methodology, but the baseline should be inter-frequency requirement
    Option 4 (Nokia): RAN4 should consider the overall system delay and consider whether the existing requirements are sufficient or whether R16 HST NE measurement requirements would need to be applied.
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(200ms, Ceil(8  1.5)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 8  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. | 

## Slide 18: SS-SINR
Option 1(QC, Ericsson): SINR accuracy requirement is not applicable to HST scenario when SNR > 5dB
Option 2 (vivo, HW, MTK): SINR accuracy requirement is not applicable to HST scenario
Option 3 (DCM): identify the SNR upper bound below which the SS-SINR measurement accuracy requirements are specified