## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e Electronic Meeting, Feb. 24th – Mar. 6th 2020
Huawei, HiSilicon
Way forward on RRM requirements of R16 enhancement for NB-IoT
R4-2002269

## Slide 2: NRSRP measurement in non-sparse PO case
NRSRP measurements in dense PO case
  UE to be allowed to make RRM measurements in dense paging occasions without preconditions

## Slide 3: Multi carrier operation non-anchor RRM
NRSRP measurements on non-anchor carrier can be filtered or combined with NRSRP measurement on anchor carrier after translating the non-anchor carrier measurement with parameter nrs-PowerOffsetNonAnchor without any conditions or prerequisites.
Any filtered results, either from anchor or non-anchor carrier, can trigger neighbor cell measurement and/or relaxed monitoring abortion.