## Slide 1: WF on NR-U FRCs
Nokia, Nokia Shanghai Bell
Draft R4-2002465
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Contributions for RAN4#94e on NR-U BS Rx requirements
R4-2000985, CR for NR-U RX requirement, ZTE Corporation
R4-2000821, NR-U BS REFSENS, Huawei, HiSilicon
R4-2000822, NR-U BS dynamic range, Huawei, HiSilicon
R4-2000982, Simulation results for NR-U BS RX FRC, ZTE Corporation
R4-2000983, NR-U BS RX REFSENS and dynamic range requirement, ZTE Corporation
R4-2000984, NR-U BS RX ICS requirement, ZTE Corporation
R4-2001463, Discussion and simulation results for NR-U BS REFSENS/ICS, Huawei, HiSilicon
R4-2001464, Discussion and simulation results for NR-U BS Dynamic range, Huawei, HiSilicon
R4-2001465, Discussion on FRC definition for NR-U BS REFSENS and Dynamic range, Huawei, HiSilicon
R4-2001674, NR-U BS receiver requirements, Nokia, Nokia Shanghai Bell
R4-2001675, Summary of simulation results for NR-U BS Rx FRC, Nokia, Nokia Shanghai Bell
R4-2001727, Update to NR-U FRC definitione, Ericsson, Nokia, Nokia Shanghai Bell
R4-2001728, NR-U BS RX Simulation Results, Ericsson

## Slide 3: Background
During RAN4#93 meeting simulation assumptions for NR-U FRCs were agreed in [1]. Simulation assumptions includes also REFSENSE/ICS FRCs and Dynamic range FRCs.
On RAN4#94e meeting cCompanies noticed that FRCs in [1] are not correctly design :
  There is no interlacing design for 60kHz in RAN1 specification (TS 38.211 clause 4.4.4.6)
  There is specific design in TS 38.211 for 15/30kHz interlaces that shall be taken into account.
FRCs parameters are critical to define Rx wanted signal and interfering signal configurations to derive NR-U BS Rx requirements, that are essential to finished Rel-16 NR-U WI.
[1] R4-1916162, WF on NR-U BS RF RX FRC, ZTE

## Slide 4: Way forward
This WF is supplement with correct FRC interlacing to simulation assumption for BS Rx requirements agreed during RAN4#93 meeting in R4-1916162 and correct FRCs design.
All other simulation assumptions except FRC interlacing, are as agreed in R4-1916162.
Companies are encourage to provide SNR simulation results based on assumption in R4-1916162 and FRCs agreements captured in this WF for next RAN4 meeting.

## Slide 5: Way forward
On 60kHz SCS FRCs:
  It is agreed to not define FRC with interlacing for NR-U due to lack of RAN1 interlacing design for 60 kHz.
  Following options are consider for 60 kHz SCS instead of interlace:
  Option 1: FRCs for 60kHz SCS from NR Rel-15 can be reused.
  (Supported by: Nokia)
  Option 2: New FRC for 60kHz SCS occupying more than 80% CBW are needed. (Supported by: ZTE)

## Slide 6: Way forward
On NR-U FRCs interlace arragement:
  Following options are to consider:
  Option 1: No overlapping, all interlaces can have different number of RBs.
  (supported by: Huawei)
  Option 3: No overlapping, all interlaces have the same number of RBs.
  (supported by: Ericsson, Nokia)
  Option 4: overlapping if necessary, all interlaces have the same number of RBs.
  (supported by: ZTE)

## Slide 7
BS channel bandwidth (MHz) | Sub-carrier spacing (kHz) | Reference measurement channel | Reference sensitivity power level, PREFSENS (dBm)
5, 10, 15 | 15 | G-FR1-A1-1 (NOTE 1) | -96.7
10, 15 | 30 | G-FR1-A1-2 (NOTE 1) | -96.8
10, 15 | 60 | G-FR1-A1-3 (NOTE 1) | -93.9
20, 25, 30, 40, 50 | 15 | G-FR1-A1-4 (NOTE 1) | -90.3
20, 25, 30, 40, 50, 60, 70, 80, 90, 100 | 30 | G-FR1-A1-5 (NOTE 1) | -90.6
20, 25, 30, 40, 50, 60, 70, 80, 90, 100 | 60 | G-FR1-A1-6 (NOTE 1) | -90.7
[10, 20, 40] | 15 | [TBD] (NOTE 2) | [TBD]
[10, 20, 40, 60, 80, 100] | 30 | [TBD] (NOTE 2) | [TBD]
[10, 20, 40, 60, 80, 100] | 60 | [TBD] (NOTE 2) | [TBD]
NOTE 1: PREFSENS is the power level of a single instance of the reference measurement channel. This requirement shall be met for each consecutive application of a single instance of the reference measurement channel mapped to disjoint frequency ranges with a width corresponding to the number of resource blocks of the reference measurement channel each, except for one instance that might overlap one other instance to cover the full BS channel bandwidth. This reference measurement channel is not applied for NR-U bands. NOTE 2: PREFSENS is the power level of a single instance of the reference measurement channel. This requirement shall be met for each single interlace of [TBD]. This reference measurement channel is only applied for NR-U Bands. |  |  | 
Table 7.2.2-2: NR Medium Area BS reference sensitivity levels
NOT PART OF WF!! ILLUSTRATION ONLY

## Slide 8: Way forward
  Following tables present detailed interlace arrangements for NR FRCs:
  [To be add after one of the option is agreed]