## Slide 1: WF on IAB-MT ACS and IBB in FR2
Ericsson
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
R4-2002491

## Slide 2: Background on ACS
During the 92bis adhoc meeting, it is agreed that BS type of ACS number should be reused for FR2 IAB MT:
  ACS [23.5]dB same as BSfor <37 GHz
  ACS [22.5]dB same as BS above >37 GHz
During 94-e, there are companies contribution to further discuss the ACS and IBB.

## Slide 3: Background on ACS (captured in 1st summary)
Issue 1-1: IAB-MT ACS value in FR2
  All company proposals are close to each other, only discrepancy is whether the ACS value is rounded to an integer value
  Agree the following values, where ACS is rounded to an integer
    IAB-MT ACS of 24 dB for 24.24 – 33.4 GHz
    IAB-MT ACS of 23 dB for 37 – 52.6 GHz
Issue 1-2: Wanted signal power level for ACS
  Proposals
    Option 1: [REFSENS + 6 dB]
    Option 2: [REFSENS + 14 dB]
  Recommended WF
    Agree option 1
  Additionally there was a proposal to specify PDSCH reference channel. Moderator recommendation is to leave this to reference sensitivity discussion

## Slide 4: Way forward on ACS on FR2
ACS value
  ACS is rounded to an integer
    IAB-MT ACS of 24 dB for 24.24 – 33.4 GHz
    IAB-MT ACS of 23 dB for 37 – 52.6 GHz
ACS wanted level
  Wide area IAB MT:
    [REFSENS + 6 dB]
  FFS on [Local areal] IAB class
    For example :[REFSENS + 14 dB]

## Slide 5: Way forward on ACS on FR2
ACS inteference signal offset, bandwidth and waveform
  Wide area IAB: Same as BS ACS req
  FFS on [Local areal] IAB class
FFS on need of PDSCH reference channel.

## Slide 6: Background on IBB(captured in 1st summary)
Issue 3-1: In-band blocking requirement in FR2
Proposals
  Option 1: Do not specify in-band blocking, impact to be covered by Rx dynamic range
  Option 2: Based on UE requirements
  Option 3: Based on BS requirements
  Option 4: increase interference level compared to current requirements, including the possibility of fixed interference power level
    Wanted signal level TBD

## Slide 7: Way forward on IBB on FR2
Agree in-band blocking requirement is required.
Agree conclusions from simulations are based on 99% point of CDF
IBB interference signal level and wanted signal level.
  Wide area IAB MT: Based on BS requirements
    Wanted signal : [REFSENS+ 6 dB]
    Interference signal: [REFSENS+ 33 + ΔFR2_REFSENS]
  FFS on other IAB class based on deployment scenario
    For example: Based on UE requirement

## Slide 8: Reference
R4-2002372, Email discussion summary for RAN4#94e_ #81_NR_IAB_Co-existence